## Slide 1
QPSK Modulation With Anti-multipath Scheme for High Speed Wireless LAN November 10 1997 Yoshikazu KAKURA, Kazuhiro OKANOUE and Tomoki OHSAWA NEC Corporation 1-1, Miyazaki 4-chome, Miyamae-ku, Kawasaki, 216 Japan Tel: +81 44 856 2255 Fax: +81 44 856 2230 {kakura|okanoue|ohsawa}@ccm.CL.nec.co.jp
IEEE P802.11
Wireless LANs
Notes: November, 1997
Page 1
Submission
doc: IEEE P802.11-97/121
Abstract
This paper describes a skeleton proposal of QPSK modulation with an anti-multipath scheme as a candidate of single carrier systems for 802.11 5GHz physical layer. We consider that a large capacity and usability for users are key requirements for successful wireless LANs. From the points of the requirements’ view, we analyze the proposed scheme. This paper implies that the proposed scheme has possibilities to achieve the requirements.
In order to improve the proposal to be concrete, we need to continue to study the proposed scheme based on the Criteria for Comparison of Modulation Methods for 802.11 5GHz physical layer. Through the study, some modifications may occur to the proposal.

## Slide 2
Status of the Presentation
A candidate of single carrier systems
Possibilities to change the proposed scheme through future studies
A skeleton proposal for
QPSK modulation with an anti-multipath scheme
Notes: November, 1997
Page 2
Submission
doc: IEEE P802.11-97/121
In this presentation, we will show a skeleton proposal taking QPSK modulation with an anti-multipath scheme as a candidate of single carrier systems.
Currently, criteria for comparison of modulation method are working in progress. After fixing the criteria, we will evaluate the proposed scheme based on the criteria. Through the evaluations, some modifications may occur for a future proposal.

## Slide 3
Requirements for High Speed Wireless LAN
Requirements from System side: Large system capacity
  Additional comparison items
    Frequency re-use capability
    Efficient transmission
Requirements from Equipment side: Usability for users
  Additional comparison items
    Cost
    Portability
    Long life time
Notes: November, 1997
Page 3
Submission
doc: IEEE P802.11-97/121
Regarding to requirements for high speed wireless LANs, we consider there exist 2 important points. From the point of system design’s view, enough system capacity should be realized by selecting a modulation method. On the other hand, reality is important for equipment design.
The system capacity consideration is important by mean of how may people can use how much bandwidth for the wireless LAN services with in limited total bandwidth. It can be basically determined by how a system can use total band efficiently. In addition to efficiency for a signal transmission, we would like to discuss an additional comparison item for physical layer; that is,
- a system which can re-use channel effectively.
While we are going to discuss about how to realize PHY (i.e. wireless link design), why do not try to coordinate system side discussion?
Wireless LAN devices will be mainly used with portable PCs or PDAs on the move, we must also take reality factors into the discussion. In order to realize the situation, we consider that the following 3 items should be taken into considerations as seriously for proposing modulation and demodulation scheme;
-cost
-portability
-long life time.

## Slide 4
Technical issues for the comparison items
Frequency re-use capability
Number of available channels
Preamble length
Hardware simplicity
Power consumption
Efficient transmission
Cost
Portability
Long life time
Technical Issues for modem
Comparison Items
Notes: November, 1997
Page 4
Submission
doc: IEEE P802.11-97/121
The above figure shows relationships between the comparison items and technical issues for modem designs.
In order for a system to achieve high frequency re-use capability, modems need to provide available channels to the system as many as possible.
For a efficient transmission, modems need to operate with a short preamble sequence.
For cost and portability, modems need to be designed in a simple hardware manner.
For long life time, modem need to save power for their operation.

## Slide 5
Impacts of the issues on modems
Number of available channels
Preamble length
Hardware simplicity
Power consumption
Transmitter
Receiver
Modulation method
Notes: November, 1997
Page 5
Submission
doc: IEEE P802.11-97/121
This figure shows how the technical issues affect modems.
Number of channels within a constant bandwidth can be determined by bandwidth of modulated signal per channel. Therefore, we consider that modulation method need to be determined with considerations on numbers of available channels in total bandwidth.
Preamble is used for initial setup for receiving signals. Hence, a preamble length affects design of a receiver.
Power consumption and hardware simplicity affects whole modem design, i.e., both a transceiver and a receiver.

## Slide 6
Considerations on Transmitter
Power Consumption
H/W Simplicity
To be solved
Low
Simple
baseband
RF/IF
(mature digital technology)
(linear high power amplifier)
To be solved
Modulation method: QPSK
Notes: November, 1997
Page 6
Submission
doc: IEEE P802.11-97/121
In our proposal, we can adopt existing mature digital technology to baseband part in a transmitter, because we propose QPSK as a modulation method. Therefore, we consider that both low power consumption and simple hardware can be realized.
In RF/IF part, however, QPSK needs linear high power amplifier to reduce spectral sidelobe growth. Therefore, it can be an important technical issue how to realize the linear high power amplifier in the conditions of a low power consumption and simple hardware.

## Slide 7
Amplifier in Transmitter
Trade off for system design
High capacity
Less adjacent channel Interference
Linear Amplifier
Non-Linear Amplifier
Low power consumption
More efficient amplifier
Notes: November, 1997
Page 7
Submission
doc: IEEE P802.11-97/121
There exist a trade off for a system design between high capacity and low power consumption.
In order to realize high system capacity, it is required to reduce adjacent channel interference. On the other hand, it is preferred for low power consumption to use more efficient amplifier, such as non-linear amplifier.

## Slide 8
Consideration on modulation method
System capacity/channel=
(data rate/channel)·r
0
0.2
0.4
0.6
0.8
1
2
4
6
8
10
12
14
16
18
20
number of channels in a system
allowable C/I=10dB
allowable C/I=20dB
allowable C/I=30dB
normalized average throughput(r)
a=3.5
C/I : Carrier to Interference Ratio
More available channel,
More system capacity
QPSK
Notes: November, 1997
Page 8
Submission
doc: IEEE P802.11-97/121
In order to consider modulation method, we estimate system capacity versus number of channels. This graph shows normalized average throughput, r, versus number of channels in a system. A parameter in the graph is allowable carrier-to-cochannel interference ratio of 10, 20 and 30 dB. Propagation constant is assumed to be 3.5. From the graph, more numbers of channel can increase r. System capacity per channel can be obtained by multiplying data rate per channel and r.
This graph shows that more available channels can provide more system capacity. For a large system capacity, we consider that QPSK can be one of the candidates as a modulation method.

## Slide 9
Estimation of System capacity/channel(Cap)
17.5
245
f [MHz]
1
2
14
15
…
…
Modulation: QPSK (roll-off=50%)
Data rate: 20Mbps/channel(12.5Msymbol/sec)
Carrier interval: 12.5[MHz]·1.4 = 17.5 [MHz]
System bandwidth: 300MHz
15 carriers
Allowable C/I: 20dB
r=0.8
+
Cap = 16Mbps
Notes: November, 1997
Page 9
Submission
doc: IEEE P802.11-97/121
Based on the previous analysis, we estimate a system capacity by using the parameters in this slide.
[paper] shows that carrier interval which is equal to 1.4 times of symbol rate can achieve bit error rate of 10-6 within 1dB degradation from theoretical siganl-to-noise ratio.
As for allowable carrier-to-interference ratio, we choose 20dB carrier-to-interference ratio. Common cellular systems such as GSM are designed based on 9-13 dB as carrier-to-interference ratio. Hence, the value include 7-11 dB margin against cellular systems.

## Slide 10
Consideration on Receiver
Power Consumption
H/W Simplicity
Low
Pending issue
baseband
RF/IF
Simple
Preamble
Short
(conventional technologies can be applied)
(Anti-multipath scheme)
Pending issue
Pending issue
Innovative anti-multipath scheme must be proposed
Notes: November, 1997
Page 10
Submission
doc: IEEE P802.11-97/121
As for a receiver for QPSK signal, conventional technologies can be applied to RF/IF part. Therefore, we consider that RF/IF part in the receiver can be realized in the conditions of low power consumption, simple hardware and short preamble.
However, an anti-multipath scheme is inevitable for the single carrier system. It is a technical issue for the baseband part how to innovate an anti-multipath scheme.

## Slide 11
Anti-multipath Scheme
Symbol-by-symbol base ML estimator
Effective usage of decision feedback loop
  Reduction of likelihood calculation
  Avoidance of weak point of ML estimator
Tap Coefficient Shift MLSCE
(Maximum Likelihood Symbol Candidate Estimator)
Notes: November, 1997
Page 11
Submission
doc: IEEE P802.11-97/121
As an anti-multipath scheme, we propose tap coefficient shift MLSCE (Maximum Likelihood Symbol Candidate Estimator).
A basic idea of the scheme is symbol-by-symbol based maximum likelihood estimator. The feature of the scheme is to use decision feedback loop more effectively. This feature can contribute to
- simple implementation by reducing likelihood calculation for pre-cursor and
- bit error rate improvement by avoiding weak point of ML estimator.

## Slide 12
Tap Coefficient Shift MLSCE
Impulse Response Estimator
Coefficient Setting Circuit
h
ML based
Pre-cursor Estimator
Decision based
Post-cursor Estimator
Decision
Rx
Preamble
h(-m-1)
h(0)
h(1)
h(n)
Pre-cursor
Post-cursor
Replicas for Pre-cursor
Replica for Post-cursor
decision
MLSCE
Notes: November, 1997
Page 12
Submission
doc: IEEE P802.11-97/121
This figure shows a block diagram of a tap coefficient shift MLSCE. MLSCE has an maximum likelihood based pre-cursor estimator and decision based post-cursor estimator.
Estimated channel impulse response are divided into pre- and post-cursor parts and directly offered to the pre- and post-cursor estimators as their tap coefficients.
The pre-cursor estimator outputs a replica of received signal distorted by the pre-cursor for each possible candidate. The post-cursor estimator outputs a replica of received signal distorted by post-cursor with decision results.
The decision part adds the replica from the post-cursor estimator and each replica from the pre-cursor estimator. Then the decision part calculates replicas of received signal itself for all possible candidates which produce replicas distorted by pre-cursor. The decision part selects the candidate which maximizes likelihood by comparing the calculated replicas and the received signal. A decision result is decided as a symbol corresponding to h(0) in the selected candidate.

## Slide 13
Preamble for Tap Coefficient Shift MLSCE
Preamble Length
= k+2(n+m)
m:number of pre-cursor
n:number of post-cursor
k:S/N improvement
k(sliding part)
k*
~
k*
~
n+m
(post-cursor est.)
k*
0
1
n+m
-n-m
k
0
0
0
0
0
0
-1
t
...
...
correlator
*:complex conjugate
Length of Inter-Symbol
Interference (ISI)
n+m
(pre-cursor est.)
~
k=10-32 symbols (10-15dB Improvement)
n+m=6-10 symbols (ISI Length)
22-52 symbols
for preamble
Notes: November, 1997
Page 13
Submission
doc: IEEE P802.11-97/121
This figure shows preamble configuration for channel impulse response estimation. Main feature is that the preamble has three parts, per-cursor estimation, post-cursor estimation and sliding parts. These parts are designed for a cross correlation characteristic between the sliding part and all of the preamble to be a impulse. Receiver can estimate channel impulse response by calculating correlation between the sliding part and received preamble sequence.
The length of the pre- and post-cursor estimation part should be the same as the length of inter-symbol interference which the MLSCE can equalize to avoid interference from symbols other than the preamble. The length of the sliding part depends on required signal-to-noise ratio of estimated channel impulse response.
For example, in the case where a inter-symbol interference length is 6-10 symbols and signal-to-noise ratio of the estimates should be 10-15 dB higher than that of received signals, the length of preamble is 22-52 symbols.

## Slide 14
Comparison of Calculation Amount
MLSCE
DDFSE
DFE
adder
Viterbi
multiplier
(complex)
0
0
m
Required
n+m·Lm
n+m·Lm
n+m
None
None
*
*
* m·Lm:one time per packet
m:tap number of Pre-cursor Estimator
n:tap number of Post-cursor Estimator
L:phase number of Modulation
Notes: November, 1997
Page 14
Submission
doc: IEEE P802.11-97/121
This table shows comparison of calculation amount among MLSCE, DDFSE and DFE.
DFE needs complex multiplier for a feed forward filter. However, MLSCE and DDFSE needs no complex multipliers, because they only convolve estimated channel impulse response and symbol candidates or decision results.
DDFSE needs a Viterbi processor, because DDFSE is designed based on a concept of sequence estimation. On the other hand, MLSCE based on a concept of symbol-by-symbol estimation does not need a Viterbi processor. This difference will be represented as performance degradation of MLSCE. However, as far as MLSCE can achieve reasonable performances, MLSCE is more preferable because of its simple implementation.

## Slide 15
Simulation Conditions
Notes: November, 1997
Page 15
Submission
doc: IEEE P802.11-97/121
In order to evaluate MLSCE, we performed computer simulation in the environment shown in the table.

## Slide 16
Simulation Results
Notes: November, 1997
Page 16
Submission
doc: IEEE P802.11-97/121
From the graph, it can be shown that MLSCE has a capability that improves bit error rate floor less than 10-4.

## Slide 17
Conclusions
Large capacity: 16Mbps/channel for 300MHz bandwidth
Transmitter: trade off for system design
Short preamble: about 20-50 symbols for MLSCE
Simplicity: neither Viterbi process nor complex multiplier
QPSK + Tap Coefficient Shift MLSCE
Skeleton Proposal for single carrier system
Notes: November, 1997
Page 17
Submission
doc: IEEE P802.11-97/121
In conclusions, we show a skeleton proposal for QPSK plus Tap Coefficient Shift MLSCE as a candidate of single carrier wireless LAN systems.
We consider that the system capacity is one of the most important keys for successful wireless LAN. As a compensation of the capacity, we need to pay high power linear amplifier. However, we consider that a linear amplifier for QPSK seems to be more reasonable than that of multicarrier systems.
As for an anti-multipath scheme, we propose a tap coefficient shift MLSCE. We show that the MLSCE can operate with a short preamble and be implemented in simple hardware.
Again, this proposal is skeleton and we will continue to study on the proposed method based on the Criteria for Comparison of Modulation Methods for 802.11 5GHz physical layer. Through the study, some modifications may occur to a future proposal.