## Slide 1
ROBUST 10-Mbps PHY: INTRODUCTION
John H. Cafarella
MICRILOR, Inc.
Wakefield, MA

## Slide 2
INTRODUCTION
Technology Development
TOPICS
Robust 10-Mbps Modulation
MSK: Low Current Drain for PC Cards
Need for TRANSEC

## Slide 3
Robust 10-Mbps in Multipath
Direct-Sequence Spread-Spectrum
  Uses 16 Chips/Symbol
  Provides 12 dB Processing Gain
Bi-Orthogonal Modulation
  Expand Data Bandwidth to SS Bandwidth
  Approximately 7 dB EB/N0
Natural Combination for DSSS

## Slide 4
Robustness Features
MAC-Level Retransmissions
  Low Latency
Retransmission Protocol also Controls
  Forward Error Correction
  Antenna Selection Diversity
  Adaptive P-CSMA
PN Codes Optimized for Multipath

## Slide 5
Other Features
Rapid Acquisition
  Small Preamble Overhead
  High Data Throughput
  P-Persistent CSMA Channel Access
Transmission Security (TRANSEC)
  Symbol-to-Symbol DSSS Code Changing

## Slide 6
MICRILOR Development
Clarion M10 in Production
  Robust 10-Mbps Transmission and DSSS Privacy (TRANSEC)
  >7.5 Mbps throughput @100m Indoors (PT=40 mW)
  >6 Mbps throughput @20 mi. (high-gain ant.)
Clarion P10 in Development
  PC Card . . . Low Current Drain and Small Form-Factor
  AP10 Access Point with DSSS Authentication and BSS Isolation
  Conforms to 802.11 MAC
1990
1991
1992
1993
1994
1995
1996
1997
Clarion M10 Bridge Modem
(transparent encapsulation of 802.3)
demo. a b prod
Clarion
demod. demo.
US Army
simulation study
US Army DUWL 3&1 Mbps
Clarion P10
PCMCIA/802.11

## Slide 7
Relationship Between 2- and 10-Mbps Standards?
System Solution
  Multiple Access Points
  Dual-Media Access Point
Product Solution
  Dual-Mode Wireless NIC
Standard Constraint
  Limit Performance for Backward Compatibility ?
  What About Future, Higher Data Rates?