## Slide 1
Support for Nomadicity with IEEE 802.11
George Fishel, AMP, Inc.
and
Bob O’Hara, Informed Technology, Inc.

## Slide 2
Wireless LAN Standards
IEEE 802.11 Standard is currently being developed will be released end 1997. Will work in conjunction with standard Ethernet.
  Spread Spectrum Direct Sequence
    1 And 2 MB/s Transfer Rate at 2.4 Ghz
  Spread Spectrum Frequency Hopping
    1 And 2 MB/s Transfer Rate at 2.4 Ghz
  Infrared

## Slide 3
Nomadicity IEEE 802.11
AP
AP
Ethernet Network
Nomadic User
Vmax < 3m/s
(< 10 MPH)
100 to 200 meters approx.

## Slide 4
Services of 802.11
MAC Data Services
  Error control
  Link encryption
MAC Management Services
  Explicit authentication
  Distributed association
  Distributed discovery
  Change notification
  Power management

## Slide 5
MAC Data Services
Error control
  Retry failed transmissions in the MAC
  Direct acknowledgment of receipt
  Duplicate frame detection and removal
Link encryption
  RC4 encryption algorithm with 40-bit key and 24-bit IV
Notes: MIB attributes control how many retries are attempted before giving up.
Acknowledgments remove dependence on long time-outs to detect frame loss.
Relates to Nomadicity Need #94 Dynamic Service Allocation and #96 Exception Handling
Link encryption provides “wired equivalent” privacy.
Relates to Nomadicity Need #93 Security

## Slide 6
MAC Management Services
Explicit authentication
  Authentication required prior to being able to access data services
  Two mechanisms currently provided
    “Open System”, i.e., none
    “Shared Key”
  Extendible to additional mechanisms
Notes: Open system authentication will always respond with a successful authentication.
Shared key authentication exchanges a challenge text encrypted with the (supposedly) shared key. The text is encrypted using the normal link encryption mechanism. If each side is able to decrypt the challenge text, the authentication is successful.
Relates to Nomadicity Need #91 - Unique & Anonymous Ids and #93 - Security.

## Slide 7
MAC Management Services
Distributed association
  Mobile station requests association
  Includes capability and rate information and location of last association
Notes: Information exchanged includes
Order Information Note
1 Capability Information
2 Listen Interval
3 Current AP Address
4 SSID
5 Supported Rates
Reassociation Request Frame Body
and
Order Information Note
1 Capability Information
2 Status Code
3 Association ID (AID)
4 Supported Rates
Reassociation Response Frame Body
Relates to Nomadicity Need #86 - Handoff Mechanism, #88 - Device Coordination, and #90 - Rerouting.

## Slide 8
MAC Management Services
Distributed discovery
  Two mechanisms provided
    Passive scanning
    Active scanning
  Information is acquired that allows other stations to be found in time-frequency space
Notes: Passive scanning conserves power (transmitter is not used) at the expense of slowing the scanning process. Station goes to a channel and listens for Beacon or Probe Response frames for a period of time, then moves to another channel.
Active scanning completes the scanning process more quickly at the expense of greater power use. Station goes to a channel, transmits a Probe Request frame and processes subsequent Probe Response frames, then moves to another channel.
The information in Probe Response and Beacon frames, includes
Order Information
1 Timestamp
2 Beacon Interval
3 Capability Information
4 SSID
5 Supported Rates
6 FH Parameter Set 1
7 DS Parameter Set 2
8 CF Parameter Set 3
9 IBSS Parameter Set 4
Related to Nomadicity Needs #86 - Handoff Mechanism, #87 - Person - Device Location, and #90 - Rerouting.

## Slide 9
MAC Management Services
Change notification
  Service indications are provided when
    losing an association
    establishing an association
    failing to establish and association
Notes: “passive loss” of association when moving out of range of current association is signaled by increasing frame error rates and frame failure rates.
“active loss” results from receipt of disassociate frame.
Success or failure of an attempted association is signaled
failure is time-out based or from fail code in associate response
success is based on receipt of associate response frame
Relates to Nomadicity Needs #94 - Dynamic Service Allocation, and #96 - Exception Handling.

## Slide 10
MAC Management Services
Power management
  Stations operate in either Active or Power Saving modes
    Active mode: receiver is always on
    Power Saving mode: receiver may be turned off for arbitrary lengths of time
  Stations buffer traffic for other stations in Power Saving mode
Notes: Stations announce changes in power management modes in acknowledged frame exchanges.
Scanning can be done while station is believed to be in power saving mode, without risk of losing messages.
Related to Nomadicity Need #89 - Communications Management.