## Slide 1
Proposal of IR 10Mbps Communication Spec. to IEEE 802.11
Jointly Developed & Proposed by: SWCC,
ITT Cannon,
LTEL
Presented by: Masa Hirayama, LTEL

## Slide 2
Proposal Outline:
1. Application to the current 802.11 MAC.
10Mbps and higher in the near future
2. Adjustment of the current PHY.
Applicable on the higher transfer rate

## Slide 3
Factors to be considered:
1. Precondition that the current MAC
is to be applicable on 10-25-100Mbps.
2. Proposal that the current 4PPM-PHY or 16PPM-PHY is to be adjusted for DMI Modulation.
(DMI: Differential Mark Inversion)

## Slide 4
Basic Connection Concept:
802.11
MAC
IR Modulation
(DMI Modem)
IR signal

## Slide 5
Performance of the new DMI Modem:
Error Rate: less than 10-10
Service Area: within the radius of 1m with
the spot reflection on the ceiling
Radiation Angle: +10’
MAC & PHY: adjusted MAC & PHY

## Slide 6
Setting of the Access Points on the ceiling:
A
B
C
AP1
AP2

## Slide 7
IR Energy Calculation from the Access Point:
Pap=40(mW) x 24=960mW
So=25pi x 104=7.85 x 105(cm2)
if PD-square is 1cm2
Ppd=Pap/So=0.96/(7.85 x 105)=1.22 x 10-6(W)
( Pmin=700nW=0.7 x 10-6W )

## Slide 8
Example of IR Communication with Wide Area Ceiling Reflection
A
B
C

## Slide 9
IR Energy Calculation:
Pmax=960mW
So=25pai x 104(cm2)
Ss=(So/3-5x5x1.73/2 x 104) x 2
=(26.18-21.65) x 2 x 104
=9.06 x 104(cm2)
Pss=(Pmax) x Ss/So
=960(mW) x 0.115
=110(mW)
if Pd square is 1cm2,
Ppd=0.11/So=1.4 x 10-7(W)
=140nW

## Slide 10
Proposed Application on the current MAC:
Error Rate: more/less than 10-10
Service Area: within the radius of 5m with
wide area reflection on the ceiling
directly under the Access Point
Radiation Angle: +60’ (with the hight of 2.5m)
MAC & PHY: applicable on the current MAC
and adjustment function to be
added on the current PHY
for DMI module

## Slide 11
Proposal of the adjusted PHY:
Current PHY with 4 and 16PPM:
Current modem circuit is fairly complicated, and the current PHY with 16PPM may not cope with the higher transfer rate imposing heavy burden on LED and optical circuit
Proposal of adjusted PHY for DMI Modulation:
Basic application of Bi-Phase Modulation for
easy DMI approach and better LED efficiency

## Slide 12
Pulse Wave Comparison in IR Modulation:
16PPM
4PPM
DMI
NRZ
0 1 1 1 0 0 0 0 1 1 1 1 0 0

## Slide 13
Difference of LED Performance:
Current IR 4-16PPM Modulation:
In 10Mbps Data Transfer, the minimum Pulse
Duty Ratio is 1/1 to 1/6 for 4PPM, and
1/1 to 1/30 for 16PPM
Proposed DMI Modulation:
In 10Mbps Data Transfer, the maximum and
minimum pulse width are 50ns and 100ns;
Easy Synchlonized Extraction
Easy Optical Circuit with the Averaged Pulse
Slower Response Capacity on LED

## Slide 14
Expandability / Applicability in the Future:
Expandable Application to the higher Transfer Rate:
DMI Modulation is easily applicable to 10, 25 to100Mbps
Networking Communication:
Easily applicable to CSMA/CD and
both Stable/Fixed and/or Portable/Mobil Communication

## Slide 15
“Header” Construction for the DMI Modulation: P: Preamble 24bit F: Flag 8bit A: Address 8bit ID: Identification Address 8bit R: Reserve 8bit CRC: Cyclic Redundancy Check 16bit
P
F
A
ID
R
CRC
Ether net data

## Slide 16
Summary:
MAC: Establishing Compatibility with the current
MAC
PHY: Adding Adjustment Function and Header on
the current 4 & 16PPM PHY for
DMI Modulation