## Slide 1
Transmission Security (TRANSEC)
John H. Cafarella
MICRILOR, Inc.
Wakefield, MA

## Slide 2
TRANSEC vs. Data Encryption
TRANSEC
  Waveform-Domain
  Protection Against Jamming, Spoofing and Traffic Analysis
  Protection for Seconds
  Local Coordination
Needed by All Users for Most Transmissions
Data Encryption
  Data-Domain
  Protection Against Disclosure of Data to Any Unauthorized Party
  Protection for Decades
  Net-Wide Coordination
Needed by Few Users for Some Data

## Slide 3
Example Repeated Code Attack
Little A Priori Information
  know that code is repeated, and its length
  don’t need code pattern
~ 3 dB less than full Processing Gain
No SSDS Protection; Must Add Encryption
~
~
~
~
~
~
NCTC
BSS
BSymbol
requires frequency offset to preserve complex signal
Data Modulation on Spread-Spectrum Carrier
Data Demodulation Statistic on Carrier

## Slide 4
DUWL/M10 TRANSEC
Security Code Channel (SCC) Seeds LFSR
Initial Acquisition Uses Non-Changing Code
Data “Frame Sync” Provides Time Alignment
PN Code Sequence Does Not Reveal LFSR States
PN Codes Selected for Best Multipath Performance
Linear Feedback Shift Register Generator
PN Code
ROM
Shift Reg.
SCC
Serial PN Code to Correlator De-Spreader

## Slide 5
PN Code Selection
16 bits: 32K Codes
(plus compliments)
Functions W0-W15
  Proper Subgroup
  Coset Decomposition
  PN Code Coset Leaders
  2048 Cosets
Pick Cosets Having Low Near-In Crosscorrelation Side Lobes
W0 W1 W2 W3 W4 W5 W6 W7 W8 W9 W10 W11 W12 W13 W14 W15
PN1
PN2
PN3
PN4
PN5
PNxWy

## Slide 6
TRANSEC Summary
Change PN Codes Symbol-to-Symbol
Synchronize in Repeated-Code Header
Code Channel = PN Code Sequence
Use Only “Good” PN Codes (Multipath)
Still Use Encryption for Select Data