## Slide 1
ROBUST 10-Mbps: MODULATION
John H. Cafarella
MICRILOR, Inc.
Wakefield, MA

## Slide 2
DSSS vs. Multipath Interference
Channel impulse response
envelope of average
multipath response vs. delay
Symbol waveform correlation
main-lobe
response
side-lobe
response
envelope
Received waveform correlation
Intrasymbol Interference Mitigation Demands:
  Increased Processing Gain to Avoid High “Irreducible Error Rate”
  Use of More Bits/Symbol for Required Data Rate
side-lobe of multipath signal interferes with main-lobe of direct-path signal

## Slide 3
Another Viewpoint
x
x
Data
Modulator
Data
Demodulator
+
white noise,
interference,
multipath
spreading
waveform
synchronized
de-spreading
waveform
De-Spread Channel
white noise plus spread
interference and multipath
f0-fc
f0+fc
Approximates white noise channel
Data bandwidth can be large
(if synchronous to spreading)
Physical Channel

## Slide 4
Data Modulation Selection
Processing Gain is chip rate divided by symbol rate; no penalty for wider data-modulation bandwidth
Spread-spectrum signaling allows the use of Power-Efficient Data Modulation

## Slide 5
Jammer/Signal Ratio Comparison
DPSK
4 chips/bit
PG = 6 dB
10 dB EB/N0
J/S= -4 dB
16-ary Orthogonal
16 chips/symbol
PG = 12 dB
13 dB ES/N0
J/S = -1 dB
J/S=PG-ES/N0 with Implementation Loss ignored
Same chipping rate and data rate
Numbers rounded to nearest dB
DQPSK
8 chips/symbol
PG = 9 dB
15 dB ES/N0
J/S= -6 dB

## Slide 6
Bi-Orthogonal Modulation Adds Another Bit
For Coherent Signaling
  Send One of M Waveforms: Log2M Bits
  Sign Conveys Additional Bit
For Non-coherent Signaling
  Send One of M Waveforms: Log2M Bits
  DPSK Between Symbols Conveys Extra Bit
16-ary Bi-Orthogonal Yields 5 Bit/Symbol

## Slide 7
Orthogonal Modulations with DSSS
Pulse-Position Modulation
  requires time gaps to accommodate multiple time positions
  can be confused in multipath
Frequency-Shift Keying
  requires extra bandwidth (convolves DSSS & M-FSK spectra)
Cyclic Code-Shift Keying (as in JTIDS)
  inter-symbol partial correlations unless time gaps inserted
  can be confused in multipath
Walsh-Function Orthogonal Signaling
  most natural for DSSS (Walsh-function sub-elements = DSSS chips)

## Slide 8
Walsh Functions
2N Functions Orthogonal Over 2N Chips
Rademacher Function Products
  Subgroup Structure
Easily Generated
Efficiently Processed
PN-Code Cosets
  Controlled Correlations
W0=R0
W1=R1
W2=R2
W3=R2W1
W4=R3
W5=R3 W1
W6=R3 W2
W7=R3 W3
W8=R4
W9=R4 W1
W10=R4 W2
W11=R4 W3
W12=R4 W4
W13=R4 W5
W14=R4 W6
W15=R4 W7
(“Natural” Order)

## Slide 9
Optional Coding
Used to Combat “Irreducible Error Rate”
High-Rate R/S Code (Modified)
  Minimal Reduction of Data Rate (8.67 Mbps)
  Approximately 2-dB Coding Gain
Short, Single-Error-Correcting Block Code
  Non-Iterative Decoding
  Very-Low Latency
Simple Hardware Implementation

## Slide 10
Data Transmission
FIFO Buffer
P-S/S-P shift reg.
5
8
FEC Subsystem
5
4
DPSK Mod.
Walsh fn. gen.
PN Code gen.
Baseband Transmit Signal
Optional (15,13)
Chip Clock

## Slide 11
Baseband Walsh Correlator
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
S
D
fc
I or Q Baseband Signal
1 sample/chip
fc/2
fc/4
fc/8
16 Walsh-Function Symbol Correlations
at
< Half the Power of 16 Independent Correlators
16 Accumulators
Full Precision
Clocked at fc/8
2 Accumulators
Least Precision
Clocked at fc
PN Code
fc

## Slide 12
Data Demodulation
Baseband Walsh Symbol Correlator
I Channel
Signal
Baseband Walsh Symbol Correlator
Q Channel
Signal
Compute Channel-by-Channel Magnitude
(determine largest)
Index of Largest
DPSK Decision
Complex Amplitude of Largest
Z-1
Previous Complex Amplitude
5
4
5-bit Demodulated Symbol

## Slide 13
PN Code Selection
16 bits: 32K Codes
(plus compliments)
Functions W0-W15
  Proper Subgroup
  Coset Decomposition
  PN Code Coset Leaders
  2048 Cosets
Pick Cosets Having Low Near-In Crosscorrelation Side Lobes
W0 W1 W2 W3 W4 W5 W6 W7 W8 W9 W10 W11 W12 W13 W14 W15
PN1
PN2
PN3
PN4
PN5
PNxWy

## Slide 14
Data Modulation Summary
10 Mbps Modulation
  Robust in Multipath and Interference
  12-dB Processing Gain
  7 dB EB/N0
  Natural Match to DSSS
Optonal FEC + Good PN Codes (Multipath)
Efficient Implementation