## Slide 1
IEEE 802.11 Wireless Access Method and Physical Specification
Title: Carrier Frequency Offset-Spread Spectrum
(CFO-SS) Scheme for Higher Speed 2.4 GHz PHY
Date: January 19, 1998
Author: Hiroyasu Ishikawa and Hideyuki Shinonaga
KDD R&D Laboratories
2-1-15, Ohara, Kamifukuoka,
Saitama, 356, Japan
Telephone: +81(492)78-7856
FAX: +81(492)78-7524
e-mail: ishikawa@lab.kdd.co.jp, shinonaga@lab.kdd.co.jp
Notes: 1

## Slide 2
Notice
This document has been prepared by KDD R&D Laboratories to assist the Standard Working Group IEEE P802.11b.
KDD specifically reserves the right to amend or modify the material contained in the proposed document.
Nothing herein shall be construed as conferring or offering licenses or rights with respect to any intellectual property of KDD.
Some simulation results are based on Japanese standards. However, those could be discussed in relation to IEEE P802.11 standards.
KDD is currently developing a 10 Mbit/s ISM band wireless communication equipment employing the CFO-SS scheme.

## Slide 3
Japanese 2.4 GHz ISM Band
Operating Frequency Range
USA: 2.4 to 2.4835 GHz
( Total bandwidth = 83.5 MHz, one sub-band = 22 MHz )
JAPAN: 2.471 to 2.497 GHz
( Bandwidth = 26 MHz, one sub-band only)
Number of Operating Channels
USA: Three sub-bands are available
JAPAN: Only one sub-band is allocated, which should be shared by multiple systems and multiple users.
Notes: 2

## Slide 4
Out of band rejection mask of Japanese (RCR) and IEEE 802.11 Standards
Notes: 5

## Slide 5
What is CFO-SS?
CFO-SS is an abbreviation of “Carrier Frequency Offset-Spread Spectrum”, which is a kind of synchronous multi-carrier DS CDMA technique and utilizing a single PN (Barker) code commonly assigned to all the multiple carriers. Orthogonality among multiple carriers are achieved by specially selected carrier frequencies.
CFO-SS employs a receiver with surface acoustic wave (SAW) matched filters (or baseband digital matched filters) to achieve rapid signal acquisition.
Good performance is achieved by CFO-SS even under multipath fading environment.
Hardware is simple. 10 Mbit/s CFO-SS transceiver basically consists of five units of the 2 Mbit/s 2.4 GHz wireless LAN terminal. One clock tracking circuit is only required which is shared by five units.
CFO-SS requires no special equalizing technique.

## Slide 6
Theoretical explanation of the CFO-SS
The correlation peak value is obtained by the following equation when a frequency offset exists between the carrier frequency of the SS signal and the nominal operating frequency of the SAW matched filter.
Y: Amplitude of the correlation peak T C : Chip duration [sec]
X: Frequency offset [Hz] N: Length of the PN code [chip]
Notes: 8

## Slide 7
Principle of CFO-SS scheme
Correlation peak vanishes at the frequencies specified by the information rate.
For 10 Mbit/s five channel system, minimum channel separation is 1 MHz. However, 2 MHz separation makes the system strong against multipath fading.
Multiple signals spread by a single PN code can be multiplexed without interfering one another(orthogonality among multiple carriers) if the following conditions (CFO conditions) are simultaneously satisfied.
(1) The symbol timing in each channel are synchronized with the PN code.
(2) PN codes of all the channels are synchronized.
Notes: 4

## Slide 8
Example transmitter configuration of CFO-SS system with a five channel model
Notes: 9

## Slide 9
Example receiver configuration of CFO-SS system with a five channel model
Notes: 10

## Slide 10
Output waveforms of SAW matched filter
Notes: 11

## Slide 11
Eye diagram of CFO-SS system when five channels are multiplexed
Notes: 13

## Slide 12
Implementation
RF/IF complexity
1) RF unit consists of antenna, divider, combiner, power amplifiers and LNA’s.
2) IF unit basically consists of five units of the 2 Mbit/s PHYs.
3) One clock tracking circuit is shared by five units.
Baseband processing complexity
1) Serial-Parallel translator.
Equalizer complexity
CFO-SS does not require a special equalizer.
Diversity implementation
Conventional selection diversity technique is also adequate to CFO-SS.

## Slide 13
Configuration of CFO-SS Terminal

## Slide 14
Antenna and RF Unit

## Slide 15
Timing recovery method for CFO-SS system
Step 1: Find the maximum average absolute output level Amax for N symbol duration

## Slide 16
Step 2: Carrier Detection State
Definition:
Carrier detected: Amax exceeds the predetermined threshold level.
Carrier not detected: otherwise

## Slide 17
Step 3: Initial Acquisition State
First, select the sampling point with Amax, and define its sampling number as Smax .
If the average absolute output level A at Smax continuously exceeds the predetermined threshold level till B state, then move to tracking state.

## Slide 18
Definition of time window in the tracking state
Select the sampling point which shows the A within the time window as the center of the time window for the following N symbols.

## Slide 19
Tracking State
Center of time window is initially defined by Smax in the initial acquisition state

## Slide 20
Eye diagram during preamble
By choosing a preferable preamble pattern for each channel, the center channel shows a clean pulse waveform to facilitate easy clock acquisition.
Rapid timing recovery and acquisition are accomplished without any difficulties.

## Slide 21
Simulation parameters
Number of channels : 3 & 5
Channel separation : 2 MHz
Frame length : 64 Bytes & 1000 Bytes
Preamble length : 64 symbols (64 msec)
PN code : 11 chip Barker sequence
Chip rate : 11 Mchip/s
Transmission rate : 2 Mbit/s
Total transmission rate : 6 Mbit/s & 10 Mbit/s
Modulation technique : SS/QPSK
Demodulation technique : Differential detection as prescribed by IEEE802.11
Band pass filter : 8th order Butterworth filter
3 dB bandwidth of BPF : 17 MHz
Timing recovery and acquisition : As described in this document
Notes: 12

## Slide 22
Line-of-sight two path model
C/D: Received power ratio of the coherent signal to the delayed signal
Dt : Arrival time difference of the coherent signal and the delayed signal

## Slide 23
BER Performance of CFO-SS System with Band Limitation under AWGN environment

## Slide 24
BER performance of CFO-SS system when Dt=45.45 nsec.
5 ch: 10 Mbit/s
3 ch: 6 Mbit/s
Notes: 15

## Slide 25
BER performance of CFO-SS system when Dt=90.9 nsec.
5 ch: 10 Mbit/s
3 ch: 6 Mbit/s
Notes: 16

## Slide 26
Relationship between BER and Dt
Notes: 17

## Slide 27
Overhead related parameters
Preamble length:
- 128 bits for synchronization is enough for CFO-SS under multipath fading environments, which is the same as the current 2 Mbit/s 2.4 GHz PHYs.
- Rapid acquisition is realized by a specially selected preamble pattern.
Slot size:
- Same as the current 2 Mbit/s 2.4 GHz PHYs.
Carrier Sense / Clear Channel Assessment Procedure:
- Same as the current 2 Mbit/s 2.4 GHz PHYs.
SIFS time:
-Almost the same as the current 2 Mbit/s 2.4 GHz PHYs.
-Process time depends on the CPU employed.
-Special techniques like equalization, deinterleaving, FEC are not mandatory.

## Slide 28
Transmission rate and channel bandwidth
10 Mbit/s five channel wireless LAN can be implemented within 26 MHz bandwidth.
Transmission rate can be designed to be 2, 4, 6 Mbit/s meeting the current 2 Mbit/s IEEE out of band rejection mask.
By control, 2, 4, 6, 8 and 10 Mbit/s rate can flexibly be selected.
Spectral Efficiency and Channel Allocation
Three sub-bands of 26 MHz can be allocated in US ISM band.
When a scanned sub-band is busy, then the CFO-SS terminal searches a vacant sub-band.
Notes: 7

## Slide 29
Service rage:
Office use (Point-to-multipoint): ~ 50 m
Point-to-point use: ~ 1 km
Throughput performance:
The throughput performance of 10 Mbit/s CFO-SS is five times of the current 2 Mbit/s systems.
Adjacent Channel Interference:
CFO-SS does not have to take care on the influence of ACI since the previous channel selection method is applied to search a vacant sub-band.
Co-Channel Interference:
CFO-SS requires no special CCI rejection technique.
CCI could be avoidable by CSMA/CA technique.
Immunity to CW jamming :
The immunity at 10% packet drop rate is to be investigated.

## Slide 30
Critical Points
Sensitivity to phase noise:
- To be evaluated by the CFO-SS hardware.
Power consumption (DC):
- Five times of that of the current 2 Mbit/s PHYs.
Complexity:
- Hardware architectures are simple.
- Oscillator with an accuracy of +/-12 ppm is sufficient.
- AGC with wide dynamic range ( ~ 60 dB) might be required.
RF PA backoff:
- Each 2 Mbit/s transceiver is equipped with an independent PA to avoid intermodulation.
- Alternatively, one PA with sufficient back-off could be employed to ensure linear operation.
Diversity techniques:
- If the operation environment is very severe, CFO-SS might need a diversity technique to improve the channel quality.

## Slide 31
Additional conditions for the current 2 Mbit/s 2.4 GHz PHYs
Add two modems for 6 Mbit/s implementation.
Add four modems for 10 Mbit/s implementation.
Set RF channel frequencies to meet the CFO condition.
Synchronize PN timings of each channel.
Timing recovery circuit is required only in one channel.
The algorithm of the timing recovery method shall be as described in this document.
Notes: 6

## Slide 32
Interoperability
Interoperability at the data level:
- By employing buffer, the system can work with the rate of 2, 4, 6, 8 and 10 Mbit/s. The data rate can be notified to the receive side through the preamble.
Interoperability at the antenna level:
- CSMA/CA protocol need not to be changed.
Identify 2 Mbit/s PHY(s):
- CFO-SS terminal could recognize the transmission rate by receiving the preamble data of each packet.
Dual schemes (i.e fast vs. low rate preamble) :
- Only one type of preamble is employed for 2, 4, 6, 8 and 10 Mbits rate.

## Slide 33
Co-existence
CFO-SS can coexist with the current 2 Mbit/s 2.4 GHz PHYs.
CFO-SS has a function of operating as 2, 4, 6, 8 and 10 Mbit/s 2.4 GHz PHYs by activating appropriate channels.
10 Mbit/s CFO-SS wireless LAN can connect with the current wireless LAN terminals by detecting the bit rate of the received signal and setting its own rate.

## Slide 34
Schedule of CFO-SS development
KDD is developing a 10 Mbit/s CFO-SS point-to-point wireless equipment to be completed in February 1998.
KDD will assess the performance of 10 Mbit/s CFO-SS terminal under various propagation models by field and indoor experiments.
CFO-SS 10 Mbit/s transceiver with an Ethernet interface will be demonstrated at NAB ‘98, in Las Vegas in April.
CFO-SS modem is smaller than B5 size. It might be compatible with a PCMCIA card if ASICs are developed.

## Slide 35
Intellectual property right
KDD’s position:
KDD follows the IEEE Patent Policy set forth in Clause 5 of the IEEE Standards Board Bylaws.
Applicable patent numbers:
US Patent number: 5,319,672. M. Sumiya and H. Shinonaga, “Spread Spectrum Communication System.”, Jun. 7, 1994.
One Japanese patent had been authorized.
Three Japanese patents pending.
Point of contact:
Shouzou Hikasa, Network planning Department, Network Headquarters, KDD ltd.
(TEL:+81-3-3347-5371/FAX:+81-3-3347-6362)
(E-mail:sh-hikasa@kdd.co.jp)

## Slide 36
Summary
CFO-SS is a kind of synchronous multi-carrier DS CDMA technique, which utilizing a single PN (Barker) code commonly assigned to all the multiple carriers.
Simulation results show that CFO-SS shows good performance under multipath fading environment.
Hardware is simple. CFO-SS transceiver basically consists of multiple transceiver units of the 2 Mbit/s 2.4 GHz wireless LAN terminal.
CFO-SS requires no special techniques like equalizer, channel estimator, frequency offset compensation.
CFO-SS is backward compatible with the current 2 Mbit/s 2.4 GHz PHYs. Furthermore, 2, 4, 6, 8 and 10 Mbit/s rate can flexibly be set.