## Slide 1
MAC Requirements on High-Speed 2.4 GHz PHY Design
Ronald Brockmann
No Wires Needed BV
January 1998 Doc: IEEE P802.11-98/32

## Slide 2
Goals for High-Speed PHY
Provide high peak bandwidth per AP
Provide fair sharing of spectrum between APs
Minimize loss of bandwidth through collisions/co-channel interference
Good performance in all topologies
Low-speed coexistence/interop.
Work with existing MAC

## Slide 3
Cell Planning
In a typical site, more than one AP is present
Therefore, cells need to be isolated from eachother
Possible means
  Time Division (TDMA)
  Code Division (CDMA)
  Frequency Division (FDMA)

## Slide 4
Inter-Cell Time Division
Existing MAC mechanisms
Use Physical and Virtual Carrier Sense to share channel
Hidden terminals
Effective bandwidth per AP is fraction of channel bandwidth
Does not allow use of PCF

## Slide 5
Inter-Cell Code Division: Near-Far Problem
Transmission by STA may disturb frame reception by nearby STA using different code
MAC has no way of detecting this
  No physical carrier sense (correlation)
  RTS-CTS of adjacent cell cannot be heard
MAC not designed for this problem

## Slide 6
Near-Far Problem between cells
Code 1, STA
Code 1, AP
Code 2, STA
Code 2, AP

## Slide 7
Inter-Cell Code Division:
Current MAC does not deal well with the near-far problem
May effectively reduce to ALOHA
Problems with one STA affect performance in the entire BSS
Effective throughput may be very low

## Slide 8
Inter-Cell Frequency Division
Multiple channels
Good isolation between cells, even if incompatible radios/protocols
Adjacent cells on different channels
Sufficient distance between cells on the same channel
Optimum number of channels?

## Slide 9
Therefore..
Coding is mandatory to provide processing gain
However, code division is not a good idea
Provide small but sufficient number of channels
Existing MAC mechanisms to share channels

## Slide 10
What about backward compatibility?
MAC supports backwards compatibility with 802.11 DS if:
  identical channelization
  compatible preambles
  identical parameters (slot times etc)
Use short preamble for high-speed, no interoperability mode

## Slide 11
Suggested Framework for High-Speed 2.4 GHz PHY
Use 802.11 DS channelization (3 to 4 channels)
Use 802.11 DS parameters (slot times, DIFS, SIFS,..)
TBD high-speed modulation for MPDU
Option for 802.11 DS preamble
Option for high-speed preamble

## Slide 12
Benefits
High peak bitrate
Efficient spectrum sharing
Good performance in multi-AP sites
Backward compatibility (long preamble)
High Speed, Coexistence (short preamble)
No changes to MAC

## Slide 13
Future Work: Case Study
Need to demonstrate that channelization is sufficient in real-life
Work needs to be done on efficiency of TDMA sharing of channel for different modulation methods
More in March?