## Slide 1
High Speed 2.4 GHz PHY and the PLCP Header Length Field
Ronald Brockmann
No Wires Needed BV
January 1998 Doc: IEEE P802.11-98/33

## Slide 2
Assumption
2.4 GHz High Speed PHY will have a backward compatibity mode using 802.11 DS preambles

## Slide 3
Background
Current PLCP Header allows high-rate PHY extensions through the Rate field
Length field is expressed in microseconds for backward compatibility
MAC requires PHY to recover exact MPDU length in octet resolution

## Slide 4
The Problem
Need uniform, deterministic way of translating ms to octets and octets to ms for odd rates (e.g. 5 or 5.5 Mbit/s)
For bit rates > 8 Mbit/s, ms resolution is insufficient to provide accurate translation into octets
For example at 10 Mbit/s, 1.25 octets go into one ms

## Slide 5
Proposed Solution
Use MSB of Service field as new LSB of Length field
Extended Length field is a 17 bit value, 0.5 ms resolution
Backward compatible
Supports rates up to 16 Mbit/s

## Slide 6
PLCP Header Revisited
EXT_LEN
17 BITS
SERVICE 7 BITS

## Slide 7
Proposed Solution Contd
Standardize on these conversion formulas:

## Slide 8
Example
Rate = 10
Transmit Octets = 63
plcp_ext_len = 101 = 50,5 ms
Receive Octets = 63
Without the additional half-microsecond resolution, this may not work out!