## Slide 1
QPSK Modulation for 5GHz-band Wireless LANs (Comparison) January, 1998 Kazuhiro OKANOUE, Yoshikazu KAKURA, Tomoki OHSAWA NEC Corporation 4-1-1, Miyazaki, Miyamae-ku, Kawasaki, 216 Japan Tel: +81 44 856 2255 Fax: +81 44 856 2230 E-mail: {okanoue,kakura,ohsawa}@ccm.CL.nec.co.jp
IEEE P802.11
Wireless LANs
Notes: Abstract
This document describes draft specifications for a QPSK modulation system for 5GHz band high speed wireless LANs PHY. Simulation results and discussions for the specifications are also described.

## Slide 2
Main Parameters for QPSK Modulation
Modulation Method: QPSK
Baseband Filter: Root Nyquist Filter (Rolloff=50%)
Symbol Rate: 12.5Msymbol/sec or 10Msymbol/sec
FEC: (31,26) BCH with parity bit for 12.5M sps or
No FEC for 10M sps
Notes: A proposed modulation method is QPSK modulation with 12.5M symbol/sec coded by (31,26) BCH code with a parity bit or 10M symbol/sec with no error correction code.
For the 12.5M symbol/sec system, the coding rate is 26/32(=0.8125). Therefore, information transmission rate is 20.3125M bit/sec.

## Slide 3
Phase constellation of QPSK Modulation
DEMUX
cos(p/4+(1-Xk)p)
sin(p/4+(1-Yk)p)
Root
Nyquist
bit stream
even
odd
Yk
Xk
Ik
Qk
Root
Nyquist
RF/IF cuircuit
Notes: This figure shows a typical baseband structure of a modulator. An input bit stream is divided into even and odd streams, Xk and Yk. The Xk and Yk are converted to Ik and Qk to be mapped into phase diagram shown in the figure.
Root nyquist filter with roll off facter 50% shapes Ik and Qk.

## Slide 4
Basic Receiver Architecture
Notes: The figure shows a typical receiver architecture. A diversity reception is an optional. First of all, received signals are fed into an AGC system and adjusted their input level.
Then a frequency offset in the received signals is estimated by an AFC system. A PLL uses the estimated offset value from the AFC as its initial value. The estimated offset is also fed into a phase shifter to cancel frequency offset in the received signal.
Then impulse response estimator estimates channel impulse response vector and supplies the estimated vector to an anti-multipath scheme such as an equalizer.
The anti-multipath scheme outputs decision results and error signals to the PLL to adaptively cancel frequency offset in the received signals.

## Slide 5
Past Metric Addition MLSCE (PMA-MLSCE)
Symbol-by-Symbol detection based on Maximum Likelihood Sequence Estimation during Channel Impulse Response duration
Low calculation amount by using decision results
Notes: As an example of the anti-multipath scheme, we can use a Past Metric Additnon MLSCE (Maximum Likelihood Symbol Candidate Estimator).
The principle of the scheme is the following two points;
symbol-by-symbol detection based on maximum likelihood sequence estimation during a channel impulse response duration
low calculation amount by using decision feed back.

## Slide 6
State Transition on PMA-MLSCE
t=i
t=i-1
t=i-2
s(i): symbol candidate
D(i-k): Decision result at t=i-k
r(i): received signal at t=i
(s(i),D(i-1),D(i-2))
(s(i-1),s(i),D(i-1))
(s(i-2),s(i-1),s(i))
(0,D(i-1),D(i-2))
(1,D(i-1),D(i-2))
(0,0,D(i-1))
(0,1,D(i-1))
(1,0,D(i-1))
(1,1,D(i-1))
(0,0,0)
(0,0,1)
(0,1,0)
(0,1,1)
(1,0,0)
(1,0,1)
(1,1,0)
(1,1,1)
state
S(t)
Example for channel impulse response(h) of length 3 and binary symbol
|r(i-2)-S(i-2)h|
|r(i-1)-S(i-1)h|
|r(i)-S(i)h|
+
+
Minimum
Detection
Possible
transition
Possible
transition
Notes: This figure shows an example of state transition for the 3tap PMA-MLSCE to estimate s(i) transmitted symbol at t=i. It is assumed that a transmitted symbol is binary, the length of a channel impulse response is 3 and the current time is i.
In this example, the PMA-MLSCE defines three state vectors S(t) for t=i, i-1 and i-2 which are consisted from symbol candidates s(i)’s and/or decision results D(i)s. Because D(i)s are deterministic, each state vector can take only 2m values where m is the number of symbol candidates in a vector. Then transitions between the state vectors can be defined as shown in the figure.
The PMA-MLSCE calculates metric, |r(i-k)-S(i-k)h| for all possible state vector values. The calculated metric are summed up along the transitions as a combined metric. The PMA-MLSCE selects a transition which presents the minimum combined metric and outputs the s(i) in the transition as a estimated results.
An implementation example of the part surrounded by the dotted line are demonstrated in the next slide.

## Slide 7
Example of PMA-MLSCE
Notes: This figure shows an implementation example of PMA-MLSCE.

## Slide 8
Channel Impulse Response Estimator
SEQ64
SEQ64*
~
~
head n-bit
of SEQ64
0
1
n
-m
1
0
0
0
0
0
0
t
...
...
correlator
~
SEQ64*
SEQ64*
last m-bit
of SEQ64
SEQ64=(X0Y0X1Y1…X30Y30X31Y31)
=(0xFF 0xF0 0xF3 0x30 0xC0 0x0F 0x0C 0xC0)
32 symbols
-1
Notes: This figure shows an example of a channel impulse response estimator. By using a preamble sequence of which correlation function becomes impulse, a channel impulse response can be obtained by calculating correlation between a received preamble and the preamble sequence itself.
We propose to use the SEQ64 for a preamble. The correlation function of the SEQ64 is presented at next page.

## Slide 9
Correlation function of SEQ64
Notes: This figure shows a correlation function of the SEQ64. It is shown that the correlation function becomes a impulse during 26 symbols.
We will present a receiver performance with the PMA-MLSCE and the channel impulse response estimator.

## Slide 10
Receiver Performance -sensitivity-
4tap PMA-MLSCE
FEC:(31,26) BCH
Notes: This figure shows a sensitivity of a receiver for 64- and 1000-byte long packet.
For 64-byte long packets, Packet Error Rate (PER) of 10% can be obtained at Eb/N0= 9dB and 6.5dB with and without FEC, respectively.
For 1000-byte long packets, Packet Error Rate (PER) of 10% can be obtained at Eb/N0= 10.5dB and 8dB with and without FEC, respectively.

## Slide 11
Receiver Performance -Delay spread (1) -
4tap PMA-MLSCE
FEC:(31,26) BCH
Notes: This figure shows PER against multipath fading without any Gaussian noise.
The receive can achieve PER of 10% against multipath fading with 145usec and 135 usec delay spread for 64- and 1000-byte long packets, respectively. A FEC gain is very little for both 64- and 1000-byte long packets.
In this simulation, it is assumed that the symbol rate is 12.5Msps. For 10Msps, PER of 10% can be obtained in multipath environments with delay spread of 181.25 usec and 168.75 usec for 64- and 1000-byte long packets, respectively.

## Slide 12
Receiver Performance -Delay spread (2) -
4tap PMA-MLSCE
FEC:(31,26) BCH
Notes: This figure shows receiver performance in conditions where both multipath fading and Gaussian noise exist.
For 64-byte length packets, PER of 20% can be achieved at Eb/N0 = 18dB and 17dB without and with FEC, respectively.
For 1000-byte length packets, PER of 20% can be achieved at Eb/N0 = 22.5dB and 22dB without and with FEC, respectively.

## Slide 13
Receiver Performance -Adjacent channel -
Notes: This figure shows receiver performances for 64-byte long packets against adjacent channel interference.
When ideal root nyquist filters for a transmitter and a receiver and an ideal linear amplifier filters are adopted, degradations of PER are negligible at DURs larger than –30dB against an adjacent channel of 18.75MHz separation. We need to study PERs for more realistic filters and amplifiers.

## Slide 14
Receiver Performance - co-channel interference -
Notes: This figure shows receiver performances against co-channel interference.
Though we have simulated at two points, receiver can achieve PER less than 10% at desired-to-undesired ratio (DUR) of 20dB.

## Slide 15
Receiver Performance - CW jamming -
Under Simulating!

## Slide 16
Receiver Performance - Gaussian jamming -
Under Simulating!

## Slide 17
Example of AFC structure
1
2
N
K
1
2
N
K
1/(KN)
Dq:phase difference per symbol
Df1...DfN:phase offset during K symbols
Df2
Df1
DfN
Dq
S
K symbols
K symbols
the same sequence
Notes: This figure shows an example of AFC structure.
As long as a multipath fading channel is time invariant, received signals produced by the same two sequences are identical. Therefore, by comparing a phase difference between corresponding symbols, frequency offset can be estimated. In order to remove fluctuations caused by Gaussian noise, the phase difference need to be averaged over several symbols.

## Slide 18
Example of PLL Structure
PMA-MLSCE
decision
averaging
phase detector
r(i)-S h
Dfi
error signal
Dq
PLL
Notes: This figure shows an example of PLL structure.
A PMA-MLSCE calculates replica of received signals, Sh. By averaging a phase of an error signal between received signal r(i) and the replica, a frequency off set can be estimated. The performances of the PLL is under simulating now.

## Slide 19
Receiver Performance -F-Offset (AFC-1)-
Notes: This figure shows PER in multipath fading channel for 64-byte packets. A delay spread, an averaging duration and Eb/N0 is set to 145usec and 16 symbols and infinity, respectively. It is shown the AFC can compensate frequency offset less than 175kHz. 175kHz is 35 ppm for 5GHz.

## Slide 20
Receiver Performance -F-Offset(AFC-2)-
Notes: This figure shows PER in static channel for 64-byte packets. Eb/N0 is set to 10dB. It is shown that thermal noise degrades AFC capability seriously. However, we consider that a PLL for a whole packet duration will improve the degradation.

## Slide 21
Receiver Performance -F-Offset(AFC&PLL)-
Under Simulating!

## Slide 22
Frame structure
SEQ64=(X0Y0X1Y1…X30Y30X31Y31)
=(0xFF 0xF0 0xF3 0x30 0xC0 0x0F 0x0C 0xC0)
Notes: This figure shows a proposed frame format. The PLCP Preamble consists of 124 symbols in a SYNC field and 8 symbols in a SFD (Start Frame Delimiter) field. The PLCP header includes both a 8-symbol header error check filed and a 6-symbol PSDU length word. The rest 2 symbols in the PLCP header are used for PLCP control information.
The SYNC filed is basically formed as a repetition of the 64-bit sequence, SEQ64. The SEQ64 can be represented based on the Xk and Yk, as follows;
SEQ64=(X0Y0X1Y1 X2Y2X3Y3 … X30Y30X31Y32)
=(1111 1111 1111 0000 1111 0011 0011 0000 1100 0000 0000 1111 0000 1100 1100 0000).
This figure also shows a structure of SYNC field. A receiver executes antenna selection, AGC (Automatic Gain Control) setup, AFC (Automatic Frequency Control) setup and channel impulse response estimation through the SYNC filed.

## Slide 23
Slot time and SIFSTime
SlotTime=CCATime+RxTxTurnaroundTime+AirPropagationTime+MACProcessingTime
SIFSTime=RxRFDelay+RxPLCPDelay+MACProcessingDelay+RxTxTurnaroundTime
SlotTime=(TBD)usec
SIFSTime=(TBD)usec
Notes: Slot size is defined as a summation of CCATime, RxTxTurnaroundTime, AirPropagationTime and MACProcessingTime. The RxTxTurnarroundTime is obtained as a summation of TxPLCPDelay, RxTxSwitchTime, TxRampOnTime and TxRFDelay. The CCATime includes CCADetectTime and RxRFDelay. The proposed Slot size is TBD.
SIFS time is obtained as a summation of RxRFDelay, RxPLCPDelay, MACProcessingDelay and RxTxTurnaroundTime. The proposed SIFS time is TBD.
AirPropagationTime is considered to be constant for any modulation methods, we would like to fix it in the meeting. For RxTxSwitchTime, we need to consider RF/IF device performance more

## Slide 24
CCA mechanism
Notes: As a CCA detection mechanism, we propose to adopt envelope detection mechanism as shown in this figure. When an averaged envelope level of received signals gets over the threshold level (TBD), the CCA detector detects that the medium is busy.

## Slide 25
CCA Performance
Notes: A CCA detection error rate with 4-symbol averaging is described in this figure. In the figure, the real and the dotted lines show the detection errors, which means that
a receiver detects that the medium is not busy though a packet has been transmitted (miss detection) and
  a receiver detects that the medium is busy though a packet has not been transmitted (false detection)
respectively. Threshold level is defined as a relative value of Gaussian noise lebel. From the figure, the proposed method achieve both of the detection errors less than 10% when signal-to-noise ratio (SNR) is 5 dB and threshold is 16dB.

## Slide 26
Channel Plan for U-NII band
Channel Separation = 18.75MHz
Notes: This table shows a channelization plan for U-NII band. 14 channels are proposed.

## Slide 27
TX Amplifier Characteristic
3dB Backoff
Notes: In order to decide channel plans, it is assumed to use a non-linear amplifier shown in this figure with 3dB backoff.

## Slide 28
Channel Allocation in 5.15-5.25GHz band
Notes: This figure shows a channel allocation plan for 5.15-5.25 GHz band. FCC 97-5 describes that all emissions within the frequency range 5.14-5.15 GHz and 5.35-5.36 GHz must be attenuated by a factor of at least 27dB; within the frequency range outside these bands by a factor of at least 37dB.

## Slide 29
Channel Allocation in 5.25-5.35GHz band
Notes: This figure shows a channel allocation plan for 5.25-5.35 GHz band. FCC 97-5 describes that all emissions within the frequency range from the band edge to 10MHz above or below the band edge must be attenuated by a factor of at least 34dB; for frequencies 10MHz or greater above or below the band edge by a factor of at least 44dB.

## Slide 30
Channel Allocation in 5.725-5.825GHz band
Notes: This figure shows a channel allocation plan for 5.725-5.825 GHz band. FCC 97-5 describes that all emissions within the frequency range from the band edge to 10MHz above or below the band edge must be attenuated by a factor of at least 40dB; for frequencies 10MHz or greater above or below the band edge by a factor of a factor of at least 50dB.

## Slide 31
Critical Points
Based on performances demonstrated here,
we will point out relative critical points for the proposed method.

## Slide 32
Intelectual Property
Several patents are under reviewing now.