## Slide 1
2.4 GHz High Rate PHY
Harris Submission
Brief

## Slide 2
Introduction
Harris proposes the MBOK waveform previously described in 97-144.
The waveform has been implemented in silicon and extensively tested.
Complexity can be traded for performance

## Slide 3
BASIC SYSTEM
1,2,5.5,11 MBPS
- 87 dBm (typ.) RX SENSITIVITY
20-30ns DELAY SPREAD
(HOME, OFFICE)
LOW COMPLEXITY
  LIMITING IF
  NO EQUALIZER
BASIC SYSTEM WITH
FIR EQUALIZER
1,2,5.5,11 MBPS
- 87 dBm (typ.) RX SENSITIVITY
30- 100 ns DELAY SPREAD
( WAREHOUSE)
MODERATE COMPLEXITY
  LINEAR IF
  FIR EQUALIZER (3-10 TAPS)
BASIC SYSTEM WITH
MLSE
1,2,5.5,11 MBPS
- 87 dBm (typ.) RX SENSITIVITY
100-200 ns DELAY SPREAD
( INDUSTRIAL)
HIGHER COMPLEXITY
  LINEAR IF
  VITERBI MLSE
ADDITIONAL SUB- OPTIONS
(ANY COMBINATION OF THE FOLLOWING:)
DIVERSITY
LOW RATE PHY PREAMBLE (120 us)
( INTEROPERABILITY WITH LOW RATE IEEE802.11 DS PHY)
HIGH RATE PHY PREAMBLE ( 26 us)
SYSTEM ARCHITECTURE OPTIONS
(I)
(II)
(III)

## Slide 4
11 Bit Barker Word
56
59
65
6A
03
0C
30
3f
8-ary modified Walsh Functions
22 MHz
11 MBps
QMBOK
5.5 MBps
BMBOK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS BPSK
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit encoded to
2 code words
11 chips
1 MSps
2 bits encoded to
4 code words
8 chips
1.375 MSps
4 bits encoded to
16 code words
8 bits encoded to
2x16 code words
8 chips
1.375 MSps
I
Q
I,Q
I
Q
I,Q
Modulation Scheme
Notes: The Harris suggested high rate modulation is a form of M-ary Bi-Orthogonal keying. We propose that both Binary and Quadrature forms of this modulation be used to provide multiple rates for stressed links.

## Slide 5
Pick One
of 8 Walsh
Functions
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
1
MBOK Modulation Approach for 11 MBps
Notes: This slide shows how to form our suggested modulation type. M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal vectors by the data word. Since the I and Q channels can be considered independent when coherently processed, both can be modulated this way. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 6
HFA 3860 DEMODULATOR BLOCK DIAGRAM
CORRELATOR
MAGNITUDE
ADC
CORRELATOR
SUB RATE
SAMPLE
ADC
Iin
Qin
CCA
PSK DEMOD
AVERAGE
PHASE
ERROR
LEAD/LAG
FILTER
NCO
ABS
DIF DECODE
COMPLEX
MULTIPLY
SIN/COS
ROM
SYMBOL
DECISION
DECISION
DIRECTED
PHASE DET
DATA
DESCRAM-
BLER
8
INTEGRATE
& DUMP
32 PHASES
PHASE
DET
SYMBOL
TIMING
SQ1
SQ2
DATA
RSSI
ADC
CCA
SIGN
CORRECT
PISO
DUAL
WALSH CORRELATOR
BANKS
SHADED BLOCK ARE THE ADDITIONS FOR HIGH RATES
SUM
ED
NCO
LEAD/LAG
FILTER

## Slide 7
Implementation Complexity
Uses same RF and IF as existing 802.11 DS PHY
Has moderate impact on baseband processor complexity. About 25% extra circuitry for a fully backwards compatible version
Equalized version replaces the IF limiter with AGC and has more A/D converter bits. It also has about 100% more baseband processor circuitry, which is a 15% increase in radio complexity.

## Slide 8
FCC Issues
An issue has been raised as to the technique’s ability to achieve FCC acceptance
The FCC’s CW Jammer and several alternative jamming margin tests have been successfully passed at an independent testing lab.
FH jamming is essentially the same as CW as shown on the following slide
The FCC is presently evaluating the hardware in their lab.
An option exists to use OQPSK for the modulation which would make the spreading 16 chips per symbol

## Slide 9
CW Jammer test data
Data shows that the performance is virtually identical with FSK and CW Jamming
The 20% discard
point is 10.3 dB
Note: channel 1
data is better

## Slide 10
WB Noise Jamming Margin
Note: Processing Gain is measured at the 1.0e-5 BER point
S/J is measured in spread rate bandwidth
PG = 16.6 + 2 - S/J = 10.9dB

## Slide 11
Optional Architectures
There is a need for a higher delay spread tolerance than any of the proposed waveforms can supply in their basic form.
  A reasonable equalizer architecture has been identified that will allow 100 ns delay spread
  A new diversity algorithm and decision metric measurement technique has been identified.

## Slide 12
4x
3x
2x
1x
802.11 11Mbps 11Mbps 11Mbps
1-2Mbps No Eq. Eq 100nsec Eq 200nsec
Implementation Penalty Vs (Multipath)Delay Spread Mitigation
Implementation
Penalty
Notes: This waveform can work without the need for a channel estimator or equalizer for those channels such as office buildings and homes where the delay spread is small. This makes for the lowest cost implementation.
Where improved performance or longer delay spread is needed, a simple channel estimator and cross sub channel interference suppressor can be added with a nominal increase in baseband processing cost.
When robust performance is needed, a complex channel corrector capability can be added without changing the basic radiated waveform or preamble.
The benefits of a good high rate waveform are an increased longevity in the marketplace and no obsolescence of the early entries. By making the units interoperable, they can be introduced seamlessly into the market. Keeping the channel distortion correction in the receiver allows the system designer to choose only the degree of performance needed for the job.
.

## Slide 13
Performance Analysis
A reference radio using the new Harris waveform has been constructed and tested
The testing shows that the simulated results for multipath are accurate. They show about a 30-50 ns delay spread capability which agrees with the simulation results presented in November.
Analysis shows that 100 to 200 ns can be achieved with various degrees of equalizer complexity

## Slide 14
Equalizer Options
An equalizer using 5 taps can improve the multipath performance of the basic design to 75 ns at 10 % PER.
The zero forcing equalizer structure needs 2 complex adds per feedforward tap and two complex multiplies per feedback tap.
The gate count for a design that meets 20 % PER at 100 ns with 2 FF and 6 FB taps is 35 K gates

## Slide 15
Moderate Multipath Options

## Slide 16
Severe Multipath Performance

## Slide 17
Equalizer Options

## Slide 18
Diversity Options
Antenna diversity can improve the performance of the link more cheaply than an equalizer
A good metric is a necessity for making the diversity decision
The metric should include quadrature channel information that is missing in the BPSK preamble
One way to get the information is to include a high rate training burst between the header and the high rate data to get the best metric

## Slide 19
Receiver Sensitivity
Data from two different radio units at two data rates

## Slide 20
Transmit Spectrum with Backoff
Shows effects of reduced PA Backoff. The amplifiers have been adjusted to 1, 2, and 3 dB of overdrive
A conclusion is that the Backoff is not an especially sensitive parameter for spectral containment

## Slide 21
Co Channel Interference, DS
The ability of the modulation to tolerate other networks in the area was tested. The results for S/J in dB that causes 5% PER are:
This indicates that the worst case Jammer for 11 MBps is the 1 MBps waveform that spoofs the preamble.
Notes: The ability of the signal to take jamming by a like signal will impact the ability to collocate nets. This set of data shows how the system will tolerate other DS signals of the various rates.
From the data we can see that the 1 Mbps radio is little effected by the higher rates since they are non correlating. On the other hand, the 1 Mbps radio jams the preamble of all the higher rates better than any other.

## Slide 22
Co-Channel Interference, FH

## Slide 23
Co-Channel Interference, FH

## Slide 24
Adjacent Channel Interference
This performance is slightly worse than the performance of a radio designed to the 802.11 standard due to the ~6 dB higher required operating SNR.
The adjacent channel performance is strongly dependent on the RF and IF components in the transmitter and receiver

## Slide 25
Interoperability
Our basic approach is to include the standard 802.11 preamble and header
For the cases where interoperability is not an issue, short, high rate headers can be used.
Antenna diversity and equalization require a somewhat longer short header than the shortest possible.

## Slide 26
Variations in the Waveform
There are variations to the chosen sequences for better multipath performance. The performance gains are slight, however.
It has been suggested that the FCC might accept that the same waveform but using offset QPSK is 16 chips per symbol (22 MCps spread rate).
If the 8 chips per symbol is an insurmountable problem, higher numbers of chips per symbol can be considered at some compromise in the data rate or spread rate, i. e. 10 MBps at 13.75 MCps with 11 c/b. This is a last resort option.

## Slide 27
BASIC SYSTEM
1,2,5.5,11 MBPS
- 87 dBm (typ.) RX SENSITIVITY
20-30ns DELAY SPREAD
(HOME, OFFICE)
LOW COMPLEXITY
  LIMITING IF
  NO EQUALIZER
BASIC SYSTEM WITH
FIR EQUALIZER
1,2,5.5,11 MBPS
- 87 dBm (typ.) RX SENSITIVITY
30- 100 ns DELAY SPREAD
( WAREHOUSE)
MODERATE COMPLEXITY
  LINEAR IF
  FIR EQUALIZER (3-10 TAPS)
BASIC SYSTEM WITH
MLSE
1,2,5.5,11 MBPS
- 87 dBm (typ.) RX SENSITIVITY
100-200 ns DELAY SPREAD
( INDUSTRIAL)
HIGHER COMPLEXITY
  LINEAR IF
  VITERBI MLSE
ADDITIONAL SUB- OPTIONS
(ANY COMBINATION OF THE FOLLOWING:)
DIVERSITY
LOW RATE PHY PREAMBLE (120 us)
( INTEROPERABILITY WITH LOW RATE IEEE802.11 DS PHY)
HIGH RATE PHY PREAMBLE ( 26 us)
SYSTEM ARCHITECTURE OPTIONS
(I)
(II)
(III)