## Slide 1
Submission
Page 1
OKANOUE,KAKURA,OHSAWA, NEC corp.
Comparison DATA of QPSK modulation February, 1998 Kazuhiro OKANOUE, Yoshikazu KAKURA, Tomoki OHSAWA NEC Corporation 4-1-1, Miyazaki, Miyamae-ku, Kawasaki, 216-8555, JAPAN Tel: +81 44 856 2255 Fax: +81 44 856 2230 E-mail:{okanoue,kakura,ohsawa}@ccm.CL.nec.co.jp
IEEE P802.11
Wireless LANs
Notes: Abstract

## Slide 2
Submission
Page 2
OKANOUE,KAKURA,OHSAWA, NEC corp.
General Description

## Slide 3
Submission
Page 3
OKANOUE,KAKURA,OHSAWA, NEC corp.
Per-Rate Feature Summary

## Slide 4
Submission
Page 4
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in AWGN channel

## Slide 5
Submission
Page 5
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in Fading with Gaussian Noise (64byte-packet) (Simple Implementation)

## Slide 6
Submission
Page 6
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in Fading with Gaussian Noise (1kbyte-packet) (Simple Implementation)

## Slide 7
Submission
Page 7
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER versus TRMS (64byte-Packet) (Simple Implementation)

## Slide 8
Submission
Page 8
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER versus TRMS (1kbyte-Packet) (Simple Implementation)

## Slide 9
Submission
Page 9
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in Fading with Gaussian Noise without FEC (64byte-packet) (Complex Implementation)

## Slide 10
Submission
Page 10
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in Fading with Gaussian Noise with FEC (64byte-packet) (Complex Implementation)

## Slide 11
Submission
Page 11
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in Fading with Gaussian Noise without FEC (1kbyte-packet) (Complex Implementation)

## Slide 12
Submission
Page 12
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER in Fading with Gaussian Noise with FEC (1kbyte-packet) (Complex Implementation)

## Slide 13
Submission
Page 13
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER versus TRMS (64byte-Packet) (Complex Implementation)

## Slide 14
Submission
Page 14
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER versus TRMS (1kbyte-Packet) (Complex Implementation)

## Slide 15
Submission
Page 15
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER versus Frequency offset (AWGN)

## Slide 16
Submission
Page 16
OKANOUE,KAKURA,OHSAWA, NEC corp.
PER versus Frequency offset (Fading+G-Noise)

## Slide 17
Submission
Page 17
OKANOUE,KAKURA,OHSAWA, NEC corp.
Per-Rate Performance Summary (Simple Implementation)

## Slide 18
Submission
Page 18
OKANOUE,KAKURA,OHSAWA, NEC corp.
Per-Rate Performance Summary (Complex Implementation)

## Slide 19
Timing and Overhead related Summary
Submission
Page 19
OKANOUE,KAKURA,OHSAWA, NEC corp.

## Slide 20
Submission
Page 20
OKANOUE,KAKURA,OHSAWA, NEC corp.
Receiver Structure (1) -Basic structure-

## Slide 21
Submission
Page 21
OKANOUE,KAKURA,OHSAWA, NEC corp.
Receiver Structure (2) -Example of Anti-Multipath scheme -
Symbol-by-Symbol detection based on Maximum Likelihood Sequence Estimation during Channel Impulse Response duration
Low calculation amount by using decision results
Past Metric Addition MLSCE (PMA-MLSCE)

## Slide 22
Submission
Page 22
OKANOUE,KAKURA,OHSAWA, NEC corp.
Receiver Structure (3) -State Transition of PMA-MLSCE -
s(i): symbol candidate
D(i-k): Decision result at t=i-k
r(i): received signal at t=i
Example for channel impulse response(h) of length 3 and binary symbol
t=i
t=i-1
t=i-2
(s(i),D(i-1),D(i-2))
(s(i-1),s(i),D(i-1))
(s(i-2),s(i-1),s(i))
(0,D(i-1),D(i-2))
(1,D(i-1),D(i-2))
(0,0,D(i-1))
(0,1,D(i-1))
(1,0,D(i-1))
(1,1,D(i-1))
(0,0,0)
(0,0,1)
(0,1,0)
(0,1,1)
(1,0,0)
(1,0,1)
(1,1,0)
(1,1,1)
state
S(t)
|r(i-2)-S(i-2)h|
|r(i-1)-S(i-1)h|
|r(i)-S(i)h|
+
+
Minimum
Detection
Possible
transition
Possible
transition
2-1 PMA-MLSCE
Notes: This figure shows an example of state transition for the 3tap PMA-MLSCE to estimate s(i) transmitted symbol at t=i. It is assumed that a transmitted symbol is binary, the length of a channel impulse response is 3 and the current time is i.
In this example, the PMA-MLSCE defines three state vectors S(t) for t=i, i-1 and i-2 which are consisted from symbol candidates s(i)’s and/or decision results D(i)s. Because D(i)s are deterministic, each state vector can take only 2m values where m is the number of symbol candidates in a vector. Then transitions between the state vectors can be defined as shown in the figure.
The PMA-MLSCE calculates metric, |r(i-k)-S(i-k)h| for all possible state vector values. The calculated metric are summed up along the transitions as a combined metric. The PMA-MLSCE selects a transition which presents the minimum combined metric and outputs the s(i) in the transition as a estimated results.
In order to reduce complexity of implementation, it is possible for the PMA-MLSCE to implement the part surrounded by the dotted line. In this case, the PMA-MLSCE uses two candidate symbols and one decision result to detect s(i). We denote the reduced PMA-MLSCE as n-m PMA-MLSCE, where n and m are tap number fed candidate symbols and decision results, respectively. Based on the notation, the part surrounded by the dotted line can be expressed as 2-1 PMA-MLSCE. The implementation of 2-1 PMA-MLSCE for QPSK is demonstrated in the next slide.

## Slide 23
Submission
Page 23
OKANOUE,KAKURA,OHSAWA, NEC corp.
Receiver Structure(4) - 2-1 PMA-MLSCE-

## Slide 24
Submission
Page 24
OKANOUE,KAKURA,OHSAWA, NEC corp.
Receiver Structure(5) - AFC -
1
2
N
K
1
2
N
K
1/(KN)
DqAFC:phase difference per symbol
Df1...DfN:phase offset during K symbols
Df2
Df1
DfN
DqAFC
S
K symbols
K symbols
the same sequence
Notes: This figure shows an example of AFC structure.
As long as a multipath fading channel is time invariant, received signals produced by the same two sequences are identical. Therefore, by comparing a phase difference between corresponding symbols, frequency offset can be estimated. In order to remove fluctuations caused by Gaussian noise, the phase difference need to be averaged over several symbols.

## Slide 25
Submission
Page 25
OKANOUE,KAKURA,OHSAWA, NEC corp.
Receiver Structure(6) - PLL -
PMA-MLSCE
decision
phase detector
r(i)-S h
Dfi
error signal
DqPLL
PLL
a
T
b
T
a:PLL factor
b:NCO factor
DqAFC
Dq
Notes: This figure shows an example of PLL structure.
A PMA-MLSCE calculates replica of received signals, Sh. Using a phase of an error signal between received signal r(i) and the replica, 2th order PLL tracking phase variations in a packet.

## Slide 26
Submission
Page 26
OKANOUE,KAKURA,OHSAWA, NEC corp.
Preamble Structure
SEQ64=(X0Y0X1Y1…X30Y30X31Y31)
=(0xFF 0xF0 0xF3 0x30 0xC0 0x0F 0x0C 0xC0)
Notes: This figure shows a proposed frame format. The PLCP Preamble consists of 124 symbols in a SYNC field and 8 symbols in a SFD (Start Frame Delimiter) field. The PLCP header includes both a 8-symbol header error check filed and a 6-symbol PSDU length word. The rest 2 symbols in the PLCP header are used for PLCP control information.
The SYNC filed is basically formed as a repetition of the 64-bit sequence, SEQ64. The SEQ64 can be represented based on the Xk and Yk, as follows;
SEQ64=(X0Y0X1Y1 X2Y2X3Y3 … X30Y30X31Y32)
=(1111 1111 1111 0000 1111 0011 0011 0000 1100 0000 0000 1111 0000 1100 1100 0000).
This figure also shows a structure of SYNC field. A receiver executes antenna selection, AGC (Automatic Gain Control) setup, AFC (Automatic Frequency Control) setup and channel impulse response estimation through the SYNC filed.

## Slide 27
Submission
Page 27
OKANOUE,KAKURA,OHSAWA, NEC corp.
Channel Impulse response Estimation
SEQ64
SEQ64*
~
~
head n-bit
of SEQ64
0
1
n
-m
1
0
0
0
0
0
0
t
...
...
correlator
~
SEQ64*
SEQ64*
last m-bit
of SEQ64
SEQ64=(X0Y0X1Y1…X30Y30X31Y31)
=(0xFF 0xF0 0xF3 0x30 0xC0 0x0F 0x0C 0xC0)
32 symbols
-1
Notes: This figure shows an example of a channel impulse response estimator. By using a preamble sequence of which correlation function becomes impulse, a channel impulse response can be obtained by calculating correlation between a received preamble and the preamble sequence itself.
We propose to use the SEQ64 for a preamble. The correlation function of the SEQ64 is presented at next page.

## Slide 28
Submission
Page 28
OKANOUE,KAKURA,OHSAWA, NEC corp.
Correlation function of SEQ64
Notes: This figure shows a correlation function of the SEQ64. It is shown that the correlation function becomes a impulse during 26 symbols.
We will present a receiver performance with the PMA-MLSCE and the channel impulse response estimator.

## Slide 29
Submission
Page 29
OKANOUE,KAKURA,OHSAWA, NEC corp.
SlotTime and SIFSTime
SlotTime=CCATime+RxTxTurnaroundTime+AirPropagationTime+MACProcessingTime
SIFSTime=RxRFDelay+RxPLCPDelay+MACProcessingDelay+RxTxTurnaroundTime
SlotTime=8.9usec
SIFSTime=7.4usec

## Slide 30
Submission
Page 30
OKANOUE,KAKURA,OHSAWA, NEC corp.
CCA mechanism
Notes: As a CCA detection mechanism, we propose to adopt envelope detection mechanism as shown in this figure. When an averaged envelope level of received signals gets over the threshold level (-78dbm), the CCA detector detects that the medium is busy.

## Slide 31
Submission
Page 31
OKANOUE,KAKURA,OHSAWA, NEC corp.
CCA Detection Performance

## Slide 32
Submission
Page 32
OKANOUE,KAKURA,OHSAWA, NEC corp.
Channel Allocation in 5.15-5.25GHz band

## Slide 33
Submission
Page 33
OKANOUE,KAKURA,OHSAWA, NEC corp.
Channel Allocation in 5.25-5.35GHz band

## Slide 34
Submission
Page 34
OKANOUE,KAKURA,OHSAWA, NEC corp.
Channel Allocation in 5.725-5.825GHz band

## Slide 35
Appendix: PER versus Phase noise
Submission
Page 35
OKANOUE,KAKURA,OHSAWA, NEC corp.

## Slide 36
Submission
Page 36
OKANOUE,KAKURA,OHSAWA, NEC corp.
Appendix: PER v.s. Narrow-band Noise

## Slide 37
Submission
Page 37
OKANOUE,KAKURA,OHSAWA, NEC corp.
Appendix: PER v.s. CW-jamming

## Slide 38
Submission
Page 38
OKANOUE,KAKURA,OHSAWA, NEC corp.
Appendix: PER v.s. Alternate Channel

## Slide 39
Submission
Page 39
OKANOUE,KAKURA,OHSAWA, NEC corp.
Appendix: PER v.s. Adjacent Channel

## Slide 40
Submission
Page 40
OKANOUE,KAKURA,OHSAWA, NEC corp.
Appendix: PER v.s. Co-Channel