## Slide 1
Wireless Solutions
Continuum of needs for wireless products
No one product which can fill all needs
Family of complementary devices
RFID
PAN
WLANs
Low performance,
low cost
High performance,
higher cost

## Slide 2
Targeted Applications
Cable replacement (point to point)
  Barcode scanner to portable/mobile computer
  Printer to portable/mobile computer
Personal area connectivity (peer to peer)
  hand held computer to numerous peripheral devices including scanners, printers, wide area network radios, etc.
PEN*KEY 6500
Picking Application
Scan Item 000123456
Description: Tide Liq., 50oz.
Scan Location: BAY 31
Enter Quantity: 40
Take to Location: Dock 5A
Keyboard
Keypad
Help
Exit

## Slide 3
Applications Solution Requirements
Very low cost
Low power consumption
Small size
Interference immunity
Ease of use
Standardized interfaces
Unlicensed, international usability

## Slide 4
Wire Replacement Concept
Complementary to WLAN/IEEE 802.11 devices
  lower range
  lower throughput
Lower complexity than WLAN devices
  reduced RF specifications
  reduced MAC/PHY complexity
Features which do not add recurring costs
  peer to peer with up to 10 nodes per PAN

## Slide 5
Short Range Radio System Sample Configurations
Personal
Area
Network
Infrastructured
Network
Access Point
PC Based Work Station
Barcode and Receipt Printers
WAN Radio
Scanner
Pen-based HHC
Ethernet

## Slide 6
Personal
Area
Network
Personal Area Network (PAN; Peer-to-Peer)
  Multiple Networks co-habitate (20 or more)
  Up to 10 devices in a single PAN
  Dynamic PAN and device IDs with network initiation
  Network maintained devices coming and going
  Temporary devices also supported
PC Based Work Station
Barcode and Receipt Printers
WAN Radio
Scanner
Pen-based HHC
Short Range Radio System Configurations

## Slide 7
Limited Infrastructured
Network
Limited Infrastructured Network
  Main device (access point) has power at all times (fast access)
  Support for more than 10 devices
  Ethernet access points with higher layer protocol
  Communications to the NT Base (STAR Base)
  Switch from PAN to LAN and back
Short Range Radio System Configurations
Access Point
Ethernet

## Slide 8
Short Range Radio System Desirable Features
Interface
  Simple interface for intelligent and “dumb” devices
  Dumb devices
    Serial, RS232 like interface (19.2kbps)
  Intelligent devices (Ability to establish and control net parameters)
    Serial, RS232 like interface (up to 115.2kbps)
    Parallel/ PC Card optional
Very Low Power Consumption
  Minimized while not operating (e.g. 6mA or less)
  Operational, fast, low power comm. (e.g. 80mA or less)
  Very low full day average (e.g. 10mA avg. over 10 hours)
Fast Response (Variable Speeds)
  “Wired Response” (e.g. avg. response time under 125mS)
  Various speeds for optimum response/range/current
  CSMA/CA; collision sense/collision avoidance

## Slide 9
Short Range Radio System Desirable Features
Immunity
  Frequency Hopping to avoid fixed interferers and multipath interference
  Able to coexist with other frequency hopping systems
  Reduced range decreases the impact of co-located networks
  High data rate reduces “air time”
Size
  Under 1/3rd the volume of typical 802.11 radios
Cost
  In mass production, should be under 25% of the projected cost of an 802.11 radio

## Slide 10
Non-licensed, ISM bands
World Wide Regulatory
  2.4GHz frequency hopping: ETSI 300 328
  Low power output: FCC Part 15.249
  Japan: RCR 33
Short Range Radio System Desirable Features