## Slide 1
PAN Feasibility: The BodyLANTM Experience
GTE Internetworking - BBN Technologies
733 Concord Avenue Cambridge, MA 02138
Rick LaRowe (rlarowe@bbn.com)
I N T E R N E T W O R K I N G
POWERED BY BBN

## Slide 2
Personal Area Networks
Driving requirements include:
Very low power consumption
Very small devices (including peripherals, sensors, etc.)
Easy integration into devices (minimal SW)
Cross-network interference tolerance
Very low cost
Simplifying characteristics include:
Data rate requirement is relatively low
Range is short (2-10 meters)

## Slide 3
BodyLAN Topology
For simplicity, a STAR topology is employed.
The Hub is at the center and runs the show.
Around the edge are Personal Electronic Accessories (PEAs)
HUB
PEA
PEA
PEA
PEA
PEA

## Slide 4
Key Characteristics
Simple TDMA structure:
Cross-network interference:
  CDMA-like burst spacing using Optical Orthogonal Coding
  Frequency agility
T
O
K
E
N
B
E
A
C
O
N
PDU
DATA
H
E
A
D
E
R
C
R
C
A
C
K
S
T
A
T
R
E
S
P

## Slide 5
Other Key Attributes
PAN requirements demand only small networks; 7-bit MAC address is sufficient.
Dynamic device attachment supported via a form of slotted Aloha layered on top of the TDMA structure.
Ad Hoc networking easily supported: any device can function as a Hub.
Prioritorized bandwidth allocation is easily achieved via Hub token allocation mechanism. (Partly demand-driven via Status Response messages from PEAs.)
Design readily enables single-chip Data-Link and MAC implementation.

## Slide 6
Proof-of-Concept Demo
Demonstrated with two real applications in early 1998.
Basic structure:
PowerPC (PPC) runs the device driver and protocol stack. (PPC selected since needed to run Inertial Navigation code used by a demonstration sensor PEA.)
Digital board contains an Altera PLD with MAC layer implementation and debug logic.
RF transceiver a small discrete implementation.
BodyLAN
Digital
Control
BodyLAN
RF
Transceiver
PPC 403
Host
Processor
PC, HPC,
or
Sensor
RS-232

## Slide 7
Host Processor & Digital PLD

## Slide 8
Characteristics of POC Demo
Fully operational, with good performance
Dynamic attachment / detachment works
Dynamic bandwidth allocation over TDMA structure
100mA with PowerPC @ 25MHz Transceiver draws 10mA when running (xmit/recv) PLD draws about 15mA (ASIC est. @ 500mA) (lots of debug and test support, no board-level optimization)
Range adjusted to about 2m, have run up to about 5m

## Slide 9
The End
Any Questions?