## Slide 1
2.4 GHz QMBOK High Rate PHY
Harris Submissions
for Comparison Matrix
Notes: This is a revision of the Harris proposal to take into account additional information that has been developed since the March meeting.

## Slide 2
Suggested Technical Approach
Utilize MOK/PSK modulation techniques to realize 4 to 8 bits/symbol
Use existing preamble and header to insure interoperability.
Increase symbol rate to 1.375 MSps (8 chip symbols) and hold existing spread rate
Use existing 802.11 DS parts for the RF & IF circuits
Notes: The high rate scheme chosen will not impact the design of the RF and IF parts currently employed. This means a small redesign effort and the ability to drop in a new baseband processor into existing radios to get the higher rates.
The new scheme requires an absolute phase reference. The PLCP preamble is BPSK and as such, will provide a 180 degree phase ambiguity. By using the last bit out of the modulator prior to the PDU as a phase reference, we can establish an absolute phase reference.

## Slide 3
11 Bit Barker Word
56
59
65
6A
03
0C
30
3f
8-ary modified Walsh Functions
22 MHz
11 MBps
QMBOK
5.5 MBps
BMBOK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS BPSK
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit encoded to
2 code words
11 chips
1 MSps
2 bits encoded to
4 code words
8 chips
1.375 MSps
4 bits encoded to
16 code words
8 bits encoded to
2x16 code words
8 chips
1.375 MSps
I
Q
I, Q
I
Q
I, Q
Modulation Technique and data rates
Notes: The Harris suggested high rate modulation is a form of M-ary Bi-Orthogonal keying. We propose that both Binary and Quadrature forms of this modulation be used to provide multiple rates for stressed links. This modulation is textbook and will have no patent issues.

## Slide 4
Pick One
of 8 Walsh
Functions
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
1
QMBOK Modulator Technique for 11 MBps
Notes: This slide shows how to form our suggested modulation type. M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal vectors by the data word. Since the I and Q channels can be considered independent when coherently processed, both can be modulated this way. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 5
Receiver Sensitivity
Data from two different radio units at two data rates
Notes: The sensitivity of two typical real radios was tested and the results shown here. The sensitivity is in line with expected results and shows that the MBOK waveform performs well in thermal noise.

## Slide 6
Reference Submissions
70254 IEEE 802.11 High data rate PHY extensions
70867 Suggested 802.11 High Rate PHY Technique
71447 Proposed 802.11 High Rate PHY Technique
80377 Multipath Issues & Architectures
80467B Harris 2.4 GHz short proposal
80477B Harris 2.4 GHz full Proposal
80557 Empirical Benchmarks
80567 Implementation for High Speed PHY
81157 Sliding DFE for Equalizing QMBOK
81167 Harris 2.4 GHz selection criterion
81347 Harris draft Text
81427 Harris IP Statement
Notes: The Harris technique has been discussed since early in 1997. Harris has also implemented the technique in silicon and thoroughly tested it.

## Slide 7
RF/IF Complexity relative to current low rate PHY
Basically uses same RF and IF as existing 802.11 DS PHY
Equalized version replaces the IF limiter with AGC and has more A/D converter bits.
A combined DS/FH mode uses non optimal wideband IF filters with some loss of FH performance in a crowded environment
Notes: The use of the same RF bandwidth makes the design of the radio more or less the same as the existing low rate PHY. The main change is that to get more delay spread capability, the receiver may be enhanced by equalization and that generally is best performed in a linear receiver. That requires an AGC type of receiver rather than a limiting receiver and more bits of ADC conversion. We expect that 5 or 6 bits of accuracy is needed in the ADC section.

## Slide 8
Receiver Structure Description
HFA3624
RF/IF
I/Q LO
I ADC
Q ADC
De-
Spread
De
Rotate
De-
Modulate
Spread,
Rotate
Modulate/
Encode
TX/Rcv
Data I/O
Control
Test I/O
AGC
CCA
Quadrature Modulator
Quadrature Demod
5th Order
Butter-
Worth
Low-Pass
Filters
FH/DS Baseband Processor
Qmodem with AGC
HFA3524 Dual Synthesizer
FLASH EEPROM
RAM
MAC
SYSTEM
INTERFACE
MAC
PROCESSOR
CORE
PHYSICAL
LAYER
PROCESSING
MEMORY
SUBSYSTEM
HFA3925
RF Power
Amp. and Tx/Rx Switch
HFA3424 LNA
VCO
VCO
OSC
44MHz
SW
MAC
SUPPORT
FUNCTIONS
Notes: The overall look of the reference radio design for the new high rates is like the existing and proven PRISM design except for the new baseband processor and MAC.

## Slide 9
Baseband Processing Complexity relative to current low rate PHYs
Addition of high rate without equalizer increases the DS only baseband processor complexity from 23K gates to 33 K gates
Addition of equalizer to increase delay spread from 30 to 100 ns takes an additional 40 K gates
The addition of FH interoperable mode has not been fully worked out yet
Notes: The complexity of the existing design when stripped to the minimum to support the standard was found to be 23 K gates more or less. To add the high rate capability without the equalizer took 10 K more gates. The equalizer is projected to take an additional 40 K gates. Since many of these will be run at high rates, the power consumption must be carefully managed by selectively turning off sections not needed for the moment. The FH interopoerability mode will use more gates, but these will not be on when the DS sections are on and vice versa.

## Slide 10
DEMODULATOR BLOCK DIAGRAM
CORRELATOR
MAGNITUDE
ADC
CORRELATOR
SUB RATE
SAMPLE
ADC
Iin
Qin
CCA
PSK DEMOD
AVERAGE
PHASE
ERROR
LEAD/LAG
FILTER
NCO
ABS
DIF DECODE
COMPLEX
MULTIPLY
SIN/COS
ROM
SYMBOL
DECISION
DECISION
DIRECTED
PHASE DET
DATA
DESCRAM-
BLER
8
INTEGRATE
& DUMP
32 PHASES
PHASE
DET
SYMBOL
TIMING
SQ1
SQ2
DATA
AGC
AGC
CCA
SIGN
CORRECT
PISO
EQUALIZER AND DUAL
WALSH CORRELATOR
BANKS
SHADED BLOCK ARE THE ADDITIONS TO DS FOR FH AND HIGH RATES
SUM
ED
NCO
LEAD/LAG
FILTER
FH DEMOD
Notes: The added capability blends well with the existing circuitry that implements the existing standard.

## Slide 11
Antenna Diversity and performance impact
Antenna diversity can improve the performance of the link more simply than an equalizer but not as much
The performance impact has shown an improvement of a factor of 2 to 4 in PER in field testing
The negative impact is to require additional length in the preamble (already covered by the 802.11 preamble)
Notes: The improvements of antenna diversity depend on the ability of the selected decision metric to discriminate the good antenna. The improvement comes cheap, but is is not as much of an improvement as an equalizer can provide. We are investigating decision metrics such as the channel impulse response measurement which is necessary for training the equalizer.

## Slide 12
Graph of PER Vs. Thermal Noise (no Multipath).
Notes: The performance of the industry standard Root Raised Cosine filtering versus the filtering that Harris used is shown. This is to show the effects of the less than ideal, but very reproducible filtering on the waveform. We find that the loss due to filtering is much less than that due to multipath, so the emphasis must be placed on the channel distortion rather than that of the radio. For all of the following charts, we use the practical filtering in the simulations or empirical evaluations.

## Slide 13
PER Vs. Multipath Only (No Noise).
Notes: The use of 2 FF and 5 FB taps with the sliding decision feedback equalization is sufficient to insure that the system meets the desired 100 ns delay spread capability.

## Slide 14
PER Vs. Thermal Noise with Multipath at 10% PER. Eb/No at 20% PER for 64 and 1000 byte packets.
20%
Notes: The performance in both multipath and thermal noise shows that the system is capable of good performance. At 20 % PER, the Eb/N0 is 18 dB for 64 Byte packets and 24 dB for 1K byte packets.

## Slide 15
FF
+
DEC
FB
AGC/
PLL
FAST WALSH
TRANSFORM
CHIP EQUALIZER
D
D
w2
w1
w3
w4
w-1
w5
D
D
D
w0
DEC
+
+
+
FEEDFORWARD
TAPS
FEEDBACK
TAPS
+/-1+/-j
DECISION FEEDBACK EQUALIZER
Notes: To illustrate the simplicity of the sliding DFE equalizer, we show how the tap parameters are calculated. First, the feedforeward taps are simplified by making one of them unity, allowing the scaling to be incorporated into the AGC/PLL multiplier.

## Slide 16
h-1
h0
h1
h2
h3
h4
h5
CHANNEL IMPULSE RESPONSE
h0 h-1
h1 h0
w-1
w0
0
1
=
w-1
w0
=
-h-1
h0
2 FF MATRIX EQUATION
SOLUTION
FEEDFORWARD WEIGHT CALCULATION
Notes: The channel impulse response is examined to find the earliest good impulse weight, and this is used for the calculation. Then the matrix for the taps is a simple two element equation where the results are the elements of the original data modified.

## Slide 17
FF
h
g
CHANNEL
IMPULSE
RESPONSE
CONVOLVE
FEEDBACK
IMPULSE
RESPONSE
h
g
g-1
g0
g1
g2
g3
g4
g5
w1
w2
w3
w4
w5
g1
g2
g3
g4
g5
=
FEEDBACK WEIGHT CALCULATION
Notes: Next, the FF solution is convolved in hardware with the original channel impulse response and the new CIR samples are the new tap weights for the FB section.

## Slide 18
Summary of Equalizer results
Notes: This chart shows the equalizer options that can be implemented to improve the receiver performance in the face of multipath. These show that the performance can be greatly improved at the cost of complexity. While this is of little concern for the system designer, it can impact power consumption and cost.

## Slide 19
Required Carrier Frequency Accuracy
The new high rate PHY requires the same carrier frequency accuracy as the existing low rate PHY or + 25 PPM.
The DS limitation is that the maximum carrier frequency offset should be less than 1/8 th of the symbol rate of the preamble.
Notes: The requirements on oscillator accuracy are the same as the existing standard. The 25 PPM oscillators are at a very good cost point versus more accurate oscillators. For example, 10 PPM oscillators can double in cost relative to 25 PPM.

## Slide 20
BER versus Carrier Offset Performance of HFA 3860
Notes: The PER curves show that the acquisition performance is adequate out to the maximum offset allowed. Once you get out to +100 PPM, the performance degrades substantially. This is because the carrier phase roll gets close to 90 degrees per symbol of the header. Exceeding 90 degrees per symbol makes the phase shift ambiguous and the modem can lock up on a sidelobe.

## Slide 21
Required Data Clock Frequency Accuracy
The new high rate PHY requires the same clock frequency accuracy as the existing low rate PHY or + 25 PPM.
The limitation is that the maximum data clock offset should drift no more than 1/8 th of a chip in 128 us.
Notes: The current standard uses 25 PPM as the clock tolerance. This technique does not require any greater tolerance than this. It is suggested that a simplification can be achieved if the carrier and data clocks are made synchronous. This would allow PN tracking to be divided from carrier tracking.

## Slide 22
BER versus Clock Offset Performance of HFA 3860
Notes: The performance of the Harris implementation is based on the performance of the symbol tracking loops. Our implementation has better tracking on the new high rate modes than on the existing modes. This is due to using 1/8th chip tracking on the high rate modulation and 1/4th chip tracking on the lower rate modulations.

## Slide 23
Preamble Length
Our DS interoperable approach is to include the standard DS or FH 802.11 preamble and header which includes ample time to do diversity and equalization.
For the cases where interoperability is not an issue, a short (52 us), high rate header is used.
For FH interoperability, a standard FH preamble and header is followed by the short high rate header.
Notes: The long, interoperable preamble and header allows ample time to do AGC, diversity selection, and equalizer training along with the normal modem acquisition processing. In the event a shorter preamble and header is desired for maximizing throughput, it must take into account those extra times.

## Slide 24
Short Acquisition
The preamble and header of the high rate waveforms will be received at a higher signal strength than the case with 1 and 2 Mbit/s, so the acquisition can be quicker. Starting point is 5.5 Mbit/s.
13.6 dB Es/N0 in sync detection allows Pd = .999 and Pfa = 10e-7 detection on 4 symbols. Use three for phase roll detection for frequency acquisition.
1 symbol is abused for switching and AGC settling
Use synchronous (FH) scrambler to avoid seeding time.
Send SFD @ 2 MBps to reduce duration by half
Send header @ 5.5 MBps and use 1 bit rate field to indicate high or low rate. Switch to 11MBps after header
Use length field expressed in 0.5 us increments (17 bits).
Notes: Shorter acquisition is greatly desired in order to minimize the overhead of the radio communications. The short acquisition has to take into account the SNR of the signal at the lowest data rate.

## Slide 25
DUAL ANTENNA ACQUISITION TIMELINE
TX signal
2
36 SYMBOL SYNC
Start
Frame
Delimiter
POOR
SIG
ANT1
AGC
Initial ACQ
SQ1
SQ2
Diversity
CIR
Tx
POWER
RAMP
ANTENNA DECISION (1)
JAM CARRIER FEQ
JAM SYMB TIMING
CORRELATOR DELAY (1)
DEMOD DELAY (1/2)
JAM CARRIER PHASE
DEMOD DELAY (1/2)
DIFF DECODER DELAY (1)
A2
HDR DET
Start HR
START 5.5
4 SYMBOLS
Measure
ANT1
GOOD
SIG
ANT2
AGC
4 SYMBOLS
4 SYMBOLS
4 SYMBOLS
4 SYMBOLS
4 SYMBOLS
4 SYMBOLS
A1
A2
A1
A2
A1
A2
A1
A2
TRY
SYMB
TIM
ANT1
SYMB
TIM
ANT2
4 SYMBOLS
VERIFY
ANT2
4 SYMBOLS
9 SYMBOLS
SFD DET
HEADER
5.5 MBps
8 SYMBOLS
TRY
SYMB
TIM
ANT1
36 + 8 + 7.3 = 51.3 us
START 2MB
Notes: This preamble is set for dual antenna acquisition with 5.5 MBps.

## Slide 26
HR preamble and header
SYNC
36BITS
SFD
16 BITS
LENGTH
17 BITS
SIGNAL
3 BITS
CRC
16 BITS
PLCP Preamble
52 BITS
PLCP Header
36 BITS
MPDU
PPDU
1 Mbit/s
2 Mbit/s
5.5 Mbit/s
5.5 or 11 Mbit/s
total overhead = 51.3 us
Notes: The total preamble and header length in bits must be factored by the bit rate of the specific section in order to get the total length in microseconds.

## Slide 27
Slot Times
We propose no change in the DS PHY slot time of 20 us or FH slot time of 50 us.
For the short header, we have allowed 4 microsecond antenna dwells which divide evenly into the 20 us slot times.
This allows ample time to detect the signal on both antennas for CCA purposes.

## Slide 28
Slot timing and CCA with 4 us dwells
T0
Start
of
Slot
T0+10
T0+20
TX
Decision
point
Transmission can start up to 5 us late
ANT A
ANT A
ANT A
ANT B
ANT B

## Slide 29
CCA mechanism and Co-Channel signal detection time
We measure the correlated signal energy in the preamble antenna dwells beginning when the receiver is enabled and compare that to a threshold
FH detection is done on clock energy in similar dwells.

## Slide 30
RX/TX turn around time and SIFS
The transmitter has a 1.3 us processing delay from bits in to bits out the antenna
The receiver has 3.3 us processing delay from bits in the antenna to bits out
The RX/TX turn around time is less than 2 us exclusive of the above delays.
We propose to use the existing 10 us DS SIFS or 28 us FH SIFS.

## Slide 31
HR Channelization Scheme
We propose the existing DS channelization scheme.
Three non overlapping channels spaced either 25 or 30 MHz in the band
A choice of 5 MHz channel centers with 11 channels in the ISM band for the US and 13 in Europe.

## Slide 32
Cell Planning With 3 Frequencies
6 far interferers
access point
interferer
desired user

## Slide 33
Adjacent Channel Interference Rejection
Only 8 dB more RX filter skirt rejection is needed to achieve the same ACI rejection as the existing low rate DS PHY
The increase is due to the higher required SNR in the spread bandwidth.

## Slide 34
802.11 spec

## Slide 35
MKK Requirements
The processing gain requirement for Japan is that the ratio of the 95% power bandwidth to the symbol rate be greater than 10:1
For rates over 8 MBps, this requires that the 95 % bandwidth be greater than that of the 1 and 2 MBps modes
  For example, the Harris approach at 11 MBps requires 13.75 MHz
Proper shaping of the baseband pulse shape can expand the power bandwidth sufficiently
See paper 98/203 for more details

## Slide 36
Bandwidth expansion by pulse shaping
Normal NRZ shaping
50 % RZ shaping
Root Raised Cosine shaping
95% Spread Factor = 9.3
95% Spread Factor = 10.6
95% Spread Factor = 10.5

## Slide 37
Spectrum Effects
The narrower pulse shape enhances the high frequency content of the waveform
The spread factor needs to be > 10.0 in order to meet the MKK requirements
The spread factor with Tc/2 pulse shape is 10.6 which is overkill, but proves the point.
To be investigated: 0.75Tc pulse shape, where width is adjusted to just pass the requirement, while being easy to implement.
This mode can be added to the basic waveform without changing its interoperability over the air
The Pulse shaping does add amplitude modulation, which is undesirable, but unavoidable.

## Slide 38
Co Channel Interference Rejection, DS
The ability of the modulation to tolerate other networks in the area was tested. The results are S/J in dB that causes 5% PER
This indicates that the worst case Jammer for 11 MBps is the 1 MBps waveform that spoofs the preamble.
Notes: The ability of the signal to take jamming by a like signal will impact the ability to collocate nets. This set of data shows how the system will tolerate other DS signals of the various rates.
From the data we can see that the 1 Mbps radio is little effected by the higher rates since they are non correlating. On the other hand, the 1 Mbps radio jams the preamble of all the higher rates better than any other.

## Slide 39
S/J where CW jammer gives 10% PER
Data shows that the performance is virtually identical with FSK and CW Jamming
The 20% discard
point is 10.3 dB
Note: channel 1
data is better

## Slide 40
Other Interference Immunity tests, WB Noise Jamming Margin
Note: Processing Gain is measured at the 1.0e-5 BER point
S/J is measured in spread rate bandwidth
PG. = 16.6 + 2 - S/J = 10.9dB

## Slide 41
Other Interference Immunity tests, FH

## Slide 42
Other Interference Immunity tests, FH

## Slide 43
Total Number of Channels in the ISM band
We propose the existing DS channelization scheme.
Three non overlapping channels spaced 25 or 30 MHz in the band
A choice of 5 MHz channel centers with 13 channels available. The highest two are not currently used by the existing standard in the US.

## Slide 44
Aggregate Throughput
The 3 non overlapping channels at 11 Mbps will allow 33 MHz total maximum achievable throughput in the ISM band.
Link probability tempers this…….

## Slide 45
Phase Noise Sensitivity
There is no particular phase noise sensitivity with the proposed waveform. It performs as well in phase noise as any QPSK scheme.
The measured phase noise of our receiver’s LO which performs well is 2 degrees RMS

## Slide 46
RF PA Backoff
The QMBOK waveform needs about 5 dB of PA backoff to insure low regrowth of spectral sidebands.
This is the same as the DS BPSK preamble requires.

## Slide 47
DC power consumption
The current, non equalized HFA 3860 QMBOK chip draws 30 mA at 3 VDC.
This represents about 12% of the radio receive power.
The equalizer will probably draw more than this.

## Slide 48
Power Consumption
Suggestions have been made to use more a constant amplitude modulation to save TX power
Some constant amplitude modulations make the equalizer more complex
If lower backoff in the PA saves 95 mA but costs 5 mA in the receiver the net savings is nil with a 5% TX duty cycle

## Slide 49
Patent Submissions
The Harris position is that we will only patent techniques having to do with our implementation.
Anything likely to be embodied in the standard will be free of license from Harris.
The QMBOK waveform is public domain.
Having a patent does not protect you from other patents which may cover the same or similar techniques.

## Slide 50
Interoperability / Co-existence strategy with current low rate PHYs
Interoperable via use of existing low rate preamble and header, either DS or FH
  In the case of the FH PHY, the low rate preamble and header must be followed by a short high rate header to re-establish antenna diversity and to train the equalizer
Will defer or cause deferral via 802.11 mechanisms currently in place.
Notes: While we originally only suggested a DS low rate interoperability, Symbol has suggested low rate FH techniques.

## Slide 51
Is the proposal Interoperable at the data and antenna levels?
Yes to both, the use of the existing preamble and header insures interoperability and the data format is not changed.

## Slide 52
Performance penalty due to Interoperability / Coexistence.
The DS overhead is 192 us Vs about 50 us without interoperability
The FH overhead is 128 + 10 + 50 us or about the same
This amounts to ~20 % on 1K byte packet
with short preamble it is 5%

## Slide 53
Performance penalty due to Interoperability / Coexistence.
Notes: It is desirable to use long packets to minimize the impact of the long preambles. Users concerned with maximizing throughput will also avoid the RTS/CTS/ACK protocol options.

## Slide 54
with 52 us preamble