## Slide 1
Proposal for 2.4-GHz PHY May 1998 Update
John H. Cafarella
MICRILOR, Inc.

## Slide 2
Key Features
32-Mchip/s Transmission Bandwidth
Low EB/N0
Nc=16
Changing Codes
16-ary DBOK
(C-4x4DBOK)
10-Mbps Data Rate
Good PN Codes
Intra-Symbol Multipath
Code Channelization
Inter-Symbol Multipath
MSK Spreading
Saturated PA
Spectral Confinement
Freq. Channelization
enabling
link
design
system
Low Acquisition Time
Low Preamble Overhead
Robust Links
BSAIsolation; Coexistence & Interoperability
High Throughput
12-dB Processing Gain
Low Battery Drain
Multipath Resolution
Multi-Signal CCA
Low Slot Time
Channel Matched Filter
Antenna Diversity
(18-Mbps Data Rate)
(15,13) FEC
Power-Efficiency

## Slide 3
Simplified Matrix
Interference Tolerance
Multipath Tolerance
Basic Data Rate
Chip Complexity
Amplifier Backoff
Weak
Less Weak
Strong
Good
Good
Weak
8 Mbps
11 Mbps
10 Mbps
60K gates
70K gates
40K gates
Yes
Yes
No
Lucent
Harris
Micrilor
Freq/Code Channels
2/48
3/1
3/1
Higher Rate (good channel)
10 Mbps
None
18 Mbps
Raytheon same as Harris except no Amplifier Backoff
Interoperate Legacy DSSS?
Optional*
Optional*
Yes
* must choose between high throughput or backward interoperability

## Slide 4
MSK operating point
PSK operating point
Power Amplifier Efficiency
(seems mundane, but does not improve with time)
MSK allows operation to power-amp 1-dB compression
PA efficiency greatly improves
D11-97/118 describes low-cost MSK implementation

## Slide 5
Interoperability
Dual-Mode transceiver (re-using circuitry)
  High-rate and Legacy DSSS PHY
  Independent Operation with common CCA
  Coordinate via RTS/CTS exchanges
Single PHY Solution
  No need for alternate PHY Headers
  Does not sacrifice high-rate potential

## Slide 6
Three-Channel Operation
Existing legacy channels
High-rate channel interoperating
ACI > 35 dB

## Slide 7
Migration Possibilities
Begin with 3 Legacy Channels
Introduce High-Rate Channel; Interoperate with Mid. Legacy Channel
Move Legacy Units from High-Rate Channel
Keep Three-Channel Deployment
or
Two High-Speed/Legacy Channels
Eventually Two High-Speed Channels

## Slide 8
Channelization
Many PN Code Channels
  Especially for BSA Isolation
Two 10-/18-Mbps Frequency Channels
Three Half-Bandwidth Channels if Desired

## Slide 9
Three-Frequency/One-Code Deployment
  Re-use of frequencies demands sharing capacity
Two-Frequency/Many-Code Deployment
  Re-use of frequencies can be shared or independent
BSA Isolation Critical for High System Capacity
Channelization Issue

## Slide 10
2 Frequency
Many Codes
3 Frequency
1 Code
400 kbps
400 kbps
12 Same-Frequency BSAs 20 STAs/BSA lAP = 20 lSTA

## Slide 11
3 Frequency
1 Code
2 Frequency
Many Codes
12 Same-Frequency BSAs 20 STAs/BSA lAP = 200 lSTA
400 kbps

## Slide 12
Conclusion
ROBUST IN MULTIPATH & INTERFERENCE
SIMPLE
HIGH DATA RATES: 10- & 18 Mbps
INTEROPERABLE
CHANNELIZATION FOR HIGH SYSTEM CAPACITY
THROUGHPUT