## Slide 1
Proposal for 2.4-GHz PHY July 1998 Update
John H. Cafarella
MICRILOR, Inc.

## Slide 2
Key Features
32-Mchip/s Transmission
Low EB/N0
Nc=16
Changing Codes
16-ary DBOK
(C-4x4DBOK)
10-Mbps Data Rate
Good PN Codes
Intra-Symbol Multipath
Code Channelization
Inter-Symbol Multipath
OQPSK Spreading
Small PA Backoff
Spectral Confinement
3 Frequency Channels
enabling
link
design
system
Low Acquisition Time
Low Preamble Overhead
Robust Links
BSAIsolation; Coexistence & Interoperability
High Throughput
10-dB Processing Gain
Low Battery Drain
Multipath Resolution
Multi-Signal CCA
Low Slot Time
Channel Matched Filter
Antenna Diversity
(18-Mbps Data Rate)
(15,13) FEC
Power-Efficiency

## Slide 3
Performance Matrix
Processing Gain
Multipath Tolerance*
Basic Data Rate
Chip Complexity
PA Backoff (10 mW PCMCIA)
360 ns
10 Mbps
40K gates
~ 2 dB (OQPSK)
Frequency Channels
3
Spin-up Rate (good channel)
18 Mbps
Interoperate Legacy DSSS?
CCA & Header
³12 dB
275 ns
~ 0 Db (MSK)
2
use CFI
July
May
Code Channels
1744
48
Interoperate Legacy FHSS?
CCA & Header
- -
* 10 Mbps with Channel Matched Filter but no MLSE; MLSE could be added to strengthen 18 Mbps mode as technology upgrade
Preamble Overhead
24 us

## Slide 4
Select New PN Codes (cosets)
8 Cosets with Best Autocorrelation Side Lobes
  Previously chosen for best full crosscorrelation
  Autocorrelation side lobes are worse problem than crosscorrelation side lobes
Increase Delay-Spread Tolerance to 360 ns
Motivates Different Data-Code-Channel Sets
  single code, 2 alternating or 4 alternating
  1744 total; 40 with “best” multipath tolerance
Coset definitions ref: Doc 97/117, Cafarella

## Slide 5
Effect of Autocorrelation Side Lobe
correlator outputs
Correct Channel
Some Other Channel
Main lobe of
direct signal
Main lobe of
direct signal
Autocorrelation side lobe of direct signal
Crosscorrelation side lobe of direct signal
Resultant signal from correct output
A high autocorrelation side lobe can reduce the magnitude of the correct output, making is easier for a crosscorrelation side lobe in any incorrect channel to exceed the magnitide of the correct channel

## Slide 6
Delay Spread Tolerance
Previously reported 275 ns was average for “best crosscorrelation” codes
Channel matched filter ref: Doc 98/175, Boer

## Slide 7
Three-Channel Operation
32-Mchip/s OQPSK Spreading Modulation
  Reduce bandwidth while retaining 10-Mbps rate
  Limits spectral re-growth in PA nonlinearity
Suppress Spectral Side Lobes
  Meet FCC protected band requirement
Expand but “Square-Up” Main Spectral Lobe
  Meet MKK 90%-energy bandwidth requirement
  Achieve same 35-dB ACR as current 802.11

## Slide 8
OQPSK Spreading
32-MHz
chip•data
Stream
Even Chips
Odd Chips
Complex Mod.
Chip Pulse
FIR LPF
D/A
5th Order LPF
Chip Pulse
FIR LPF
D/A
5th Order LPF
No SAW Filter Required on Transmit
Shaping approach ref: Doc 98/203, Webster & Andren
< 200 gates I & Q
-50 dB
16
32
48
Baseband Spectrum to Modulator

## Slide 9
Power Amplifier Backoff
100 mW Tx power requires almost 5-dB backoff,
but for 10-mW PCMCIA is closer to 2-dB

## Slide 10
Interoperability
Multi-Signal CCA for Legacy DSSS and FHSS
Dual-Mode transceiver (exploit CCA circuitry)
  High-rate DSSS plus Legacy DSSS or FHSS PHY
  Transmit Legacy Header as Precursor to High-Rate DSSS
Single PHY Solution
  No need to coordinate Alternate High-Rate PHY Headers
  Does not sacrifice high-rate throughput potential

## Slide 11
Summary
Robust In Multipath & Interference
Simple Hardware
High Data Rate: 10 Mbps (+ 18 Mbps spin-up)
Low Preamble Overhead for High Throughput
3 Frequency Channels
Code Channels For High System Capacity
Interoperable with Legacy DSSS or FHSS