## Slide 1
IEEE P802.11 WPAN SG
Wireless Personal Area Network Guidelines

## Slide 2
Contents
Summary
December 2, 1997 Cleveland, OH
January 15, 1998 Memphis, TN
March 10, 1998 Irvine, CA
April 9, 1998 Cambridge, MA
May 6, 1998 Utrecht, NL
“Current” - May 19, 1998 Irving, TX

## Slide 3
Summary
The following slides are a compilation of the Wearables Ad Hoc Committee and IEEE 802.11 WPAN Study Group discussing the Functional Requirements for WPANs.
This document is a work in process and as such refer to the slides marked “Current” to determine the latest Guidelines.

## Slide 4
Cleveland, OH 12/2/97 Application Matrix

## Slide 5
Memphis, TN 1/15/98 Functional Requirements
Power Management: Low current consumption
Range: 0-10 meters
Speed: 19.2 - 100Kbps (actual)
Small Size e.g., ~.5 cubic inches no antenna
Low Cost: i.e., relative to target device
Should allow overlap of multiple networks in the same area
Networking support for a minimum of sixteen devices

## Slide 6
Irvine, CA 3/9/98 Functional Requirements
Mobility: 0-10mph
Power Management: Very Low current consumption
Range: 0-10 meters
Speed: 19.2 - 100Kbps (actual)
Small Size e.g., ~.5 cubic inches no antenna
Low Cost: i.e., relative to target device
Should allow overlap of multiple networks in the same area
Networking support for a minimum of sixteen devices

## Slide 7
Irvine, CA 3/10/98 Environmental Requirements
Power Management: Very Low current consumption
  Average 20mW @ 10/90 or less
Small Size e.g., ~.5 cubic inches w/o antenna
Low Cost: i.e., relative to target device

## Slide 8
Irvine, CA 3/10/98 Functional Requirements WPAN
Range: 0-10 meters
Mobility: 0-10mph (no roaming to another PAN)
Effective Data Rate at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
Should allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Should allow coexistence of multiple Wireless Systems i.e. P802.11 in the same area
Networking support for a minimum of 16 devices
Bridge or Gateway connectivity to other data networks

## Slide 9
Cambridge, MA 4/9/98 WPAN Guidelines Environmental
Power Management: Very Low current consumption
  Average 20mW @ 10/90 or less
Small Size e.g., ~.5 cubic inches
  excludes antenna & battery
Low Cost: i.e., relative to target device

## Slide 10
Cambridge, MA 4/9/98 WPAN Guidelines Technical
Range: 0-10 meters
Mobility: 0-10mph (hand-off not required to another PAN)
Effective Data Rate at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
Should allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Should allow coexistence of multiple Wireless Systems i.e. P802.11 in the same area
Networking support for a minimum of 16 devices
Bridge or Gateway connectivity to other data networks

## Slide 11
Current WPAN Guidelines Sorted ABC’s
A
  WPANs will seek worldwide spectrum allocations for unlicensed bands e.g., 2.4GHz
  Low Cost: i.e., relative to target device
  Small Size e.g., ~.5 cubic inches
    excludes antenna & battery
  Power Management: Very Low current consumption
    Average 20mW @ 10/90 or less
  Data
  Should allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
  Should allow coexistence of multiple Wireless Systems i.e. P802.11 in the same area
  WPAN Network Access Control

## Slide 12
Current WPAN Guidelines Sorted ABC’s
B
  Delivered Data Throughput at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
  All devices within a WPAN must be able to communicate with each other
  Networking support for a minimum of 16 devices
  Voice
  Range: 0-10 meters
  Attach: within one (1) second, once within range
  Bridge or Gateway connectivity to other data networks

## Slide 13
Current WPAN Guidelines Sorted ABC’s
C
  No single element of failure
  Video
  Roaming: hand-off to another PAN

## Slide 14
New Guidelines
WPAN Density: 1 WPAN in 2 square meters, average density at acceptable [TBD] performance levels
Power Consumption: Each WPAN Device will consume <20 mW long term average [TBD] given a 10% TxRx load in the WPAN