## Slide 1
IEEE P802.11 WPAN SG
Wireless Personal Area Network Guidelines

## Slide 2
Contents
Summary
December 2, 1997 Cleveland, OH
January 15, 1998 Memphis, TN
March 10, 1998 Irvine, CA
“Current” - April 9, 1998 Cambridge, MA

## Slide 3
Summary
The following slides are a compilation of the Wearables Ad Hoc Committee and IEEE 802.11 WPAN Study Group discussing the Functional Requirements for WPANs.
This document is a work in process and as such refer to the slides marked “Current” to determine the latest Guidelines.

## Slide 4
Cleveland, OH 12/2/97 Application Matrix

## Slide 5
Memphis, TN 1/15/98 Functional Requirements
Power Management: Low current consumption
Range: 0-10 meters
Speed: 19.2 - 100Kbps (actual)
Small Size e.g., ~.5 cubic inches no antenna
Low Cost: i.e., relative to target device
Should allow overlap of multiple networks in the same area
Networking support for a minimum of sixteen devices

## Slide 6
Irvine, CA 3/9/98 Functional Requirements
Mobility: 0-10mph
Power Management: Very Low current consumption
Range: 0-10 meters
Speed: 19.2 - 100Kbps (actual)
Small Size e.g., ~.5 cubic inches no antenna
Low Cost: i.e., relative to target device
Should allow overlap of multiple networks in the same area
Networking support for a minimum of sixteen devices

## Slide 7
Irvine, CA 3/10/98 Environmental Requirements
Power Management: Very Low current consumption
  Average 20mW @ 10/90 or less
Small Size e.g., ~.5 cubic inches w/o antenna
Low Cost: i.e., relative to target device

## Slide 8
Irvine, CA 3/10/98 Functional Requirements WPAN
Range: 0-10 meters
Mobility: 0-10mph (no roaming to another PAN)
Effective Data Rate at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
Should allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Should allow coexistence of multiple Wireless Systems i.e. P802.11 in the same area
Networking support for a minimum of 16 devices
Bridge or Gateway connectivity to other data networks

## Slide 9
Current WPAN Guidelines Environmental
Power Management: Very Low current consumption
  Average 20mW @ 10/90 or less
Small Size e.g., ~.5 cubic inches
  excludes antenna & battery
Low Cost: i.e., relative to target device

## Slide 10
Current WPAN Guidelines Technical
Range: 0-10 meters
Mobility: 0-10mph (hand-off not required to another PAN)
Effective Data Rate at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
Should allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Should allow coexistence of multiple Wireless Systems i.e. P802.11 in the same area
Networking support for a minimum of 16 devices
Bridge or Gateway connectivity to other data networks