## Slide 1
OFDM for 5 GHz
Introduction
OFDM Signal Processing
Comparison with Single Carrier Modulation
Summary

## Slide 2
Introduction
OFDM can achieve large delay spread tolerance at high bit rates by:
Converting single bit stream in N parallel bit streams
  Symbol duration is increased, so relative delay spread decreases
  Each parallel bit stream is modulated on one of N subcarriers
Adding a guard time to each OFDM symbol
  Intersymbol interference is avoided
  Guard loss is made small (<1 dB) by choosing N large enough
  Simple and effective way to deal with multipath; avoids need for equalizer and equalizer training, which may take too much training overhead
Use coding to correct for subcarriers in deep fades
  In a multipath channel, subcarriers have different amplitudes
  By using coding, performance is determined by average received power rather than lowest subcarrier power

## Slide 3
OFDM Transceiver

## Slide 4
OFDM Signal Processing
FFT / IFFT : 64 point FFT in 4.8 ms = 53 M real multiplications per
second : comparable to load of existing Digital Video Broadcasting
chips, which do 8192 point FFT in 1 ms (100 M multiplications per
second).
Decoding : Standard code, soft decision decoding chips already
exist for speeds up to 60 Mbps. A binary code is used; QPSK and
16-QAM formed by 2 or 4 binary values, respectively.
Synchronization: Can be done similar to synchronization of a
direct-sequence spread-spectrum receiver, see later slide.

## Slide 5
QAM Mapping
Modulation options are QPSK, 16-QAM (possibly 64-QAM)
Same binary coder / decoder is used for all modulations
Use Gray mapping to map 4 binary inputs to 16-QAM
In receiver, 16-QAM symbol is split into 4 binary metrics, which are the
inputs for the soft decision Viterbi decoder (see IEEE Trans. on Comm.,
vol. 43, no.6, June 1995, pp. 2001-2004, ‘Coded QAM Using a Binary
Convolutional Code’, by Q. Wang and L. Onotera.)
Mapping 2 bits onto 4-PAM Demapping 4-PAM into 2 metrics

## Slide 6
Timing and Frequency Synchronization
Correlation function of OFDM signal Correlation function with {0,1,-1} taps
Correlate with a known OFDM training symbol before doing FFT, so OFDM
symbol is used in same way as the Barker code in a 802.11 direct-sequence system
Use peak to determine timing, phase shift between peaks gives frequency offset
Simple correlator with {0,1,-1} tap values can be used

## Slide 7
Fallback Rates
In single carrier systems, equalizer breaks down when
delay spread gets too large because of error propagation
in equalizer.
Hence, fallback rates not possible, which is very
undesirable for a practical system; users which experience
more than 100 ns delay spread get no connection !
In OFDM, 30 Mbps up to 175 ns delay spread,
20 Mbps up to 225 ns
10 Mbps up to 500 ns
So OFDM does provide a reliable connection for all users,
even if they cannot send at the highest rate because of a
bad channel

## Slide 8
Complexity
Key difference between OFDM and single carrier
proposals is FFT versus equalizer
FFT complexity = 64 complex multiplications per 4.8 ms =
= 53 million real multiplications per second
16 taps Equalizer at 25 MHz means 2*16*25 =
= 800 million real multiplications per second
OFDM order of magnitude less complex!
Fast equalizer training is more complex than
equalizer itself, so real complexity difference is even larger

## Slide 9
Summary
Main advantages of OFDM over single carrier are:
  Less complex
  Can tolerate higher delay spreads, especially in
fallback modes, which are not possible for
single carrier
  More channels, better total capacity