## Slide 1
BCPM Implementation details Jan Boer, Lucent Technologies
See the notes pages for an
explanation of the slides

## Slide 2
Contents
Transmitter
  10 Mbit/s modulation scheme
Receiver structure / complexity
Implementation / performance trade-off
Preamble / training
  interoperability / coexistence

## Slide 3
8 Mbit/s
Notes: At 8 Mbit/s 8 bits (d0 to d7) are transmitted per symbol. In BCPM scheme d2 to d4 define the position of the start of the Barker sequence for the I component, d5 to d8 define the position for the Q component (disjoined BCPM). d5 to d8 are defined in the same way as d2 to d4. See Table.
The figure shows a modulation example for three 8 Mbit/s symbols. A symbol has 11 chip moments (positions in time) of which 8 can be used to start transmitting the 11 chip barker sequence according to the table. Because of the different positions in the symbols, overlap occurs , resulting in the signal I (sum of I-1, I-2 and I-3) and Q (sum of Q-1, Q-2, Q-3).
(see also document 98/10r1: draft spec for BCPM)

## Slide 4
10 Mbit/s
Notes: The modulation for 10Mbit/s is in essence similar to the modulation method of 8Mbit/s. The only difference is that the symbol duration is reduced from 11 to 9 chips. The duration of a chip is not changed. The first 8 chips again define the possible positions (P0 to P7) for the starting points of the Barker sequence. The ninth chip is not used. The figure illustrates the modulation method for 10 Mbit/s.
The reduction of the symbol rate (with essentially the same modulation as 8 Mbit/s: transmitting Barker sequences each symbol) determines the bitrate: 11/9*8 Mbit/s = 9.77 Mbit/s

## Slide 5
Basic receiver structure
RF and IF
stages
Complete
Mixer
A/D
Correlator
Correlator
LO
I
Q
Synchronization
andTiming
Find I,Q peak,
determine
position,
polarity
Decode
position,
polarity
pos, pol
I,Q
1,2,5,8,10
Mbit/s
Notes: The basic receiver structure is not different from the 1 and 2 Mbit/s receiver.
The correlators for the I and Q signal correlate with the 11 chip Barker sequence. The output of the correlators gives each symbol a peak at one of the chipmoments. With a peak detector the position and polarity of the peak can be determined. The outcoming bitstream can be decoded using the decoding table.
In the next slides the output of the correlators is depicted for 8 and 10 Mbit/s

## Slide 6
8 Mbit/s after the correlator
Notes: This slide gives the output of the correlators for 8 Mbit/s.
At the I component peak can be detected at the positions 4,0 and 2, for the Q component at 1,6 and 1. Only the position 0 to 7 are possible, the positions 8,9,and 10 are not used!
Because of the sidelobs of the Barker sequence of +/-1 the detection margin for 1 or 2 Mbit/s (non overlapping Barker codes) is 11:1. At 8 and 10 (and also 5) Mbit/s the sidelobs overlap and can add destructively. The detection margin is reduced to 9:3.

## Slide 7
10 Mbit/s after the correlator
Notes: Compare the correlator output for 10 Mbit/s with 8Mbit/s.
There are still 8 positions (0 through 7) where a peak can occur. But in 10 Mbit/s there are only 9 positions in a symbol where the ninth position is not used .
Note The Barker sequence is still 11 chips.
The symbols are just shifted into eachother.

## Slide 8
8 and 10 Mbit/s compared
Eb/N0
  detection problem is the same (QPSK and 1 out of 8 positions)
    Eb/N0 = 6dB for both 8 and 10 Mbit/s
SNR
  At 10 Mbit/s 11/9 more (0.87dB) than 8 Mbit/s
  Effect on link budget minimal, because also 11/9 more energy is send at the transmitter (Barker sequences shifted into each other)

## Slide 9
Performance at multipath channel
Delayspread in combination with Barker sidelobs reduce the performance
With basic receiver delayspread up to 30-40 ns can be handled
Dramatic improvement by treating sidelobs and the channel with MLSE techniques
MLSE receiver structure is not complex due to Barker correlation properties

## Slide 10
MLSE Receiver Structure
RF and IF
stages
Complete
Mixer
A/D
Correlator
Correlator
LO
Synchronization
andTiming
CPE
CMF
I
Q
Tentative Symbol
Estimator
Mode Sifter
(Viterbi)
Final
Estimates
Conventional Receiver
CPE channel parameter estimator
CMF channel matched filter
Notes: The properties BCPM makes it possible to split a ‘full blown’ MLSE receiver in relatively simple blocks. Added to the ‘conventional receiver’ are a Channel Matched Filter (CMF), a Tentative Symbol Estimator (TSE) and a Mode Sifter (MS) block.
The TSE estimates the four most likely position combinations of I and Q in a symbol. At this point the signal is disrupted because of cross rail interference (i.e.. the interference caused by the different position of the I and Q peak and the channel impulse response), the intersymbol interference (also caused by the channel impulse response) and the Barker sidelobs. Analyses showed that if initially in the TSE the sidelobs and the ISI are ignored, but the cross rail interference is removed, the estimation of the four most likely (tentative) position combinations is very reliable.
The Mode Sifter uses these 4 estimates. In a 4X4 trellis structure the MS removes the sidelobs and the ISI to come to a final decision.
These blocks will be explained in the next slides.

## Slide 11
Channel Matched Filter
CMF is the complex conjugate of the channel impulse response c(t)
c(t)
c (t)
*
q(t)
Tx
channel
CMF
Output of CMF is the impulse response of the transmitted signal by the convolution of the channel and the CMF [c(t) * c (t)]
*
Notes: During the training at 1Mbit/s it is simple to estimate the impulse response of the channel. There are many ways of doing this.
The output of the correlator delivers for each symbol at one chip moment the peak, while the signals at the other chips are a result of the echoes of the channel. Averaging the output over several symbols gives a good estimate of the channel impulse response. Note that the data must be removed (e.g. inverse the impulse response if the peak is negative) before averaging.
The CMF is the complex conjugate of the impulse response of the estimated channel. The structure of the CMF is a FIR filter. Once the channel response is known, the taps can be loaded in the CMF. The number of taps have effect on the overall performance. In Lucents implementation the number of taps is 6 (at chiprate).
The transmitted signal is filtered by two filters (serial): the channel and the CMF. The output of the CMF is determined by the convolution of the transmitted signal with the channel and the CMF.

## Slide 12
Simple example
  Two ray channel impulse response
I
Q
time
I
Q
time
c(t)
c(t) * c (t)
*
(1)
(1)
(-1)
(1)
(2)
Notes: This slide give a simple example for a two ray channel impulse (c(t)). The first ray is 1 at the I-axis, the second is delayed e.g. 1 chip and gives a 90 degrees turn (1 on the Q-axis).
The convolution of c(t) with its complex conjugate c*(t) gives the impulse response at the right hand side.
The following characteristics for the overall impulse response are generally true:
The energy is more concentrated in one ray, thus improving the SNR: in the example one ray of length 2 compared to two rays of length 1.
The convolution also gives always a anti-symmetric impulse response. This symmetry is very helpful to reduce the complexity in the algorithms used in the TSE and ModeSifter.
Finally the application of the matched filter gives optimal sample timing. This is not shown in the slide. To give an idea why, suppose the peak of the correlator is sampled in the slopes: In the channel estimation the will
look like a two ray impulse response. After the CMF the impulse response looks like: giving optimal timing.

## Slide 13
Benefits of the application of the CMF
  Concentrates energy, improving SNR
  Gives (anti-)symmetric impulse response
  Gives optimal sample timing

## Slide 14
Tentative Symbol Estimator
  With knowledge of channel the TSE removes cross rail interference i.e. crosstalk of I component on the Q component and vice versa and estimates the 4 most likely positions combinations for I and Q
  Crossrail interference is caused by the channel (echoes) and the CMF (convolution of the two)
  Interference is known
  Interference of I on Q and Q on I is symmetrical because of the antisymmetrical impulse response of the channel and the CMF and is defined by the imaginary part of c(t) * c (t)
*

## Slide 15
Crossrail example
I
Q
time
c(t) * c (t)
*
(-1)
(1)
(2)
I
Q
time
Tx: q(t)
*
I
Q
time
Because of knowledge of the channel crossrail terms (imag. part of c(t) * c (t) ) are known (bias terms)
Bias terms are calculated during training (8 values for 8 positions)
p0
p1
Notes: This slide gives an example of cross rail interference. The left-hand signal is the transmitted signal before it is spreaded with the Barker sequence. At position 0 (p0) the I puls is transmitted; At position 1 (p1) the Q puls.
The channel impulse response is the same two ray channel as in slide 12. At the right the received signal after the correlator is constructed. As can be seen, a crossrail term of the Q component adds up to the I component and vice versa.
Because the overall channel impulse response [c(t) * c*(t)] is known (learned during training) the crossrail terms are known. They are defined by the imaginary part of the channelresponce.
It can be seen that the crossrail terms are a function of the relative position of I and Q. In above example the position distance of 1 the crossrail term is +1; the positiondistance of -1 has a crossrail term of -1. At a higher distance in this example there is no crossrail.
Within a symbol the distance between a I and Q peak is maximum 8. For any channel impulse response the crossrail terms can be determined. We call them the Biasterms.

## Slide 16
Biasterms
I
Q
time
c(t) * c (t)
*
b1
b2
b3
b4
etc..
only imaginary term contribute to bias terms
Notes: An example of the biasterms for another (combined) channel response. Note again that only the imaginary part contributes to the terms.
b1 is the biasterm if the distance between the I and Q peak is 1 chip, b2 for the distance of 2 chips ect.

## Slide 17
TSE procedure
For all possible positions of I (from 0 to 7) and Q (also from 0 to 7) calculate:
maximum determines polarity of I and Q
b+(I+Q) + +
b-(I+Q) - -
-b+(I-Q) + -
-b-(I-Q) - +
Select 4 maxima out of 64 (to be evaluated in the Mode Sifter (trellis))
Notes: Each symbol there are 8 positions possible for the peak of the I component and 8 for the peak of the Q component. The peaks, and even the polarity of the peaks, are obscured by all before mentioned distortions (crossrail, ISI, sidelobes and of course noise and possible other interferers). It is the task of the TSE to make an assessment of the 4 most likely combinations of I and Q peak positions.
All 64 position combinations are being checked. Thereby the TSE also decides on the polarity of the I and Q peaks. For each combination 4 calculations are being done. The metric for the decision is the sum of the possible I and Q peak taking into account the possible polarity and the bias term that belongs to the positioncombination (function of the distance between the peaks). So for this metric the crossrail effect is being removed (The Mode Sifter takes care in a later stage of the ISI and sidelobeffects)
The metric is listed in the slide for the 4 polarity combinations. Based on the highest value the polarities of the I and Q peak are decided upon.
After evaluation of all 64 position combinations the 4 highest metric values are selected for further processing in the ModeSifter. By analysis it is shown that selecting only 4 tentative symbols is sufficient. This is mainly caused by the fact that the sidelobs of the Barker sequence are low (+/- 1), so that they may be ignored in this processing step.
The 4 selected Tentative Symbols are being described by their metric value, the positions for I and Q and the polarity of the peaks.

## Slide 18
Example of TSE calculation
I
Q
time
Tx: q(t)
*
I
Q
time
I
Q
c(t) * c (t)
*
(-1)
(1)
(2)
b=-2
-b
p0
p2
p1
p3
= +
Position evaluation
I position Qposition b b+(I+Q) b+(I-Q) -b+(I-Q) -b-(I-Q)
1 2 -2 -2 -2 4 0
1 0 2 2 2 0 -4
3 2 2 2 2 0 -4
p1
p2
Notes: The above example is to show the process of the TSE in a somewhat simplified manner. The transmitted signal has (before the spreader) an positive I peak on position p1 and a negative Q peak on position p2. We use again the same channel as in earlier examples (two ray). At the right is the signal constructed after the correlator. There are two I-peaks at position p1 and p3 and two Q-peaks at the positions p0 and p3.
In the slide three (out of the 64) possible position combinations are evaluated. Evaluation shows that the I-peak on position p1 and Q-peak at position p2 has the highest metric. The polarity this combination is for the I-peak positive and for the Q-peak negative. This shows that by compensating for the crossrail a right decision can be made.
The metric for the other combinations is less. These combination will however also be forwarded to the modesifter (in this example not really necessary) for further evaluation.

## Slide 19
TSE Implementation
b+(I+Q)
b-(I+Q)
-b+(I-Q)
-b-(I-Q)
4 out of 64
Notes: The slide gives a blockdiagram for a possible TSE implementation.
8 evaluation blocks are in parallel. In these blocks at each clockcycle (e.g. chip interval) the 8 I-positions are evaluated in combination with the one of the Q-positions. In this cycle the metrics are being calculated and a decision is made on the most likely polarities for each combination.
At the left side is the Q shift register, taking care that the next cycle the following Q value is shifted into the evaluation blocks.
The (parallel) shiftregister with the bias term takes care that the right biasterm is shifted in each evaluationblock as a function of the distance between each to be evaluated I- and Q- position.
Out of the 64 results of the evaluation blocks the 4 I_Q positoncombinations with the highest metric are selected to be forwarded to the modesifter.
It can easily be seen that each evaluation block makes 4*2 addition per clockcycle, resulting in a total of 8*8*4*2 addition per symbol.
In the whole TSE block there are no multiplications.

## Slide 20
TSE implementation
Low complexity:
  in evaluation block 64 *4*2 additions during a symbol period (1 microsecond)
    optimal implementation choices can reduce this number
  selection of 4 maximum values out of 64

## Slide 21
The Mode Sifter
Reduced state trellis structure sifting the tentatively retained modes (maxima of TSE)
Calculates path metric taking ISI and sidelobs into account
Trellis path determines final estimate
  path depth of 4 is sufficient

## Slide 22
Trellis structure
Notes: The algorithm to be implemented is schematically shown in the slide and is a well known trellis structure. The inputs to the trellis are the 4 tentative decisions of the TSE. Practical results have shown that a depth of 4 of the trellis is sufficient.
The node (bullet) can be any of the N=256 symbols (64 position combinations plus the polarity of I and Q). The 4 paths (solid line) all end in different symbols . The paths are the strongest of the 4 possible paths (dashed lines) ending at that symbol. This is determined by the metric .Ideally the paths converge to a single symbol at position k-3, which will roll-out as a decision at the next step. Anyway, at the next step k+1 the symbol at the tail of the strongest (windowed) path is put out as decision.
Taking a decision is one task of the MS. Before taking the decision, the MS has to calculate the metric.

## Slide 23
Metric calculation
Iteration process
where V is the metric as calculated in the TSE
G is the ISI term
At each step (symbol) the addition of the two terms have to be performed for 16 possible paths
Notes: The iteration process is such that the metric of the new outputs of the TSE are added up to the previous metrics. This is corrected by the ISI term G.

## Slide 24
The ISI term
Notes: Because of the applied pulse positioning modulation the I- and Q-peaks in adjacent symbols can lay close together. The minimum distance at 5 and 8 Mbit/s is 4 chips, while at 10 Mbit/s this is even only 2. Because of the delayspread in the channel there will be Intersymbol interference. One of the tasks of the ModeSifter is to remove this ISI.
Also the sidelobs of the Barker sequence overlap over the symbol boundary. It is also the function of the MS to remove this interference.
In principle in the same way as for the Biasterms in the TSE the ISI between the I- and Q- peaks is known, because the transmission channel (inclusive the CMF) is known. Also here the amount of ISI is a function of the distance between the peaks. These ISI terms are calculated and stored at the time of training of the receiver .
The effect of the Barker sidelobs is also a function of the distance between the peaks. This effect is also included in the stored ISI terms by correlating the channel with the Barker code.
The actual ISI for the I- and Q-peaks of 2 consecutive symbols is calculated according to the formula in the slide.
The first term takes care of the ISI of the two I-peaks (taking into account the polarity), the second term for of the Q-peaks, the third term for the ISI of the I-peak of one symbol to the Q-peak of the other and the fourth vise versa.
Note that the formula is only an addition of four terms. The sign of the terms is determined out of the polarity of the peaks.
For the metric calculation the process adds 3 additions per metric.

## Slide 25
Complexity of Modesifter
Metric calculation
  16 * 5 additions per symbol
Path maintenance
  basic digital techniques can be applied
Because the reduced trellis structure (4X4) the Modesifter has, compared to other blocks, a rather low complexity in terms of gates

## Slide 26
Performance/complexity trade-off
Basic receiver
  no CMF, TSE or MS
  gate count 20-30 Kgates
  will work in a (simple) office environment
    up to 30-40 ns delayspread for 8 and 10Mbit/s
    fall back to 1,2 or 5 Mbit/s

## Slide 27
Performance/complexity trade-off
Basic receiver with CMF
  gatecount 35-45 Kgates
  works in office environments and most other environments at 5 Mbit/s fallback
  delayspread
    5 Mbit/s 275-350 nsec
    8 Mbit/s 55-90 nsec
    10 Mbit/s 50-80 nsec
Notes: 5 Mbit/s does not suffer from crossrail interference. Only at high delayspread values the ISI will limit the performance.
For 8 and 10 Mbit/s the crossrail interference is the limiting factor. At delayspread values around the chiptime (90 nsec) ISI is not an factor, because their is a guard interval between the symbols (at 8 Mbit/s 3 chips, at 10 Mbit/s 1 chip). That why the performance between 8 and 10 Mbit/s does not differ very much.

## Slide 28
Performance/complexity trade-off
receiver with CMF, TSE and MS
  gatecount about 60 Kgates
  works in office, retail and industrial environments
  delayspread
    5 Mbit/s 355-400 nsec
    8 Mbit/s 235-265 nsec
    10 Mbit/s 130-220 nsec
Notes: Here we see that the performance improvement caused by the TSE and MS for 5 Mbit/s is moderate. The removal of ISI (there is no crossrail interference) takes care of an extra 50-100 nsec in terms of delayspread.
The implementation of the TSE and MS especially pays off for 8 and 10 Mbit/s. Removal of crossrail and ISI makes that both rates can work in environments with high delayspreads. The difference between 8 and 10 is mainly caused by the fact that 10 Mbit/s has a lower guard against the ISI that is left.

## Slide 29
Preamble and training
Training (above standard 1 Mbit/s)
  8 or 16 symbols for CMF
  calculation for Bias and ISI terms
    during processing of 1Mbit/s SFD (16 symbols)
Optional short preamble is proposed
  draft text doc 98-10r
  March presentation 98-99

## Slide 30
Interoperability / Coexistence conclusion
Interoperabilty
  short preamble Tx - short preamble Rx
  long preamble Tx - long preamble Rx
  long preamble Tx - short preamble Rx
Coexistence
  all Proposed DS Phy’s
BUT..

## Slide 31
Coexistence with FH
Symbol Technologies showed that coexistence with Frequency hoppers can be achieved by adding a FH signal preceding the preamble.
Lucent proposes to incorporate the optional extension into the BCPM proposal.

## Slide 32
Conclusions
BCPM is not complex
Implementation of a MLSE structure is not complex for BCPM
  CMF, TSE and MS described
  Doubles gate count compared to 2 Mbit/s DS
Implementation (gate count) / performance trade-off
Coexistence/interoperability with current DS and FH standard