## Slide 1
IEEE 802.11 5.2 GHz OFDM proposal MAC performance

## Slide 2
Traffic & MAC assumptions
Traffic
  constant 1500 byte packet length
  20, 30 Mbit/s (according to Lucent/NTT proposal)
  Poisson packet arrival process
  75% downlink traffic, 25% uplink traffic
  No handoffs / roaming
MAC
  CMSA/CA according to IEEE 802.11 spec
  MAC Parameters according to Lucent/NTT proposal
    SlotTime = 6 ms
    SIFS = 13 ms
    DIFS = 25 ms
    PHY overhead = 21 ms + (2.4 or 1.6) ms
  Buffer capacity of 10 packets (15Kbyte)

## Slide 3
Radio parameters
Transmit power 200mWatt (23dBm)
0dB-gain omni directional antennas
Pathloss model: 5.2 model as developed for Magic WAND
Log-normal fading of 8dB
Receiver Noise Figure: 5dB
Thermal Noise: (-103dBm) (2Mbit/s DSSS: -114 dBm)
Simulated BER curves used as input
  assume i.i.d. bit errors with probability pi for i-th bit
  Assess BER for i-th bit and calculate
Pr{packet error} = 1 - Pi (1-pi)

## Slide 4
Topology
STA - AP separation: 20 m: RSS = -58dBm,
One Access Point, 10 Stations
Two Access Points 60m apart, 10 Stations, 20m away
Range approximately 50 m (see next slide)
Simulated 10 minutes of real time

## Slide 5
Pathloss versus distance

## Slide 6
Constellation 1
AP
STA
STA
STA
STA
STA
20m
STA
STA
STA
STA
STA

## Slide 7
AP
STA
STA
STA
STA
STA
AP
STA
STA
STA
STA
STA
20m
60m
Constellation 2

## Slide 8
Theoretical max throughput per station
packet length [bytes]

## Slide 9
Constellation 1, Throughput

## Slide 10
Constellation 1, Delay

## Slide 11
Constellation 2, Throughput

## Slide 12
Constellation 2, Delay

## Slide 13
Conclusions
Maximum Throughput without reuse
  21 Mbit/s of 30 Mbit/s (70%)
  15.5 Mbit/s of 20Mbit/s (77%)
  compare: 1.72 at 2Mbit/s (86%)
Throughput at 5% Packet loss probability
  0.67, for offered traffic 0.7, at 30Mbit/s
  0.75 for offered traffic 0.8 at 20Mbit/s
  0.4 for offered traffic 0.9 at 2Mbit/s DSSS
Delay
  less than 3.2 ms at 30Mbit/s
  less than 5.0 ms at 20Mbits/s
  compare 44.1 ms at 2Mbit/s
High speed MAC maintains efficiency due to PHY preamble
  4% to 5% of 1500 byte packet (3% at 2Mbit/s)