## Slide 1
Why Should you Choose Offset Quadrature Modulation?
Naftali Chayat + Kazuhiro Okanoue
BreezeCOM + NEC

## Slide 2
Why not PPM?
PPM does not live to its promises:
  Power saving by PA switching is unrealistic (with stringent out-of-band restrictions)
  Sensitivity to multipath (how to set threshold?)
PPM proposal did not show complete data
PPM data contains inconsistencies
  Unrealistic AWGN sensitivities

## Slide 3
OQM vs. OFDM - Similarities
Both proposals are basically good
  Both utilize multipath as a frequency diversity, OFDM by coding, OQM by equalization
Both proposals behave similarly in terms of
  Sensitivity
  Throughput
  Phase noise tolerance
  CCI

## Slide 4
OQM advantages vs. OFDM
OQM enables smaller backoffs (especially in binary mode)
Higher rates reached
Possibility to trade multipath tolerance for complexity

## Slide 5
OQM disadvantages vs. OFDM
More processing power is required
Less channels (9 vs. 11)
Harder to implement low, more robust rates

## Slide 6
OQM is practical - some details
Simple CCA implementation
Equalization
Equalizer initialization
Carrier Tracking

## Slide 7
Header and CCA detection
+
Z1
+
-
+
Output
matched
to A1
Output
matched
to B1
+
Z2
+
-
+
Output
matched
to A2
Output
matched
to B2
+
Z32
+
-
+
Output
matched
to A64
Output
matched
to B64
+
Z64
+
-
+
Output
matched
to A128
Output
matched
to B128

## Slide 8
Equalizer and Carrier tracking
jk
2 in - 1 out
FFF
Slicer
1 in - 2 out
Reconstr. F
1 in - 1 out
FFF
Dual Matched filter
NCO
Loop
Filter
Delayed Input Samples

## Slide 9
Equalizer Initialization
Paper by Dan Raphaeli - 98/188
  Based on Iterative (Gauss-Siedel) technique for matrix inversion
  Adapted to high speed implementation (no divisions, just shifts
  Fits well within framework of hardware already present for equalization

## Slide 10
RX block diagram
Notes: This slide shows a tentative receiver architecture. A diversity reception is an optional. First of all, received signals are fed into an AGC system and adjusted their input level. Then a frequency offset in the received signals is estimated by an AFC system. A PLL uses the estimated offset value from the AFC as its initial value. The estimated offset is also fed into a phase shifter to cancel frequency offset in the received signal. Then impulse response estimator estimates channel impulse response vector and supplies the estimated vector to an anti-multipath scheme such as an equalizer. The anti-multipath scheme outputs decision results and error signals to the PLL to adaptively cancel frequency offset in the received signals.

## Slide 11
RF/IF chain for O-QPSK

## Slide 12
A/D accuracy (1)
Notes: shows a packet error rate (PER) performance vs A/D accuracy in an environment of 100nsec delay spread. This figure indicates that A/D accuracy of 8-bit slightly degrades PER and the degradation seems to be negligible.

## Slide 13
AD accuracy (2)
Notes: In the simulation, I assumed a dynamic range of input signal level as +/- 1.0 and a dynamic range of A/D converter as +/- 1.5, as shown in this slide.

## Slide 14
CCA mechanism (1)
Notes: As a CCA detection mechanism, we propose to adopt envelope or RSSI signal detection mechanism as shown in this slide. When an averaged envelope level of received signals gets over the threshold level, the CCA detector detects that the medium is busy.

## Slide 15
CCA mechanism (2)
Notes: This slide shows performances of the CCA detection mechanism in AWGN channel. In this figure, we assumed to use envelope detector. The graph shows both misdetection and false detection error rates. The misdetection error rate is a probability which a receiver can not detect signals even if the receiver receives signals. The false error rate is a probability which a receiver detects noise as a signal. From the figure, the false error rate can be negligible by setting CCA threshold about 6db higher than noise level. The misdetection rate depends on receiver sensitivity and the number of averaging symbols. Though each vendor can choose the appropriate values for his implementation, it is one suggestion to use 4 symbol duration for averaging and threshold 6dB higher than noise level.

## Slide 16
Equalizer Architecture
Notes: This slide shows an example of state transition for the 3tap PMA-MLSCE to estimate s(i) transmitted symbol at t=i. It is assumed that a transmitted symbol is binary, the length of a channel impulse response is 3 and the current time is i. In this example, the PMA-MLSCE defines three state vectors S(t) for t=i, i-1 and i-2 which are consisted from symbol candidates s(i)’s and/or decision results D(i)s. Because D(i)s are deterministic, each state vector can take only 2m values where m is the number of symbol candidates in a vector. Then transitions between the state vectors can be defined as shown in the figure.
The PMA-MLSCE calculates metric, for all possible state vector values. The calculated metric are summed up along the transitions as a combined metric. The PMA-MLSCE selects a transition which presents the minimum combined metric and outputs the s(i) in the transition as a estimated results.
In order to reduce complexity of implementation, it is possible for the PMA-MLSCE to implement the part surrounded by the dotted line. In this case, the PMA-MLSCE uses two candidate symbols and one decision result to detect s(i). We denote the reduced PMA-MLSCE as n-m PMA-MLSCE, where n and m are tap number fed candidate symbols and decision results, respectively. Based on the notation, the part surrounded by the dotted line can be expressed as 2-1 PMA-MLSCE.

## Slide 17
Equalizer Architecture
Notes: The implementation example of 2-1 PMA-MLSCE for O-QPSK is demonstrated in this slide. The vector multipliers produce replica for all possible states. The vector multipliers can be implemented without any multipliers, because input signals, s(1), s(0), D(i-1) and D(i-2) are +1 or -1. After summing up the metrics along the state transition described in the previous slide, the summation corresponding to each state transition are fed to the minimum detector. The minimum detector detects the minimum value all the input signal and outputs the decision results. Moreover, the minimum detector controls the selector so as to output a replica which minimizes the metric.

## Slide 18
PLL Architecture
Notes: In order to obtain stable carrier, we use 2nd order PLL by using PMA-MLSCE output and received signal. The PMA-MLSCE calculates replica of received signals. A phase difference between received signal and a replica which produces minimum metric is input to the 2nd order PLL. The PLL output controls carrier frequency and phase.

## Slide 19
Equalizer Initialization
Notes: The MLSCE requires only channel impulse response for its initialization. In order to estimate channel impulse response, a correlation technique between received signal and known preamble sequence can be available as shown in this slide.

## Slide 20
Sensitivity @ Delay Spread

## Slide 21
Backoff requirements

## Slide 22
AWGN Link Budget

## Slide 23
Choose OQM!!!
It is practical for low-2-medium delay spreads
It optimizes a resource which will not improve with time
You can match a complexity to an application