## Slide 1
Code Separation vs. Frequency Reuse
Submission to IEEE P802.11 Wireless LANs
Karen Halford
Mark Webster Harris Semiconductor mwebster@harris.com

## Slide 2
Code Separation vs. Frequency Reuse Problem Statement
Description of Frequency Reuse
Coding Techniques
  Description
  Asynchronous Nature
WER vs. SIR Simulation Results
Description of Average Interference Simulation
Average Interference Simulation Results
Overview
Notes: Code separation and frequency reuse are different ways of isolating users (or stations.) However, one must choose how much of the available resources should be dedicated to separating users via codes and how much should be dedicated to separating users spatially.
Frequency reuse for an 8/3 scheme and a 16/2 scheme are described in more detail.
The coding techniques used in our simulations for the 8/3 scheme and the 16/2 scheme are described in detail. The important issue of “asynchronous transmission” is also discussed.
Simulations comparing the 8/3 scheme with the 16/2 scheme with respect to signal-to-interference ratio are given.
An “average interference” scenario is described, and simulation results are given for this scenario.

## Slide 3
8 Chip Code/Frequency Reuse:3
16 Chip Code/Frequency Reuse:2
Notes: This slides shows the tradeoff between the 8/3 scheme and the 16/2 scheme.
BASIC DESCRIPTION:
The 8/3 scheme uses 8 chips codes. (Each sequence carries 4 information bits.)
The 16/2 scheme uses 16 chip codes. (In our simulations each sequence carries 4 information bits.)
The 8/3 scheme has a frequency reuse pattern which allows three cells to use a different frequency band. Once the three frequency bands have been used, they must be “reused”. In the diagram, cells using a common frequency band are indicated in the same color.
The 16/2 scheme only has a frequency reuse of 2. Notice the close proximity of cells using the same frequency band.
CONCLUSION:
Recall that longer codes provide more separation. Here we define the code separation of the 8/3 scheme to be 2 chips/bit (8 chips/4 information bits). In these simulations for the 16/2 scheme, we used a code separation of 4 chips/bit (16 chips/4 information bits.) This is different from the Micrilor scheme which actually only has a code separation of 3.2 (16 chips/5 information bits.)
By using the shorter codes, the 8/3 scheme provides a significant buffer against “same frequency interference” in the frequency plan. For instance, if a station is at the edge of the cell, its nearest neighboring interferer is at least a cell radius away. The 16/2 scheme does not provide any protection for its cells from common frequency neighboring cells. In fact, if a station is at the edge of a cell boundary, its nearest interferer can be right next to it.

## Slide 4
8/3 Scheme
16/2 Scheme
8 interferers:
4 near/4 far
6 far interferers
Cellular Layout for 2 Schemes
access point
interferer
desired user
Notes: The frequency reuse plan is shown in more detail for the 8/3 and 16/2 scheme in this slide.
All red cells use exactly the same frequency bands. Let’s assume that a desired station at the “green star” is trying to communicate with the access point in the center of each diagram. Any stations in the nearby red regions can cause interference with this communication.
In the 8/3 scheme, there are only 6 cells which cause interference, and stations in these cells are at least a cell radius away from the desired user.
The 16/2 scheme, on the other hand, has 8 cells, 4 of which are actually touching the cell with the desired user. In fact, we show a worst case here in which an interferer could actually be located right next to the desired user.

## Slide 5
3 Data Bits choose
1 of 8 codes
Walsh
Encoding
Hex 3
Cover Code
User 1’s
Random
Bits
Walsh Encoding
4 Incoming Data Bits
8 Chip Spreading
rate=R
rate=R/2
rate=R/2
4th bit
determines sign
x
-1
Cover Code:
Notes: This slide shows the the coding sequence that was used in our simulations.
4 bits are broken into a group a 3 bits which selects 1 of 8 walsh codes and the other bit determines the polarity of the Walsh function. Finally a hex 03 code is placed on top of that code. This results in a code separation of 8 chips/4 information bits or “2”.

## Slide 6
16 Data Bits
Walsh Encoding
Cover 4 Walsh Words with CA CB CC CD
Walsh
Encoding
CA CB CC CD
Cyclic Cover Code
User 1’s
Random
Bits
16 Chip Spreading
rate=R
rate=R/4
rate=R/4
Notes: This slide shows the the coding sequence that was used in our simulations for the 16/2 scheme.
4 bits select 1 of 16 walsh codes. Once 4 of these sequences are selected, the resulting 64 chip sequence is covered with one of 48 “cover codes”. These codes merely scramble the sequences.
This yields a code separation of 16 chips/4 information bits or “4”. Micrilor’s scheme actually uses a 5th bit that determines the polarity which was not included in our simulations. Thus, Micrilor’s code separation is actually only 3.2 instead of 4.

## Slide 7
ith code
User 1
User 2
User 3
(i+1)st code
(i-1)st code
(i-1)st code
ith code
(i+1)st code
(i+1)st code
ith code
(i-1)st code
Asynchronous Transmission
Notes: One more important issue is the problem with “asynchronous transmission.”
If a perfectly synchronous system (without multipath) could be maintained then a set of orthogonal codes could be chosen for that system such that interference from adjacent channels would be minimal. In such a case, performance analysis would be very simple. However, this system is not synchronous and is certainly not free of multipath.
The performance of both the 16/2 and the 8/3 schemes is affected by asynchronous transmission. In order to accurately analyze this system, it is necessary to consider the crosscorrelations of all codes at all possible delays for varying numbers and amplitudes of interferers. Thus the most appropriate way to measure performance is by simulating the systems with random delays and random codes. This has been our approach in this paper.

## Slide 8
Simulations: A Fair Analysis
Must account for asynchronous stations.
AGN is not an accurate model of multiaccess interference.
CW is not an accurate model of multiaccess interference.
Notes: As discussed on the previous slide, simulations are a fair way to compare the 8/3 system to 16/2 system since we must account for users whose signals are asynchronous relative to each other. Simulations are also able to model the various cover codes transmitted by the 16/2 system.
It is well known that additive Gaussian noise is not an accurate model of multiaccess interference. Additive Gaussian noise is only an effective model when there are many users whose signals arrive at the receiver with fairly equal power. This is certainly not the case in this system since such constraints on the received signal would require tight power control.
A CW signal is also an inaccurate model of multiaccess interference. A CW signal does not model the random data transitions of a real interferer.

## Slide 9
8/3 : 16/2 vs. Harris : Micrilor
Realistic model of multiaccess interference.
Lognormal fading included in
performance comparison.
Multipath, channel characteristics not included
(not necessary to draw conclusion.)
Gives Micrilor false advantage on code separation.
Notes: In these simulations, we have boiled down the Harris and Micrilor schemes to simpler schemes which we can easily compare. Therefore, we would like to explain the difference between our simulations and the actual systems in order to translate our results to Harris’ and Micrilor’s systems.
These simulations realistically model multiaccess interference. Real interferers’ signals are generated and added to the desired user’s signal before detection.
In our final simulation in which we compare the two systems, we do include lognormal fading.
We have not included multipath or channel characteristics such as phase offsets. However, multipath can be viewed as “additional” coherent interferers which means that these results easily translate to the multipath case.
We have also given Micrilor an unfair advantage in the simulation of the codes by ignoring the 5th “polarity” bit in their code. This allows the 16/2 codes more code separation than Micrilor’s codes actually have.

## Slide 10
Walsh Error Rate vs. Signal to Interference Ratio
Single Interferer
Randomized delay
Randomized cover codes (16/2)
No additive noise or fading
Notes: This plot gives the Walsh Word Error rate vs. Signal-to-Interference Ratio in dB for both the 8/3 and the 16/2 schemes.
There is only one interferer in the presence of a desired user.
In both cases, the relative delay between the desired user and the interferer has been randomized.
The cover codes for the 16/2 scheme are randomized.
This is an ideal simulation with no additive noise or lognormal fading.
CONCLUSIONS
Notice that both schemes have a “plateau” at which the word error rate stays constant. This is expected since both schemes must contend with short codes. This plateau smooths out as the number of interferers increases.
This plot does not indicate anything about the relative performance of the two schemes. We would certainly expect the 16/2 scheme to have a smaller word error rate for a given SIR. The 8/3 scheme will actually operate at a lower SIR than the 16/2 scheme because its cochannel interferers are much farther away.

## Slide 11
8/3 Scheme
access point
interferer
16/2 Scheme
Interferers at center of nearest half of cell
Lognormal fading with std dev of 8dB
Random delay and cover codes
Average Interference Scenario
Notes: As mentioned on the previous slide, the WER vs. SIR plot indicates nothing about the relative performance of the two schemes. Therefore, we have devised an “average interference scenario” which does indicate relative performance.
Here we show the frequency plan for both schemes. The yellow triangles indicate cochannel interferers. For each scheme we have placed a potential interferer at the centroid of the nearest half of each cochannel cell.
In these simulations, we also include lognormal fading with a standard deviation of 8dB.
The delays of all users are randomized. The cover codes of the 16/2 users are randomized.

## Slide 12
Simulate &
Combine All Possible
Interference Situations
Overview of Interference Simulation
Notes: Simulations were run for every possible set of interferers. As an example, we show all possible sets for the 8/3 scheme in this slide. The results of these simulations were combined using a binomial distribution along with the probability that a given interferer was actually transmitting.
This same technique was used to enumerate all possible sets of interferers for the 16/2 scheme, and the results were combined appropriately.
This produces a true “average” comparison of the 8/3 scheme vs. the 16/2 scheme.

## Slide 13
Walsh Error Rate vs. Pr. of an Active Interferer
Multiple Interferers
Randomized delay
Randomized cover codes (16/3)
Lognormal Fading
(8 dB Std dev)
Notes: The simulations were run including randomized delays, randomized cover codes, averaged interferers and lognormal fading with 8 dB standard deviation, and this was the resulting curve.
The y-axis shows the Walsh word error rate, and the x-axis shows the “probability of an active interferer.” The probability of an active interferer is simply the probability that a given interferer is actively transmitting.
Notice that the 8/3 scheme consistently outperforms the 16/2 scheme. Although the probability of an active interferer is small on this plot, this result is consistent as that probability is increased. The 8/3 scheme always outperforms the 16/2 scheme.

## Slide 14
Packet Error Rate vs. Pr. of an Active Interferer
Multiple Interferers
Randomized delay
Randomized cover codes (16/3)
Lognormal Fading
(8 dB Std dev)
Notes: We show the same results with the Packet Error rate rather than the Walsh Error rate. In this plot, the 16/2 scheme is given another unfair advantage because we used a word size of 5 bits instead of the 4 bits that were simulated. The 16/2 scheme’s curve would rise slightly if this advantage were removed.
These simulations clearly indicate that the 16 chip code is more vulnerable to the large interference encountered with a frequency reuse of 2 than the 8 chip code with a frequency reuse of 3.
These plots translate to a direct and fair comparison between the Harris (8/3) scheme and the Micrilor (16/2) scheme, and Harris outperforms Micrilor.