## Slide 1
Differential Pulse Position Modulation for 5 GHz

## Slide 2
Why DPPM?
Low-Cost, Low-Complexity 5 GHz PHY
    Non-Coherent Detection
    No Equalizer
      Equalizer Training & Error Propagation are fundamental problems.
      “Text-Book” Equalizers and their Simulations don’t make Products.
    No FFT Processor
      OFDM more suitable for outdoors.
      Sub-optimal for indoors.
Power Efficient
    Transmit with Nonlinear PA & Pulsed.
    Receive with low-current Baseband Processor.
User Throughput Efficient
U-NII Compliant
    10 Mbps products at 5.2, 5.3, & 5.775 NOW
Demonstrated Implementations evidence at 10 Mbps.
5 GHz technology available for licensing.
Equalizer
Complexity

## Slide 3
Introduction to DPPM
Unexplored Potential for RF Applications
      “Differential Pulse-Position Modulation for Power-Efficient Optical Communcaitons”, D. Shiu & J. Kahn, University of California, Berkeley, Submitted to IEEE Transactions on Communications, August 1997.
      “Differential Overlapping Pulse-Position Modulation in Optical Direct-Detection Channel”, T. Ohtsuki et al., IEEETransactions on Communications, December 1994.
      “Capacity and Cutoff Rate for Optical Overlapping Pulse-Position Modulation Channels”, H. Shalaby et al., IEEETransactions on Communications, 1994.
      Very popular for high-speed optical communications (AWGN & Multipath Channels)
      (fiber optics, sattelite communications, IR WLANs)
Very Low RF Power Communications Candidate,
      (FCC 15.249: “Low-Power Devices”, RadioLAN Product)
DPPM has higher capacity and cutoff rate than PPM
DPPM with overlapping pulses: Ideal for Power-Limited & Bandwidth-Limited Applications
DPPM is a simple nonlinear block code
      L-binary L-tuples with unity hamming weight.

## Slide 4
DPPM Transceiver
DPPM
Encoder
Source bit
sequence
Transmitted
Chip Sequence
Pulse
Generation
Carrier
Nonlinear PA
DPPM
Decoder
Dtected bit
sequence
Detected
Chip Sequence
Filtering
Carrier
LNA
IF Carrier

## Slide 5
Power Efficient Transmission
Nonlinear Amplifier
Pulsed PA
TX Current Competitive Analysis
  Class of MMIC / Power Device
  Cost
  Complexity
    Thermal
    RF
    Mechanical / Size
Transmit Power Competitive Analysis
  Present U-NII Regulations
  After Re-Consideration

## Slide 6
Multipath Tolerance
Inter-Symbol
  Embedded Guard-Time:
    100 nsec Guard-Time is one of the “Pulse Positions”
  Pulse Processing
Intra-Symbol
  Blanking
    Blankingpost-rising-edge distortions
  Edge-Detection
Simple Detector Implementations Examples
Pulse
Slimmer
Signal
Slow
Peak Detector
Fast
Peak Detector
Ave
T/H
Baseband
Signal
Pulse
Slimmer
Signal
Peak
Detector
RSSI
(AGC)
T/H
T/H
Baseband
Signal

## Slide 7
Power Efficient Reciever
RF Receiver DC Power
  Lower Current due to Non-Coherent RF/IF Receivers
Basband Processor DC Power
Receive Baseband Current Competitive Analysis
Receive Baseband Complexity Competitive Analysis

## Slide 8
Throughput Efficiency
Single-Channel, Single Rate Efficiency
Aggregate Rate per AP, Single Rate, Indoor per Channel
  User Rate
Aggregate Rate per AP, Multi Rate, Indoor per Channel
Aggregate Rate per AP, Single Rate, Free Space per Channel
Aggregate Rate per AP, Multi Rate, Free Space per Channel

## Slide 9
DPPM Summary
Low-Cost, Low-Complexity 5 GHz PHY
  Non-Coherent
  No Equalizer (Equalizer Training & Error Propagation are fundamental problems)
  No FFT Processor
Power Efficient
  Transmit
  Receive
User Throughput Efficient
  10 Mbps Fall-back rate!
  higher data rates are possible
U-NII Compliant
  FCC-Approved 10 Mbps, U-NII products at 5.2, 5.3, & 5.775 NOW
Demonstrated Implementations evidence at 10 Mbps.
5 GHz Chip-set and technology available for licensing.

## Slide 10
DPPM
Simple
Fast
Low-Cost
A Proven Path to Product

## Slide 11
Complexity & Cost