## Slide 1
Multipath Delay-Spread Tolerance
John H. Cafarella
MICRILOR, Inc.

## Slide 2
Outline of Symbol-Based Approach
Probability of Symbol Error Conditioned On:
  Data Pattern of Symbol
  Data Pattern of Neighboring Symbols
  Code Channel Used
  Multipath Impulse Response
  Noise Samples for Symbols Involved
Use Simulation to Generate Test Statistics
Evaluate Error Probabilities Analytically

## Slide 3
WHY?
Dimensionality
  4 symbols: 106 (5 bit/symbol)
  10 Significant Paths: 1020 (100 levels each)
  48 Code Channels
  64 Noise Samples: 10128 (100 levels each)
Do Not Handle Noise By Simulation
Dimensionality Still Large (~Avogadro’s #)

## Slide 4
Generating a Test Statistic
Generate Sample Multipath Profile
  Path delay spacing Ts (minimum of 2 per TRMS)
  Path delay span 10 times TRMS
  Exponential distribution of s2 with delay
  Rayleigh amplitude, uniform phase per path
Convolve with Rx Chip-Pulse Response
Select Largest Path for Demodulation

## Slide 5
Generating a Test Statistic (cont.)
Decimate to One Sample per Chip
Generate Signal
  Select code channel
  Generate 4 or 8 symbols of 5-bit data
Convolve Signal and Chan. Impulse Resp.
Select 16 Samples for Symbol 3 or 6
Compute 16 Correlator-Output Magnitudes

## Slide 6
Statistical Averaging
Generate Sample Correlator Statistic
Evaluate PE vs. SNR
Average Results for 4K or 8K Randomizations (typical)
Full Resolution Multipath
Filtered/Decimated
Channel Matched Filter
8 Channel Symbols
16 Signal Samples
16 Correlator Outputs
Signal Data and Code Channel

## Slide 7
Probability of Symbol Error
Union Bound
  Sum of binary-orthogonal error probabilities
  Correct output vs. 15 incorrect outputs
Binary Probability of Error
  Compare correlator magnitudes
  Probability that one Rice variate exceeds another
  Procedure given in (D98/118R)

## Slide 8
Example Run
Ts/Tc=1
TRMS=5Tc (~150ns)
103 Randomizations per Curve
Irreducible Errors
  1 high
  2 none
  2 ~ average

## Slide 9
Estimation of Packet Failure Probability from Symbol Error Probability
PSE=PN (SNR,Data,TRMS)+PI (Data,TRMS)
  PI = asymptotic symbol error probability
  Thermal errors PN » PSE-PI
Thermal Symbol Errors Uncorrelated
Irreducible Errors Correlated within Packet
  PM is probability of “bad” multipath condition
  PE|M is conditional probability of symbol error
  PI=PM•PE|M

## Slide 10
Estimation of PE|M
2 of 16 Members of a Coset Likely to Cause Errors in “Bad” Multipath (D97/120)
Each Coset has 1/8 PE|M (original assumption)
One of Four Cosets (in code channel) has 1/8 PE|M

## Slide 11
What is PE|M Really?
Run Full-Packet Simulation
  64 Bytes Random Data
  One Multipath Randomization per Frame
  No Thermal Noise
Determine Packet Error Probability
Accumulate Symbol Error Statistics
  Estimate PE|M

## Slide 12
Packet Error Results
4096 Multipath Profiles per TRMS
PER 10% @ 275 ns
Use
Only 1 of 4 Cosets Hurt by Specific Multipath Profile