## Slide 1
System Capacity with Channelization
John H. Cafarella
MICRILOR, Inc.

## Slide 2
Access-Point-Location Geometries
Two Frequency Channels
Many Data-Code Channels
Three Frequency Channels
One Code
Same nearest-neighbor separation gives » same areas per AP

## Slide 3
Basic BSA Geometry
Alternate-frequency APs fall on radius 2RP
RP is “BSA Packing” Radius
STAs scattered around AP

## Slide 4
Basic BSA Geometry
Alternate-frequency APs fall on radius 2RP
RP is “BSA Packing” Radius
STAs scattered around AP
20 STAs per BSA
Randomized placement < R0
Probe performance > R0
R0 =1.2RP is Radius of nominal coverage

## Slide 5
Generation of Sample Connectivities
Generate Random Link Connectivities within BSA0
If AP Signal < Threshold+3 dB at STA
  Re-generate that link connectivity (3 tries max.)
  Emmulates fine-scale repositioning STA if poor contact
Also Compute Links Between other BSAs and BSA0
Same Local Random STA Positions Re-Used in All BSAs
  Allows use of BSA0 STA & AP parameters for All BSAs

## Slide 6
Propagation Models
Large Scale Variation
  Free-Space to 1m
  Rn beyond 1m
  n=1.5 to 4
Local Signal Fading
  None
  Rayleigh
  Three-Ray
Used: n=2.5 & Rayleigh

## Slide 7
Interaction for Different Frequencies
Interference at Short Range
Suppressed by ACI Rejection Ratio (~35 dB)
Consider Only Nearest Off-Frequency BSAs

## Slide 8
Interaction for Same Frequencies
Multiplicity of Effects
  Interference (Near/Far)
  Signal Correlations (Leakage)
Must Consider Near and Some Far BSAs

## Slide 9
Typical 3-Frequency Deployment

## Slide 10
Typical 2-Frequency Deployment

## Slide 11
Typical Link Statistics
2 frequency channels
Links more than 10-dB below Rx Threshold
Links in first 10-dB below Rx Threshold
Links in first 10-dB above Rx Threshold
Links within BSA0
Links between Off-Frequency BSAs and BSA0
Links between Off-Frequency BSAs and BSA0
20 STAs/BSA 100-dB Path Loss Tol. 35-dB ACI Rej. 2450 MHz

## Slide 12
BSA Traffic Model
STA-to-AP and AP-to-STA Only (no peer-to-peer)
20 STAs Each Offer Poisson Traffic l Frames/s
AP Offers 20 l Frames/s
1024-Bytes Frames
AP Contends with STAs (no CFI)
All BSAs Carry Same Traffic Load (by symmetry)

## Slide 13
Generalized Throughput Equations
Detailed Balance
Aggregate Queued Traffic
Average Contention Parameters
Compute Throughput
What is ?

## Slide 14
PXm for Uncorrelated Codes
For successful Exchange, Data Frame and ACK Must Get Through
STA
AP
“external” frames at STA of greater power than AP signal
“external” frame at AP of greater power than STA signal
Requires neither of these happen

## Slide 15
PXm for Single Code
STA
AP
Hidden external STAs cause interference (handle as in many-code case)
Stronger than AP signal at STA, but don’t see AP
Stronger than STA signal at AP, but don’t see STA
Good Links to STA and AP

## Slide 16
Effect of Leakage for Single Code
Include effect of queued traffic as seen by each STA individually
STA
“external” frames at STA above Rx threshold
“Internal” frames at STA

## Slide 17
Random Deployment made Worse
All Units
BSA0 Units Only
Cluster in bad corner
(4 by symmetry)

## Slide 18
Ext. STAs above Rx Threshold at AP
They can be from quite a distance!

## Slide 19
STAs 10-dB above Rx Threshold at AP

## Slide 20
Isolated BSA: Case 1
3 Frequencies
1 Code
SNRin=8dB

## Slide 21
Isolated BSA: Case 2
2 Frequencies
Many Codes
SNRin=2dB

## Slide 22
Full Network
2F/MC
3F/1C
400 kbps
400 kbps
Worst Case

## Slide 23
Random Placements
3F/1C
2F/MC

## Slide 24
Summary
Case 1
  3 Frequency Channels, Single Code, SNRin = 8 dB
Case 2
  2 Frequency Channels, Many Code Channels, SNRin = 2 dB
19 BSAs, 20 STAs + AP per BSA
Use of Code Channels Offers Greatly Improved System Throughput by Isolating Leakage
Excursions Show 2 vs. 3 Frequencies & SNRin of Less Importance