## Slide 1
WPAN Proposal TDMA-based MAC Layer
GTE Internetworking - BBN Technologies
733 Concord Avenue Cambridge, MA 02138
Rick LaRowe
617-873-2193 (rlarowe@bbn.com)
I N T E R N E T W O R K I N G
POWERED BY BBN

## Slide 2
Introduction / Overview
This is not a proposal for a specific solution, but rather a general approach.
The general approach is backed up by a POCD, as well as forthcoming solutions.
Overview:
  Requirements
  Keys to success
  Benefits / Issues
  Possibilities

## Slide 3
Requirements
Driving requirements include:
  Very low power consumption
  Very small devices (including peripherals, sensors, etc.)
  Easy integration into devices (minimal SW)
  Wireless, no line-of-sight limitation, networks
  Cross-network interference tolerance
Simplifying characteristics include:
  Data rate requirement is relatively low
  Range is very short

## Slide 4
Keys to Success
Keep transceiver OFF
  Duty-cycling is key to reducing average current
  Receiver consumes as much as transmitter (approximately) in the PAN environment
Keep the MAC simple
  Simplicity lends itself to small finite-state machines, running at slow clock rates
  Few gates, clocked slowly, yields target result

## Slide 5
TDMA meets objectives
Time Division Multiple Access
  Devices KNOW when to receive and when to transmit AND when they can turn OFF
  No need for higher-order timing overlay, as in 802.11, to accomplish this primary goal.
TDMA structure defines an operational sequence easily implemented as a finite state machine.
Byte-oriented TDMA structure lends itself to a slow-clocking MAC implementation.

## Slide 6
Common TDMA Fallacies
Fallacy: “TDMA, which requires a Hub, cannot support ad hoc, peer-to-peer networks.”
Truth: As long as any device can operate as Hub, and devices can determine when to become a Hub, this is not an issue.
Fallacy: “TDMA is inefficient in its usage of bandwidth, due to slots unused by assignee.”
Truth: Dynamic allocation can be used for highly efficient assignment of bandwidth.

## Slide 7
Example TDMA Structure
High-level structure includes five components:
Embedded sliding window, bandwidth allocation

## Slide 8
Cross-Network Interference
Time-Based Spreading
  Bursts can be spaced according to code patterns as in a CDMA system, but not for the same reason
  Optical Orthogonal Coding used in BodyLAN
Frequency Agility
Frequency Hopping maps well to TDMA structure
Direct sequence spread spectrum can also be applied to a TDMA-based MAC.

## Slide 9
Example Low-Level TDMA
Interference tolerance, FEC, power efficiency
1 Second = approximately 66 TDMA Frames
1 TDMA Frame = 73 OOC Windows
1 Event Slot = 8 Symbol Slots
First 2 OOC
Windows used
for Beacon
1 OOC Window = 13 Event Slots
3 bursts per window, one data byte

## Slide 10
Dynamic Attachment
Devices desiring to join an existing network can listen for beacons, establish synchronization.
Attachment can proceed via Slotted Aloha embedded within the same TDMA structure.
  Hub can dictate how much bandwidth allocated to the support of attaching devices
  Attaching devices do not interfere with operational ones
Assorted mechanisms can be used to direct attachment to the desired networks.

## Slide 11
Example Numbers
BodyLAN base numbers:
  Active digital (MAC Layer): 100mA (few gates, clocked very slowly)
  RF transceiver: 130mA - 2.7mA - 14mA (base-level current, stand-by, transmit/receive)
BodyLAN, full data rate Hub: 5.4mA average
BodyLAN, half data rate device: 2.8mA average
Staying attached without sleeping: 790mA