## Slide 1
May 1998
Slide 1
Pat Kinney, Intermec Technologies
Proposal for a Wireless Personal Area Network Medium Access Control and Physical Layer
Pat Kinney Intermec Technologies Corporation 550 Second St S.E., Cedar Rapids, IA Phone: (319) 369-3593 Fax: (319) 369-3299 e-Mail: kinneypw@norand.com

## Slide 2
May 1998
Slide 2
Pat Kinney, Intermec Technologies
Introduction
Typical applications such as the mobile worker and Physiological Monitoring involve short messages and short distances between devices. Key attributes for these devices include:
low cost
small size
low current drain
minimal operator intervention
Notes: May 1998
Page 2
Pat Kinney, Intermec Technologies
doc.: IEEE 802.11-98/xxx

## Slide 3
May 1998
Slide 3
Pat Kinney, Intermec Technologies
Features
Dynamic addressing: allows the network to be intiated and maintained with minimal operator intervention
Temporary network: allows a device to temporarily split from its PAN, attach to a non-PAN device, detach from that device and resume participation in the original PAN

## Slide 4
Sample Configuration
Personal
Area
Network
PC Based Work Station
Barcode and Receipt Printers
WAN Radio
Scanner
Pen-based HHC
Slide 4
Pat Kinney, Intermec Technologies

## Slide 5
May 1998
Slide 5
Pat Kinney, Intermec Technologies
Cost
One of the major drivers behind WPAN is the lowest possible cost. Cost is typically driven by complexity and high performance requirements. The design philosophy behind this proposal is a system design with relaxed requirements on hardware cost drivers and which leverages existing technology and componentry where possible for the lowest recurring costs.

## Slide 6
May 1998
Slide 6
Pat Kinney, Intermec Technologies
Cost
MAC greatly simplifies requirements on RF design
  SIFS/DIFS/PIFS are greatly relaxed, etc.
Low MAC S/W overhead (estimate 25% of 802.11)
Low MAC/PHY gate count (estimate 10% 802.11)
Single conversion receiver
Direct launch VCO

## Slide 7
Power Consumption
Minimal MAC complexity allows:
  reduced ASIC current drain
  reduced microprocessor on time
Minimal transceiver performance requirements allow:
  reduced active componentry
Above results in less than 6 mA current drain @ 3.3V for connection maintaince
Slide 7
Pat Kinney, Intermec Technologies

## Slide 8
May 1998
Slide 8
Pat Kinney, Intermec Technologies
Coexistence
It’s essential that these devices operate satisfactorily in congested spectral environments. The proposal is for CSMA/CA protocol, Frequency Hopping, with a high speed aggregate data rate to aid in Coexistence with:
  20 other co-located PAN networks
  WLAN FH networks

## Slide 9
May 1998
Slide 9
Pat Kinney, Intermec Technologies
Range
The majority of requirements for PANs are met with a maximum range of 10 meters. Intermec Technolgies’ implementation of this proposal has a demonstrated range of greater than 10 meters as verified in a cubicle environment and in shipping and receiving areas.

## Slide 10
May 1998
Slide 10
Pat Kinney, Intermec Technologies
Regulatory
Worldwide
  US: Part 15.249
  Europe: ETS 300 328
  Japan: RCR 33

## Slide 11
May 1998
Slide 11
Pat Kinney, Intermec Technologies
Hardware
2.4 GHz operation
  world wide regulatory
  reduced non-desired emissions from host device
  wide bandwidths allow simple high speed modulation/demodulation methods
  low cost componentry from PCS and WLAN products

## Slide 12
May 1998
Slide 12
Pat Kinney, Intermec Technologies
Hardware
Frequency Hopping
  world wide regulatory as spread spectrum
  low cost, low current drain, spread spectrum technique
  interference immunity from narrow band sources
  allows a simplified strategy of coexistence in a congested area

## Slide 13
May 1998
Slide 13
Pat Kinney, Intermec Technologies
Hardware
Low transmit power: <1 mW
  low current drain
  complimentary to an effective coexistence strategy
  allows submission under FCC 15.249 (no hop sequence constraints)
  low device count
  reduced consumer concerns about safety

## Slide 14
May 1998
Slide 14
Pat Kinney, Intermec Technologies
Hardware
1 Mb/s aggregate data rate
  more effective coexistence strategy due to reduced transmit durations
  reduced average current drain
  reduced response times yield reduced host current drain

## Slide 15
Protocol Requirements
Support Functional Requirements in CFP (except only 10 stations)
Support Power Management
Support Auto Configuration
Support Temporarily Split Networks
Slide 15
Pat Kinney, Intermec Technologies
Notes: Page 13

## Slide 16
Basic Protocols
Initialization
Normal Operation
Termination
Slide 16
Pat Kinney, Intermec Technologies
Notes: Page 14

## Slide 17
Initialization Protocol
One Station is “coordinator”
Others “join”
Coordinator broadcasts inits
Others unicast attaches
Coordinator accepts or declines
When all expected stations attach, coordinator starts normal operations
Slide 17
Pat Kinney, Intermec Technologies
Notes: Page 15

## Slide 18
Normal Operation Protocol
Coordinator periodically broadcast synchronization information (beacons)
After beacons, stations transmit to powered down stations by requesting other stations to leave receiver on, and after a short interval sending to that station
Stations transmit to powered up stations at any time
Slide 18
Pat Kinney, Intermec Technologies
Notes: Page 16

## Slide 19
Termination Protocol
Coordinator broadcast (after beacons) termination notification
This is repeated several times
Slide 19
Pat Kinney, Intermec Technologies
Notes: Page 17

## Slide 20
Medium Access Control (MAC)
CSMA/CA
P-persistent with reservations (the reservation is similar to that in 802.11)
Unicast frames all have an immediate response from recipient
Slide 20
Pat Kinney, Intermec Technologies
Notes: Page 18

## Slide 21
Frame Sequences: Initiation
Init Broadcast
Attach Req
Attach Rsp
Init
Interval
Init Broadcast
Start Broadcast
Init
Interval
Beacon
Slide 21
Pat Kinney, Intermec Technologies
Notes: Page 19

## Slide 22
Frame Seq’s:Normal Op Send to Powered Down Sta
Beacon
RFP Win
Dwell
RFP
Dwell
Poll
RFP
Poll
Data
Clr
B
e
a
c
o
n
I
n
t
Slide 22
Pat Kinney, Intermec Technologies
Notes: Page 20

## Slide 23
Frame Seq’s:Normal Op Send to Powered Up Sta
Beacon
RFP Win
Dwell
Dwell
RFP
Poll
Data
Clr
B
e
a
c
o
n
I
n
t
Slide 23
Pat Kinney, Intermec Technologies
Notes: Page 21

## Slide 24
May 1998
Slide 24
Pat Kinney, Intermec Technologies
Differences from CFP
10 vs 16 nodes per network
  this number is arbitrary
Currently at 1.5 cubic inches
  shape factor dictated by host device

## Slide 25
May 1998
Slide 25
Pat Kinney, Intermec Technologies
Summary
Dynamic: self initiating, self contained network
Cost: minimal cost, low relative to host
Power Consumption: less than 20 mW for connection maintenance
Coexistence: both WLAN networks and PAN networks
Range: greater than 10 meters in cubicle environment