## Slide 1
WPAN Study Group Is 802.11 the Answer? Topics for Discussion
Rick LaRowe
GTE Internetworking - BBN Technologies
617-873-2193 (rlarowe@bbn.com)

## Slide 2
Introduction / Overview
Statement of perceived WPAN requirements
Summary of requirements clearly / easily satisfied by the 802.11 standard
Summary of 802.11 capabilities simply not required by the WPAN technology
Discussion of the overlap
  Is the basic 802.11 MAC/PHY appropriate for WPAN?
  Are there parts that should be exploited? Avoided?

## Slide 3
Technical Guidelines
From April 8-9, 1998 Cambridge, MA meeting:
Mobility: 0-10 mph (no handoff required)
Range: 0-10 meters
Data rate at MAC SAP: 19.2 - 100 kbps
WPAN Coexistence: 20 within 400 square feet
Coexistence with other wireless systems (e.g., 802.11)
Networking support for minimum 16 devices
Bridge or Gateway connectivity to other networks

## Slide 4
Additional Guidelines
Other requirements we know we must satisfy:
Very low power solutions feasible
Very small solutions feasible
Low c--- solutions feasible (can I use the “c” word?)
Solutions with minimal interfaces feasible
  simple hardware and software interface assumptions
  necessary to interface to the simplest peripherals and sensors
Not infrastructure-based networks

## Slide 5
802.11 and Technical Guidelines
Can 802.11 satisfy the 4/8-9/98 guidelines?
Mobility: 0-10 mph (no handoff required) YES
Range: 0-10 meters YES
Data rate at MAC SAP: 19.2 - 100 kbps YES
WPAN Coexistence: 20 within 400 square feet ????? PHY dependent, FHSS more likely, with minimal transmit power
Coexistence with other wireless systems YES
Networking support for minimum 16 devices YES
Bridge or Gateway connectivity to other networks YES

## Slide 6
802.11 and Additional Guidelines
Can 802.11 satisfy our additional guidelines?
Very low power solutions feasible DEPENDS
Very small solutions feasible DEPENDS
Low c--- solutions feasible DEPENDS
Solutions with minimal interfaces feasible NOT YET
Not infrastructure-based networks YES
It’s the DEPENDS items that are the issue. Today solutions don’t satisfy what many want, ultimately the could. But of course, simpler solutions would be even better by then.

## Slide 7
“Extra” 802.11 Requirements
802.11 meets requirements WPANs do not have:
Roaming
WEP (Wired Equivalent Privacy) hooks might be nice
MAC-level fragmentation? might be nice, but as a requirement could be unwise

## Slide 8
802.11 and WPAN
If we were to use 802.11 for a WPAN, we’d need:
Hidden node mechanisms, since CSMA based MAC makes this critical for basic operation.
Synchronization mechanisms (TSF Timers, beacons)
Power management (TIM, DTIM, sleep, etc.)
Independent BSS support for distributed power management, since WPAN has no infrastructure
Association / Scanning mechanisms for IBSS (network) formation and management

## Slide 9
Observations
Power control is absolutely critical to WPAN
802.11 does power control via beacons, coordinated sleep, and TIM/DTIM messages layered on top of base CSMA/CA protocol.
This is TDMA on top of CSMA.
In fact, time-bounded services (CFS) and many of the performance optimizations in the standard are based on the use of TDMA-like structures layered on top of the CSMA foundation.
Argument: This TDMA-on-CSMA is one of the reasons 802.11 is considered complex by many.

## Slide 10
Opinion to Start Discussion
802.11 could certainly be used to satisfy the base technical requirements for WPAN identified at 4/8-9/98 Cambridge meeting.
Technology will drive down power, size, c--- of 802.11 products. BUT …
Much simpler approaches can be applied to the specific WPAN requirements to directly attack the problem.
Technology will drive down the power, size, c--- of those solutions as well, to even lower points.

## Slide 11
Final Comment
Remember:
The fact that I can build a calculator with a Pentium and Windows 95 doesn’t mean that I should.
Even if the power consumption of Pentiums is coming down every year.