## Slide 1
Spontaneous Proximity Networking with Piano-enabled Devices
Richard Ditch
Motorola
Future System Platforms
p26658@email.sps.mot.com
Notes: #
#

## Slide 2
What is Piano?
Motorola code name for short-range spontaneous wireless network
Based on short-range wireless medium
Networks are transient, formed as needed when devices come into proximity
Peer-to-peer without a designated controller
Supports but does not require a connection to the internet/intranet

## Slide 3
The Motorola Vision for Piano
A future in which many electronic devices (enabled with Piano) are:
  aware of other nearby Piano-enabled devices
  have the capability of communicating with other discovered Piano-enabled devices
  automatically exchange basic information about fundamental capabilities
  establish temporary wireless networks, as appropriate

## Slide 4
Piano-Enabled Public Applications
Context /Location-specific triggers
Kiosks - printing, information transfer
Queue reduction - hotel, theater, restaurant
Universal User Interface - thin servers
E-commerce
Matchmaker services
Notes: Locations: office, home, restaurant, theatre, hotel, airport, shopping mall
Context examples:
UUI - thin server:

## Slide 5
Principal Features of Piano Networking
Short-range wireless medium
Peer-to-peer device discovery
Peer-to-peer service discovery
  User oriented service description
  Device oriented service description
Client distribution for discovered services
Peer-to-peer authentication/authorization

## Slide 6
Short-range Wireless Medium
Omni-directional – permits hidden, automatic operation (I.e., briefcase computing)
Low power consumption – permits small size, portable operation
Limited range – frequency sharing through spacial isolation
Low-cost – enables ubiquity
Wire equivalent privacy – protection from eavesdropping and spoofing

## Slide 7
Peer-to-peer Device Discovery
Each device can detect and communicate with all nearby devices.
Devices operate as peers without the use of a central controller.
Devices can begin communicating without device-specific configuration or human interaction.
Device associations are temporary.

## Slide 8
Peer-to-peer Service Discovery
Enables users to see available services
  provides enough information for user to decide if further interaction is desired
Enables devices to automatically utilize recognized services
Provides information on service protocols and connection parameters
  sufficient to establish a session with the service
Distributed naming of services

## Slide 9
Service Discovery (continued)
Service naming separate from device naming
Service grouping and categorization
Asynchronous notification when a requested service enters proximity
Protocol support for caching of service attributes
Incremental discovery based on authentication/authorization

## Slide 10
Client Distribution for Discovered Services
Enables service-specific user interfaces for multiple services without pre-configuring a client for each service
Enables a service-specific user interface for newly encountered services
Clients may be downloaded on demand from the internet/intranet, from the server offering the service, or may be pre-loaded

## Slide 11
Summary
The Motorola Piano team has focused on the “things you come near” aspect of short-range wireless networking (I.e., Personal Operating Space)
Piano Goal: work within Bluetooth and the IEEE to standardize the Egalitarian, ad hoc networking protocols and Application Programming Interfaces.