## Slide 1: Outline of Draft Standard for 5 GHz
Hitoshi Takanashi, Masahiro Morikura, Richard van Nee
Lucent + NTT

## Slide 2: Advantages of OFDM
Robust against delay spread
No feed back loop : stable
Any modulation schemes can be applied to the base band modulation. Same spectrum shape is found.
Fall back function is supported
Same PHY as BRAN’s would be possible

## Slide 3: Configuration of PHY
Modulation in Base band

## Slide 4: OFDM Parameters
48 sub-carriers in 12.5 MHz
Center carrier is not used
64 points of FFT/IFFT
Base band modulation :
  DPSK, DQPSK and 16QAM
5 carriers in 100 MHz (15 MHz separation)

## Slide 5: Sub-carrier Allocation
The center carrier interfered by the DC offset is not used.

## Slide 6: Base band Modulation
DBPSK and DQPSK
  Differential coding for differential detection
  DBPSK, r=1/2 : 5 Mbit/s
  DQPSK, r=1/2 : 10 Mbit/s
  DQPSK, r=3/4 : 15 Mbit/s
  Pilot carriers (#3, 26 and 47)
16 QAM
  Pilot carriers (#3, 26 and 47)
  r=1/2 : 20 Mbit/s
  r=3/4 : 30 Mbit/s

## Slide 7: Channelization in L & M band
10 carriers in 200 MHz band
Guard band : 13.875 MHz to the band edge
15 MHz separation

## Slide 8: Channelization in Upper band
Same as lower / middle band

## Slide 9: Header Parameters
Long Guard Interval is secured

## Slide 10: Cyclic Extention
A raised cosine window to reduce out band power (roll off factor : 0.025)
Ts=T+TG
 T
T
Tpostfix
Tprefix

## Slide 11: Training Symbols
Short and Long symbols

## Slide 12: Encoder
64 states convolutional encoder
rate : 1/2 - 3/4 (punctured)

## Slide 13: Bit stealing/insertion

## Slide 14: Layer Reference Model
As used in the current MAC
New Primitive parameters are defined

## Slide 15: PLCP Frame Format

## Slide 16: Other Functions
Bit stuff to make the MPDU length multiples of an OFDM symbol.
Tail bits to set the convolutional encoder to a state.
Scrambler to minimize the data DC offset.
Interleave to enhance error correction function (within an OFDM symbol)