## Slide 1
WPAN Applications
Steve Shellhammer Symbol Technologies, Inc. shell@symbol.com

## Slide 2
List of Possible Applications
Current Applications
  Cordless Scanners
  Cordless Printing
Future Applications
  Interconnection of multiple wearable or hand-held devices
  File transfer between several PDAs or portable terminals

## Slide 3
Cordless Scanners
A cordless connection is used as a “cable eliminator” to allow the user to wander around his work area.
Point-to-point operation.
One-way communication with an acknowledgment.
Range up to 100 feet required.

## Slide 4
Cordless Scanners
Limited data rate required - 19.2 Kbps
10 to 15 characters every second at most.
Scanners can be associated by scanning a bar code on the receiver.
Scanners do not associate with a base automatically.
Latency of 200 ms is okay. We give audible feedback before transmitting.

## Slide 5
Cordless Scanners
The scanner has to coexist peacefully in many possible RF environments.
  900 MHz Wireless LANs
  2.4 GHz Wireless LANs
  Several other cordless scanners in the area.
  Cordless phones, etc.
Low power: 30 ma at 3 volts.
Small size: 0.25 inch2 to 1 inch2

## Slide 6
Cordless Printing
In either a hand-held or wearable terminal we need to form a cordless connection to either a belt worn or fixed mounted printer.
Point-to-point operation.
One way communication with an acknowledgment.
Range of about 20 feet required.

## Slide 7
Cordless Printing
Limited data rate required - 19.2 Kbps
100 - 1000 characters every 3 seconds.
Terminal can be associated by scanning a bar code on the printer.
Terminals do not associate with a base automatically.
Latency of 200 ms is okay.

## Slide 8
Cordless Printing
The terminal & printer have to coexist peacefully in many possible RF environments.
  900 MHz Wireless LANs
  2.4 GHz Wireless LANs
  Several other cordless terminals in the area.
  Cordless phones, etc.
Low power: 30 ma at 3 volts.
Small size: 1 inch2

## Slide 9
Connecting Multiple Devices
Connect
  Hand-held or belt-worn terminal
  Scanner
  Printer
  Wrist I/O unit
Terminal acts as the master and the other devices are the slaves.
10 to 15 feet of range required

## Slide 10
Connecting Multiple Devices
Scanner transmits bar code data to the terminal.
Terminal sends bar code label information to the printer.
Terminal sends display information to the wrist I/O unit.
Keyboard information is sent from wrist I/O unit to terminal.

## Slide 11
Connecting Multiple Devices
Terminal may likely also contain an IEEE 802.11 radio.
The terminal receives message from host over 802.ll WLAN.
The two radios inside the terminal need to coexist peacefully.

## Slide 12
Connecting Multiple Devices
One form of association is for the scanner to scan a bar code on the terminal and then scan bar codes on the other peripherals.
Low power: 30 ma at 3 volts.
Small size: 0.25 inch2 to 1 inch2

## Slide 13
File transfer between PDAs
Two people with PDAs, portable terminals, or laptop computers, meet in any location and want to be able to exchange files.
Data rate as low as 19.2 Kbps for PDA type applications to 1 Mbps for laptop type applications (i.e. larger files).
Association initiated by one of the users and accepted by the other user.

## Slide 14
File transfer between PDAs
Point-to-point communication.
10 to 20 feet of range is fine.
Latency is not an issue. Total file transfer time is concern.
Any possible interference since you could be anywhere.
Low power: 30 ma at 3 volts.
Small size: 0.25 inch2 to 1 inch2

## Slide 15
Sharing information in a meeting
Multiple users (2 ~ 20 people) attend a meeting and one person would like to be able to broadcast a file to all the users in the room.
A good example of this is the IEEE 802.11 meetings. (In that case the number of users could be much higher).

## Slide 16
Sharing information in a meeting
The master broadcasts to the slaves.
The master could change since different people may want to transmit a file at different times.
Association should be initiated automatically when you are in the area.
The user accepts association with the network.

## Slide 17
Sharing information in a meeting
Data rates as high as 1 Mbps would be useful if the files are large.
Latency is not an issue. Total file transfer time is concern.
Any possible interference, since you could be anywhere.
Low power: 30 ma at 3 volts.
Small size: 0.25 inch2 to 1 inch2

## Slide 18
Broadcast Information for People Entering a Location
When a user, who is carrying a PDA, enters a location (e.g. store or office room), he receives messages.
Association is automatic.
Some information is passed in the association request signal.
User accepts association either manually, or for some applications, automatically.

## Slide 19
Broadcast Information for People Entering a Location
Master-slave configuration, with fixed transmitter acting as master, and the users with their PDAs, being slaves.
Information (e.g. advertising) is broadcast.
Users can act on the information.
Latency is not a major issue.
Message sizes are likely under 1 Kbytes.

## Slide 20
Broadcast Information for People Entering a Location
19.2 Kbps is probably fine.
Interference could include WLAN and cordless phones.
Low power: 30 ma at 3 volts.
Small size: 0.25 inch2 to 1 inch2