## Slide 1
WPAN CFA
Harshal Chhaya
Texas Instruments
hchhaya@ti.com

## Slide 2
Application Scenario for WPAN
Network of personal computing devices in a classroom environment

## Slide 3
Need for a New Standard
A classroom network:
  does not need range (typical range < 10m)
  does not need ad-hoc networking (has well defined network control)
  does not need support for telephony
  does not need roaming/hand-off between networks
all of which are part of LAN stds and add
complexity, cost, power

## Slide 4
System Characteristics
Characteristics of the educational network environment
  1. There is a teacher (control)
  2. A concentrated set of nodes
  3. Nearby cells (classrooms)
  4. Moderate high bandwidth
  5. Very cost sensitive
  6. Long battery life (24 hrs)
  7. Data reliability/premium on usability/self-correcting/redundancy

## Slide 5
Well-defined Control (Teacher)
One primary controller
No peer-peer communication
Teacher
(controller)
Students
(portable units)

## Slide 6
Concentrated Set of Nodes
Typical classroom
  30 (school) - 128 (college) students in a room
  Maximum distance from teacher < 15m
  Distance between students (nodes) ~ 1 m

## Slide 8
Adjacent Networks
Adjoining classrooms create co-located networks
Neighboring networks should not interfere
Implies limited communication range for hand-held units

## Slide 10
Moderately High Bandwidth
Desired: 1-2 Mbps
Data types:
  Bulk transfers (broadcast)
  Multimedia streams
  Interactive sessions

## Slide 11
Very Cost Sensitive
Network devices are PDAs, calculators, data loggers etc.
Cost: US$ 100-200
The price premium for networking cannot exceed 20% of the cost of the endpoint devices

## Slide 12
Strict Power Requirements
Devices are battery powered
Peak power drain: 100 ma @ 3V
The network and endpoint devices must be capable of continuous uninterrupted operation for an entire working day

## Slide 13
Network Reliability
An unreliable network is unusable - too disruptive
Worst case should be a slow down

## Slide 14
System Features
Network should be scalable from classrooms (~30 students) to lecture halls (~100 students)
Should support outdoor networking (field trips etc.)
Presence of minimal emitters - data loggers, pointing devices etc.
Various classroom cells connected via (wired?) School LAN

## Slide 15
PHY Considerations
IR
  Pluses
    Negligible interference with other consumer devices
    Cheap
    Physically contained
    No regulatory constraints (no EMI issues)
  Minuses
    Line of sight propagation
    Degradation in direct sunlight

## Slide 16
PHY Considerations
RF
  Pluses
    Not line-of-sight
    Variety of vendors/technologies
  Minuses
    Interference with adjacent cells (classes)
    Regulatory constraints

## Slide 17
PHY Considerations
No clear choice!

## Slide 18
MAC Characteristics
Fair: access to network should be position independent
Power efficient: a battery life of 8-12 hrs, ideally more
Support for bulk transfers, isochronous and asynchronous data
Cheap to implement: network devices are not computationally powerful

## Slide 19
Theory of Operation
Devices within controller’s sphere of influence can join the network
Once “logged in”, they use the network to transfer data
Mechanics of data-transfer are MAC-dependant
Network devices can access other networks (school LAN, Internet) via the controller

## Slide 20
Theory of Operation (Contd.)
Adjacent networks (cells) should not interfere
Their controllers may communicate via another network (school LAN)

## Slide 21
Why Is This Interesting?
Completely untapped market
~ 10 million communications capable hand-held devices in schools
Solve the “last 10 m” problem
Allow access to vast resources on the Internet
Support NSF initiatives
Socially relevant

## Slide 22
WPAN application: Classroom network
Comments/Questions?