## Slide 1
The CCK 11 MBps Modulation for IEEE 802.11 2.4 GHz WLANs
Mark Webster and Carl Andren Harris Semiconductor
With support from:
Jan Boer and Richard van Nee Lucent Technologies
Notes: A new modulation scheme has been adopted by the IEEE 802.11 standards committee to implement Wireless Local Area Networks (WLANs) that will provide 1 to 11 MBps rates in the 2.4 GHz ISM band. This scheme will provide interoperability with the 802.11 DS equipment operating at 1 and 2 MBps and also offer rates of 5.5 and 11 MBps for those users that need more speed. This paper discusses the new modulation scheme and the considerations that led to the adoption of this technique for the standard.

## Slide 2
Summary
CCK modulation will enable 11 MBps operation in the 2.4 GHz ISM band
An interoperable preamble and a short preamble will allow both interoperability and co-existence with low rate LANs
Notes: Harris has built chips on the MBOK waveform and extensively tested them in the lab and field. Several commercial applications have been tested and are ready to be fielded. Based on this performance and the simulations that show the CCK waveform to be superior, we are embarking on the development of chips to embrace the CCK waveform as well. We are also working on the design of the fully equalized version for introduction early to mid next year.
We thank Lucent Technologies for the extensive help in the definition and simulation of the CCK waveform and their help in getting it adopted in the IEEE 802.11 high speed 2.4 GHz PHY standards group. We look forewords to rapid development of the standard so that the market can enjoy Ethernet line speeds in the indoor wireless LAN arena.

## Slide 3
Preamble Length
Our basic approach is to include the standard DS or FH 802.11 preamble and header
This length includes ample time to do diversity and equalization
For the cases where interoperability is not an issue, a short, high rate header can be used.
Antenna diversity, WEP initialization and equalizer training require a somewhat longer short preamble than the shortest possible.
Notes: The long, interoperable preamble and header allows ample time to do AGC, diversity selection WEP engine initialization, and equalizer training along with the normal modem acquisition processing. In the event a shorter preamble and header is desired for maximizing throughput, it must take into account those extra times.

## Slide 4
PLCP Preamble
MPDU
144 bits
SYNC
SFD
16 bits
SIGNAL
8 bits
8 bits
16 bits
LENGTH
CRC
128bits
SERVICE
PPDU
PLCP Header
48 bits
16 bits
SCRAMBLED
ONES
1 MBPS
DBPSK
BARKER
1 DBPSK BARKER
2 DQPSK BARKER
5.5 or 11 Mbps CCK
PACKET WITH LONG PREAMBLE
192 us

## Slide 5
shortPLCP Preamble
MPDU
72 bits @ 1 Mbit/s
shortSYNC
shortSFD
16 bits
SIGNAL
8 bits
8 bits
16 bits
LENGTH
CRC
56 bits
SERVICE
PPDU
PLCP Header
48 bits @ 5.5 Mbit/s
16 bits
variable @ 5.5 or 11 Mbit/s
SCRAMBLED
ZEROS
BACKWARDS
SFD
DBPSK BARKER
5.5 Mbps CCK
PACKET WITH SHORT PREAMBLE
80.7 us

## Slide 6
No
Hit
Ant A
No
Hit
Ant B
Hit
Ant A
Hit
Ant B
Hit
Ant A
AGC
Ant B
AGC
Ant A
CIR & Freq
Estimate
Ant B
CIR & Freq
Estimate
Ant A
SFD
Switch Ant.
&
SFD Search
MPDU
TAIL
0 5 10 15 20 25 30 35 40 45 50 55 60
CCA
SLOT k
CCA
SLOT k+1
AGC LOCK
ON ANT B
AGC LOCK
ON ANT A
SYNC
mSEC:
56 mSec
ANTENNA
SELECT
ANTENNA DIVERSITY: SIGNAL PRESENT AT BOTH ANTENNAS
SHORT PREAMBLE TIME LINE
SWITCH DUE
TO TRANSPORT
LAG
CCA
SLOT k+2

## Slide 7
No
Hit
Ant A
No
Hit
Ant B
Hit
Ant A
No
Hit
Ant B
Hit
Ant A
AGC
Ant A
CIR & Freq
Estimate
Ant A
SFD
SFD Search
MPDU
TAIL
0 5 10 15 20 25 30 35 40 45 50 55 60
AGC LOCK
ON ANT A
SYNC
mSEC:
56 mSec
ANTENNA DIVERSITY: SIGNAL FADED ON ANTENNA B
SHORT PREAMBLE TIME LINE
No
Hit
Ant B
SWITCH DUE
TO TRANSPORT
LAG
CCA
SLOT k
CCA
SLOT k+1
CCA
SLOT k+2

## Slide 8
SHORT PREAMBLE PERFORMANCE
SIMULATION PARAMETERS
FREQ OFFSET: 50 PPM
STATE: Linear (AGC locked)
TIME SPAN: 10 msec of Sync
SAMPLE RATE: 2 per Chip
CIR ESTIMATES: 11 Chip
CMF: Used CIR estimate
64 BYTE PACKETS (Equalized RAKE)
DELAY SPREAD @ 10% PER: 350 nsec
Eb/No @ 20% PER with 350 nsec: 15.5 dB
MPDU
SYNC
JAM CIR ESTIMATE
AND FREQ OFFSET
PACKET-ERROR-RATE
SIMULATION
PREAMBLE
SIMULATION
10 mSec
SYNC
AGC
SIMULATION
10 mSec
AGC
LOCK

## Slide 10
FH Interoperability Preamble
MPDU
PPDU
Short PLCP
120 BITS
GAP
FH PLCP Preamble
96 bits
FH SYNC
FH SFD
16 bits
PLW
12 bits
4 bits
CRC
80 bits
PSF
FH PLCP Header
32 bits
16 bits
128 us

## Slide 11
Signal Field
The 8 bit 802.11 Signal Field indicates to the PHY the modulation which shall be used for transmission (and reception) of the MPDU. The data rate shall be equal to the Signal Field value multiplied by 100kbit/s. The extended DSSS PHY supports four mandatory modulation services given by the following 8 bit words, where the LSB shall be transmitted first in time:
  0Ah (MSB to LSB) for 1 Mbit/s DBPSK
  14h (MSB to LSB) for 2 Mbit/s DQPSK
  37h (MSB to LSB) for 5.5 Mbit/s CCK
  6Eh (MSB to LSB) for 11 Mbit/s CCK

## Slide 12
Length Field
Since there is an ambiguity in the number of octets that will be described by a length in microseconds for any data rate over 8 Mbit/s, an extra bit will be placed in the service field to indicate when the smaller potential number is correct.
5.5Mbit/s CCK Length = #octets * 8/5.5, rounded up to the next integer.
11Mbit/s CCK Length = #octets * 8/11 , rounded up to the next integer and the service field LSB bit shall indicate a ‘0’ if the rounding took less than 8/11 or a ‘1’ if the rounding took more than 8/11.
At the receiver, the number of octets in the MPDU is calculated as follows:
5.5Mbit/s CCK #octets = Length * 5.5/8, rounded down to the next integer
11Mbit/s CCK #octets = Length * 11/8 , rounded down to the next integer, minus 1 if the service field LSB bit is a ‘1’.

## Slide 13
FH PSF Field
The first bit (#0) of the PSF which is reserved in clause 14.3.2.2.2 will be used to indicate that a high rate transmission will
follow. This bit is nominally 0 for transmissions compliant to the clause 14 standards. When raised to a 1, it will signal that
a high rate short preamble will follow. The remainder of the bits will indicate the rate which should be used to calculate the
end of the packet. Table shows the rate mapping of the PSF bits.
b0
b1
b2
b3
Indicated rate
0
X
X
X
Rates 1 - 4.5 Mbps per existing text
1
0
0
0
5.5 Mbps
1
0
0
1
11 Mbps
1
0
1
0
16.5 Mbps
1
0
1
1
22 Mbps
1
1
0
0
27.5 Mbps
1
1
0
1
33 Mbps
1
1
1
0
38.5 Mbps
1
1
1
1
44 Mbps

## Slide 14
11 Bit Barker Word
22 MHz
11 MBps
CCK
5.5 MBps
CCK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS BPSK
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit used to
BPSK code word
11 chips
1 MSps
2 bits used to
QPSK code word
8 chips
1.375 MSps
2 bits encoded to
4 complex code
words; 2-QPSK
8 chips
1.375 MSps
I, Q
I, Q
I, Q
Modulation Technique and Data rates
I, Q
6 bits encoded to
64 complex code
words; 2-QPSK
Code set
Notes: The Harris/Lucent suggested high rate modulation is a form of M-ary Orthogonal keying to be known as Complementary Code Keying (CCK). We propose that two Quadrature forms of this modulation be used to provide multiple rates for stressed links.
For the 5.5 MBps CCK mode, the incoming data is grouped into 4 bit nibbles where 2 of those bits select the spreading function out of the set of 4 while the remaining 2 bits bit set the QPSK polarity of the symbol. The spreading sequence chosen then QPSK modulates the carrier by driving the I and Q modulators. To make 11 MBps CCK modulation, the input data is grouped into 2 bits and 6 bits. The 6 bits are used to pick one of 64 complex vectors of 8 chip length and the other 2 bits DQPSK modulate the whole symbol.

## Slide 15
CODE DIMENSIONALITY
8 QPSK CHIPS: 4^8 = 65536 CCK Code words
64 CCK Code words are selected for maximum distance properties with 4 rotations
Notes: This shows how the two modulations schemes compare. For the MBOK mode, there are 8 BPSK chips that have a maximum vector space of 256 code words of which you can find sets of 8 that are orthogonal. For the CCK modes, there are 65536 possible code words, of which you can find sets of 64 that are orthogonal.

## Slide 16
DIFFERENTIAL-PHASE MODULATION
Code word
Select Bits
Differential-
Phase Bits
CODE WORD
TABLE
Code word
rotate
Code words
PHASE
MAP
Quadri-phase
Previous-phase
Like 1 and 2 Mbps
Noncoherent Rcvr Enabled
Notes: The original MBOK waveform used both I and Q channels independently and that required that the system process the signal coherently with an absolute phase knowledge. This is not a large concern as the preamble and header can supply the necessary means to lock up a PLL in a given state and the actual demodulated header can resolve the phase ambiguity. This and the parallel correlators for the demodulation moderately increase the complexity of the demodulator. The CCK waveform, having the I and Q channels coupled, allows the use of differential coding, which can in turn, allow simpler, non-coherent, demodulation.

## Slide 17
Data Encoding 5.5 MBps
Input data is broken into 4 bit nibbles where the first two bits are the sign bits d0 and d1. These are encoded as differential carrier phase shift according to the table used for 2 MBps.
The next two bits of the nibble are encoded as CCK with d2 and d3 selecting the symbol to be transmitted from the following table. Note that this table has the cover code included. To get the raw symbol, negate the 4th and 7th chips.
The spread symbols are sent with the leftmost chip first in time. Notice that the chip which is constant in phase across all symbols of the set is the last chip and this one could be considered the symbol’s reference phase chip. The symbol’s cover code is applied as the symbol leaves the modulator. The cover code rotates the chips.
d2, d3

## Slide 18
Chip Encoding @ 5.5 MBps
01
10
00
11
+I
+Q
-I
-Q
01
10
00
11
+1
+j
-1
-j
Rotate +45 degrees
(CCW) and convert
binary to Grey code
Real/Imaginary form
from definition
I/Q form for modulation
01 00 01 11 01 00 10 00
10 11 10 00 01 00 10 00
10 11 10 11 10 00 01 00
01 11 01 00 10 00 01 00
+1
+j
-1
-j
Data
Q,I pairs
Complementary Codes (with cover)

## Slide 19
Differential Encoding
Dibit pattern (d(0),d(1))
d(0) is first in time
Even Symbols
Phase Change (+j
w
)
Odd Symbols
Phase Change (+j
w
)
00
0
p
01
p
/2
3
p
/2 (-
p
/2)
11
p
0
10
3
p
/2 (-
p
/2)
p
/2
The differential phase encoding table treats odd and even symbols differently.

## Slide 20
CCK Modulator Technique for 5.5 MBps
Pick One of
4 Complex
Codes *
MUX
1:4
d2, d3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
Data Rate = 4 bits/symbol * 1.375 MSps = 5.5 MBps
Scrambler
d0
d1
Differentially
Encode Phases,
Odd/Even
Cover Codes
11 MHz
Complex
Multiply,
Rotate
Complex
Multiply,
Rotate

## Slide 21
CCK Cover Sequences
The only cover sequence so far defined is one that rotates the 4th and 7th chips by 180 degrees.
This makes the DC term of the data #0h symbol less of a problem
In general other cover sequences may rotate any chip into any quadrant, so a 16 bit sequence is needed to define them.

## Slide 22
CCK Cover Code Rotations
The data and cover code are performed in the I/Q domain and the output is also in this domain. All operations are in Grey code
The cover code application and removal requires a rotational decode, so the best approach is a look up table .
data, rotation
00 00
00 01
00 11
00 10
01 00
01 01
01 11
01 10
11 00
11 01
11 11
11 10
10 00
10 01
10 11
10 10
output
00
01
11
10
01
11
10
00
11
10
00
01
10
00
01
11
01
10
00
11
+I
+Q
-I
-Q

## Slide 23
Data Demodulation, 5.5 MBps
A/D converter
Compl.
Mult
Decover
rotation
Fast
Walsh
Transform
Biggest
Picker
Sign
Detector
Carrier
PLL
Binary to
Grey and
Differential
Detector
Select 5.5 set
Cover
Sequence
Analog
Input
Data
Output
Descrambler
Data
Reformatter,
serializer
2
2
CCK Data Mapping

## Slide 24
CCK Data Mapping
The first output data bit of the Biggest Picker and sign detector represents a 180 degree change and the second bit a 90 degree change. This is a binary code
The mapping from the raw data to the output bits works out as binary to Grey decoding.
Additionally, the differential decoding requires a odd/even rotational decode, so the best approach is a look up table which does all at once.
Binary to Grey and Differential Decoding

## Slide 25
Data Encoding 11 MBps
Input data is broken into bytes where the first two bits are the phase bits d0 and d1. These are differentially encoded as carrier phase shift according to the table on following slide. The next six bits of the byte are encoded as CCK with d2 to d7 selecting the symbol to be transmitted from the following formula:
c
e
e
e
e
e
e
e
e
j
j
j
j
j
j
j
j
=
+
+
+
+
+
+
+
+
+
+
+
+
{
,
,
,
,
,
,
,
}
(
)
(
)
(
)
(
)
(
)
(
)
(
)
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
1
2
3
4
1
3
4
1
2
4
1
4
1
2
3
1
3
1
2
1
The f1 term is the phase term derived from d0 and d1 according to the table on the following slide. The f2 term is derived from the d2, d3 pair, f3 from the d4, d5 pair, and f4 from the d6, d7 pair, all in accordance with the chart on the following slide. A look up table will most likely be the form of the symbol encoding for the d2..d7 terms.

## Slide 26
Encoding 11 MBps Continued
Dibit pattern (d(i),d(i+1))
d(i) is first in time
Phase
00
0 +1
01
p
/2 +j
11
p -1
10
3
p
/2 (-
p
/2) -j
The spread symbols are sent with the left most chip first in time. Notice that the chip which carries the symbol’s phase is the last chip.
The symbol cover code is applied after the symbol has been defined.
The table below shows how the d0..d7 terms are pairwise encoded into the phase terms.

## Slide 27
CCK Modulator Technique for 11 MBps Modulation
Pick One of
64 Complex
Codes
MUX
1:8
d2…d7
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
Scrambler
d0
d1
Differentially
Encode Phases,
odd/even
Cover Code
11 MHz
Complex
Multiply,
Rotate
Complex
Multiply,
Rotate
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps

## Slide 28
Data Demodulation, 11 MBps
A/D converter
Compl.
Mult
Decover
Fast
Walsh
Transform
Biggest
Picker
Sign
Detector
Carrier
PLL
Binary to
Grey and
Differential
Detector
Select 11
Cover
Sequence
Analog
Input
Data
Output
Descrambler
Data
Reformatter
6
2

## Slide 29
Adjacent channel interference
ACI @ 25 MHz separation: 30 - 35dB
  makes a 3 frequency channel topology possible at certain distance mix
  3 X throughput
x
x
x
3m
3m
3m
60m
Notes: In the figure x’s are 3 antennas (access points) at three different frequencies. One AP is disturbed by another over 3 meter, but can still receive a station over 60 meters.
dB separation is dependent on filtering (saw filter and transmit spectrum shape) The effect of lower ACI figures will change the distance mix.

## Slide 30
Receiver Minimum Input Level Sensitivity
The Frame Error Rate (FER) shall be less than 8x10-2 at an MPDU length of 1024 octets for an input level of -80 dBm measured at the antenna connector. This FER shall be specified for 11 Mbit/s CCK modulation. The test for the minimum input level sensitivity shall be conducted with the energy detection threshold set less than or equal to -80 dBm.

## Slide 31
CCA mechanism and Co-Channel signal detection time
We measure the correlated signal energy in the preamble over 5 us dwells beginning when the receiver is enabled and compare that to a threshold
The detection time is less than the slot time by enough to include diversity
FH detection is done on clock energy in similar dwells.

## Slide 32
CCA
The DSSS PHY shall provide the capability to perform Clear Channel Assessment (CCA) according to at least one of the following three methods:
  CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detecting any energy above the ED threshold.
  CCA Mode 2: Carrier or modulation sense only. CCA shall report a busy medium only upon the detection of a DSSS signal. This signal may be above or below the ED threshold.
  CCA Mode 3: Carrier or modulation sense with energy above threshold. CCA shall report a busy medium upon the detection of a DSSS signal with energy above the ED threshold.

## Slide 33
CCA Threshold
The CCK codes are not as easily detected as Barker Codes, so detection may not occur in the middle of the message. This is a rare event except when a packet is dropped in the middle, for example when a receiver not configured for the optional short preamble sees one.
  a). If the valid signal is detected during its preamble within the CCA assessment window, the energy detection threshold for 98 % probability of detection shall be less than or equal to
  -80 dBm for TX power > 100 mW
    -76 dBm for 50 mW < TX power <= 100 mW
    -70 dBm for TX power <= 50 mW.
After detection of the carrier in the short preamble by a receiver not capable of processing the short preamble, CCA busy is raised. When no SFD is detected CCA shall be kept busy until an energy drop of 10 dB. Thus, during the whole message (which is known to be a 802.11 message but not understood by the receiver) the receiving modem will keep silent. After the energy drop the modem will be in slot sync again.

## Slide 34
Interoperability
CCK can recognize both long and short preambles. If the CCK receiver detects a short preamble it trains on the short. If the receiver detects the long preamble it trains on the long preamble. If long, it can now also recognize the data rate, which can be a legacy DSSS rate (1 or 2 Mbit/s).
Scenario: CCK starts with a short preamble. Legacy DSSSS modems defer on that preamble. It is normally received by the CCK modems that have the option to receive a short preamble. The CCK modem can receive both CCK (short and long) and legacy DSSS transmissions. If reception is poor (or there is, for whatever reason, a coexistence problem with IEEE modems), the transmitter falls back to 5.5 Mbit/s or to the long preamble. The long preamble is also recognized by the legacy DSSS only modems, making use of the IEEE imbedded multi-rate capability.
Result: CCK modems send, if circumstances allow, the short preamble, making full use of the higher throughput capabilities. They are at all times interoperable with legacy DSSS modems, recognizing the long preamble, receiving (and sending) at the low rates. If there are coexistence problems the CCK modems falls back to the long preamble.

## Slide 35
Coexistence
Low rate and high rate PHYs will coexist within the same network.
Short preambles will be used only within networks of high rate PHYs
Short and long preambles may be intermingled on the same network.
All (rate) PHYs will perform CCA on either long or short preambles
Performing CCA in the middle of a packet on CCK is problematic.
Notes: By designing in the long preambles with the high rate hardware, we have tacitly assumed that they will coexist with the low rate stations on the same network. Dynamic switching of rates is expected. Even if all stations are high rate capable, some may require low rates in order to maintain connection.
A network can be set up to maximize throughput at the expense of reliability by using only short preambles. This does not allow downshifting to 1 and 2 MBps. If downshifting was needed, the short preamble would not be useable to convey this information if the SNR could only support 1 MBps.
For example, the beacon transmissions may be performed with long preambles in order to make sure that all PHYs can get the message. The high rate stations can sense that the short or long preamble is incoming by the state of the unmodulated sync section and process it accordingly. This allows it to do a better job in setting up an equalizer on the long preamble. This allows all PHYs to use all four rates for maximum reliability.
Leakage from nearby low rate networks may occur. A low rate station receiving the short preamble will not see the SFD and will probably not even be tracking when it occurs. It will miss the SFD but will none the less perform CCA on the preamble since it exists for more than 20 us. Once the body of the packet is started, it will not see it unless it is processing ED. Thus, low rate PHYs using CS only for CCA may interfere with high rate PHYs. High rate PHYs will be able to sense the length field of the low rate transmissions and defer.

## Slide 36
Coexistence Philosophy
Coexistence means that short preamble CCK defers for legacy DSSS (and long CCK) and vice versa.
legacy DSSS
  detects short preamble (carrier or energy); CCA reports channel busy;
  waits for Start frame delimiter but will not find it.
  It is not prescribed in the standard what action the receiver has to take, there are several possibilities:
  once the CCK signal starts after the preamble, the receiver might loose code lock and causes CCA to go to the channel IDLE state. The receiver returns to the RX idle state and starts looking for a carrier, which it does not see (because of CCK). This might result in a collision or the receiver being out of slot sync.
  The receiver times out on the SFD. This also leads to out of sync and possible collision
  CCA reports channel busy until the ED drop of the CCK signal. In this case the DSSS receiver stays in slot sync.
  It is clear that the third implementation (ED) is the best guaranty for coexistence.

## Slide 37
Coexistence Philosophy
CCK receiver
  configured to process a short preamble, the receiver will also detect the long preamble and process the legacy DSSS frame. The CCK receiver can see the legacy transmitter CS in the middle of a message and defer if necessary.
  On the CCK portion of the packet, the CCK receiver also loses the CS if it is based on Barker correlation and will not behave. Therefore it too needs a better CCA measure like improved ED.