## Slide 1
802.11 MAC Analysis
Definitions & Suggestions as they relate to the WPAN

## Slide 2
WPAN Study Group Vision 802.11 MAC Lite
2.4 GHz radio
Freq. Hopping
Spread Spectrum
2.4 GHz radio
Direct Sequence
Spread Spectrum
Infra-Red
1 Mbit/s
2 Mbit/s
2 Mbit/s
1 Mbit/s
1 Mbit/s
2 Mbit/s
Legend: italic (and red) = optional
Higher data rate extension in 2.4 GHz
802.11b
Higher data rate extension in 5 GHz
802.11a
11 & 5.5 Mbit/s
6-12-18...54 Mbit/s
MAC
Lower data rate extension in 2.4 GHz
802.11x
<1Mbit/s
MAC Lite

## Slide 3
Access Point Definition
An AP is a station that organizes all of the other stations in the wireless LAN around itself
It acts as a conduit for all of these stations communications
  In 802.11, if there is an AP present then there is no peer-to-peer communication
    This is a requirement on how the protocol is used

## Slide 4
Creation of a WPAN “AP”
Add an IUT (WPAN “AP”) to the existing PICS
  Can be used for a “deeper” power management function
    This avoids the need for the ATIM function
Operation of the WPAN “AP”
  The WPAN “AP” would wake up and send a beacon then go to sleep. It basically sets the NAV in this beacon to help “shutdown” other devices in the WPAN
  The other stations in the WPAN could go to sleep during the same “sleep” period as the “AP”
  Provision is for a non-continuously powered AP
This function could be implemented with a new element in the existing 802.11 beacon

## Slide 5
WPAN-AP Considerations
Stations that are Uni-directional in their communications model can “sleep” for as long as they need
For devices that are Bi-directional and require longer sleep periods
  Buffering of data packets is implied
    This is a tradeoff that needs to be considered in the architecture and classes of devices supported by the WPAN

## Slide 6
Suggestions for Moving Forward
For present purposes, define the PICS for the WPAN with an AP and a station as its elements
  To address the need for no single point of failure at least one and possibly more stations need to assume that function
  The function of transitioning to another AP is undefined at present and may be placed at a higher level in the stack than the MAC layer
  Using an AP may be the only way to meet the WPAN power requirements

## Slide 7
Authentication (PC1.2)
The process of identifying another station and deciding to allow/disallow communication with it
  Transient devices can enter and leave the WPAN with authentication services
  Open authentication allows for a positive ACK for any device that comes in range of the WPAN (PHY parameters & BSS ID must be set prior to this step)
  Use of shared keys provide for a higher level of security
    Creation & exchange of the shared key is not part of the 802.11 MAC

## Slide 8
WEP (PC2)
Wired Equivalent Privacy
  Minimal encryption for operation
  Without WEP present, you could have a manual authentication process
ALTERNATIVE 1
  Use WEP & a shared key authentication, or...
ALTERNATIVE 2
  Use open authentication with higher level functions (including manual) authentication
  This is the minimal cost solution

## Slide 9
NAV (PC3.1)
Net Allocation Vector
  This is a “virtual” busy signal from the network to handle the hidden node problem
  For example, it prevents stations from accessing the medium before the ACK returns
If you ASSUME:
  That all nodes within a WPAN can hear each other at all times, then the NAV function is not required

## Slide 10
PCF (PC4)
Point Coordination Function
  This controls access to the medium for contention free services
  This function can be removed from the MAC if the concept of WPAN-AP power saving modes are included in the design of the WPAN
    This approach allows the WPAN-AP to power down
  Implication of this change:
    Lengthens the joining process (by a few seconds)

## Slide 11
Fragmentation/Defragmentation (PC6 & PC7)
Function depends upon the error characteristics of the channel in use
The function is needed to support efficient use of the radio spectrum
Performance of the WPAN will be better if this function is implemented at the MAC level
  This reduces the overall # of bytes transmitted per MSDU
Recommend that we keep it!
Cost of implementation is a wash - this is needed somewhere in the implementation

## Slide 12
Multirate Support (PC9)
If this option is removed it may limit the future extensions of WPANs
  Lower power implementations
  Gateway extensions to higher speed networks
This option can add complexity to the implementation of the MAC...
  So, the WPAN requirements need to place a relative value on its importance

## Slide 13
Timing Synchronization (PC11.1)
A Given...
  The concept of timing needs to exist within the network infrastructure
How does the network maintain its timing if the AP losses its power ?
  In this scenario, the network timing function can be transferred to another station either...
    Automatically in the MAC (Distributed Beaconing)...
    By a higher layer protocol or ...
    Manually by the user

## Slide 14
Timing Synchronization (PC11.1) [Cont.]
ALTERNATIVE 1
  Use a “Distributed Beacon” mechanism and tweak it so that one station will assume the role of sending the beacon (WPAN-AP)
  This allows for the immediate recognition & recovery of the network when the beaconer is lost or goes away
The Implication:
  This would push the function of frame buffering onto the stations in the network capable of being an AP
  Potentially, this could increase memory requirements, and likely the WPAN device cost

## Slide 15
MIB (PC15)
Management Information Base
  Recommend that it be re-defined for WPAN applications
  Existing MIB will affect power consumption and memory requirements for WPAN applications
  Need to address authentication & encryption in our review of the new MIB implementation

## Slide 16
MAC Frame Format
Recommend that the WPAN MAC frame format remain identical to the existing 802.11 frame format:
  WPAN may need to define at least one and maybe two new IUTs (Implementation Under Test)
  These “new” devices would be compliant as new classes of 802.11 devices

## Slide 17
WPAN MAC Summary
Keep 95% of the existing 802.11 MAC
Extend current 802.11 capabilities
  The AP gains power management
  AP functionality migrates between WPAN capable devices
Remove some OH
  Slim down the MIB
  Eliminate RTS/CTS
  Eliminate IBSS