## Slide 1
Wireless Personal Area Networking A Study Group Report
November 11, 1998
Albuquerque, NM

## Slide 2
Agenda
WPAN Study Group Status
Albuquerque Summary
Motions:
  Motion 1 - WG approval of SG Direction
  Motion 2 - SG wants extend the WPAN SG from Albuquerque to Austin
  Motion 3 - SG Recommends that the WG investigate coexistence with other Wireless Network Systems in the 2.4GHz band
Liaisons Contacts

## Slide 3
WPAN Study Group Background
Submitted a Motion for a PAR & 5C approval in LaJolla Plenary 7/98
During the Plenary Our Sponsor postponed our Motion due to lack of detail
Since LaJolla we have had significant support from 802.11
During this session we want to report progress and receive comments from 802.11

## Slide 4
WPAN Application Feature List
Consensus
Strong
Weak
Priority
High
Low
low cost
low power
small size
packet data < 1 Mbps
range < 10m
active devices < 10
manual auth/auto attach
coexistence with 802.11
packet + isochronous
encryption
mobility < 10 mph
gateway
native IP
inter-pan connectivity
topology
active devices 10 - 128
coexisting PANs 4-30

## Slide 5
WPAN Study Group Vision 802.11 MAC Lite
2.4 GHz radio
Freq. Hopping
Spread Spectrum
2.4 GHz radio
Direct Sequence
Spread Spectrum
Infra-Red
1 Mbit/s
2 Mbit/s
2 Mbit/s
1 Mbit/s
1 Mbit/s
2 Mbit/s
Legend: italic (and red) = optional
Higher data rate extension in 2.4 GHz
802.11b
Higher data rate extension in 5 GHz
802.11a
11 & 5.5 Mbit/s
6-12-18...54 Mbit/s
MAC
Lower data rate extension in 2.4 GHz
802.11x
<1Mbit/s
MAC Lite

## Slide 6
WPAN MAC Summary
Keep 95% of the existing 802.11 MAC
Extend current 802.11 capabilities
  The AP gains power management
  AP functionality migrates between WPAN capable devices
Remove some Overhead
  Slim down the MIB
  Eliminate RTS/CTS
  Eliminate IBSS

## Slide 7
Background for Motion 1
The SG received inputs from 802.11 experts on the standard to provide information on a method on deriving an 802.11 MAC Lite:
  98/322r2 “MAC PICS vs. WPAN Requirements”
  98/323 “802.11 Terminology related to WPAN”
  98/324 “PHY PICS vs. WPAN Requirements”
Strawpoll Nov10, 16/1/7

## Slide 8
Motion 1: On behalf of the SG, I:
Move to have the 802.11 Working Group endorse the WPAN SG’s direction to create an 802.11 MAC Lite & corresponding PHY Layer(s) based on a derivative of the 802.11 MAC Layer.
SG Motion: Nov11, Ian/Ken 9/0/1, Motion Passes

## Slide 9
Motion 2: On behalf of the SG, I:
Move to extend the timeframe of the Wireless PAN Study Group under 802.11 to ensure continuity and submit the PAR to our Sponsor at its Jan99 Interim Meeting
Chair: Dick Braley
  Vice Chair: Bob Heile
  Secretary/Tech Editor: Ian Gifford
Motion: Nov11, Ian/Jim Z., 11/0/0 motion passes

## Slide 10
Background for Motion 3
This motion is a result of the Study Group’s desire to have coexistence with 802.11 devices and we feel it would be prudent for 802.11 to investigate coexistence with other Wireless Network Systems in the 2.4GHz band

## Slide 11
Motion 3: On behalf of the SG, I:
Move to recommend that the 802.11 Working Group investigate the need for coexistence with other Wireless Networking Systems in the 2.4GHz band
Motion: Nov11 Ian/Jim, 9/1/3

## Slide 12
Archive, Mailing List, URLs
Archives
  ftp://ftp.flexipc.com/wearablesgroup/
  http://grouper.ieee.org/groups/802/11/index.html
Mailing List
  stds-802-wpan@majordomo.ieee.org
Bluetooth Special Interest Group
  http://www.bluetooth.com/
Home RF Working Group
  http://www.homerf.org/
To add your name to IEEE mailing list please send an e-mail
to Ian Gifford giffordi@amp.com

## Slide 13
Liaison Contact Info
Bluetooth SIG
Simon Ellis
Intel Corporation
Manager Mobile Marketing, Communications
E-M: simon.c.ellis@intel.com
TEL: 408/765-4461
HomeRF WG
Ben Manny
Intel Architecture Labs
Engineering Manager for Residential Networking
E-M: ben.manny@intel.com
TEL: 503/264-7752
FAX: 503/264-3483

## Slide 14
IEEE 802.11 Meeting Schedule
1999
  Jan 11-15 - Grovsvenor Resort, Lake Buena Vista, FL, Interim (Harris)
    DEADLINE November 15th, 1998!
  March 8-12 - Hyatt Regency, Town Lake, Austin, TX, Plenary
  May TBD - Japan?, Interim (Clarion)
  July 5-9 - Queen Elizabeth, Montreal, PQ, Canada, Plenary
  Sept TBD - Israel?, Interim (BreezeCom)
  November 8-12 - Hyatt Regency Kauai, Koloa, HI, Plenary