IEEE P802.11
Wireless LANs

Comments received on draft standard IEEE P802.11b/D1.0
in response to Letter Ballot 15
Second and last batch

Date:	November 8, 1998

Author:	Vic Hayes
	Lucent technologies
	Zadelstede 1-10
	3431 JZ Nieuwegein, the Netherlands
	Phone: +31 30 609 7528
	Fax: +31 30 609 7556
	e-Mail: vichayes@lucent.com

Comments

Please not that Stan Reible and John Cafarella submitted their comments in table format in this table, replacing the unformatted comments from document -98/376.

.

| 1 | Table 1 | TG | e | n | Column 4 contains the line “ = CCU” | “0 = CCK” |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 18.2.3.5 | TG | e | n | Paragraph 2, line 4 contains the phrase “extra bit will be placed” | “extra bit shall be placed” |  |
| 3 | 18.2.3.5 | TG | e | n | In the descriptions in b) and d), the phrases “the rounding took” are not clear. | Replace the descriptions with equations, such as: Encode = ceiling((#octets * 8) / 11) Decode = floor((length * 11) / 8) - ext.bit ext.bit = (length*8) mod 11 in [3,2,1] |  |
| 4 | Table 3 | TG | e | n | In the heading of column 2, the equation is wrong, but the information in the column is correct | (Octets +1) * 8 / 11 |  |
| 5 | 18.2.6 | TG | T | n | There is no information in the TXVECTOR that tells the PHY which preamble length to use. This information also needs to be in the RXVECTOR to indicate which preamble length was received. | Add a TXVECTOR parameter to the PHY-TXSTART.request to specify which preamble is to be generated. Add an RXVECTOR parameter to indicate the received frame’s preamble length. |  |
| 6 | 18.2.6 | TG | t | n | The sentence “The PLCP Header parameter LENGTH is calculated from the TXVECTOR element by multiplying by 8 for 1 Mbit/s and by 4 for 2 Mbit/s.” is incomplete without the 5.5 and 11Mb/s rates. | “The PLCP Header parameter LENGTH is calculated from the TXVECTOR element using the algorithms described in 18.2.3.5” |  |
| 7 | Figure 9 | TG | t | N | In the PLCP Transmit State Machine, TX SYNC PATTERN block, the operation “TX 128 Scrambled 1’s” is incomplete | “TX 128 Scrambled 1’s for the long preamble or TX 56 Scrambled 0’s for the short preamble” |  |
| 8 | Table 6 | TG | T | N | aPreambleLength is a single integer. Since it is not a vector, it cannot contain lengths for the three different preambles. Also, the correct values are 144uS, 72uS, and 208uS, not 144uS and 56uS as shown. | Three operating modes should be defined, and all members of a BSS must be in the same mode. The modes would be LongPreamble, ShortPreamble, and FHPreamble. In LongPreamble mode, the long preambles would always be used. In ShortPreamble mode, long preambles would be used for 1 and 2Mb/s rates, and short preambles would be used for 5.5 and 11Mb/s rates. In FHPreamble mode, FH mode would be used for 1 and 2Mb/s rates and short preambles would be used for 5.5 and 11Mb/s rates. The value for aPreambleLength would remain a single integer of value 144, 72, and 208, for these three modes, respectively. |  |
| 9 | Table 6 | TG | t | N | aMPDUMaxLength cannot exceed 2^12 in FH interoperability mode, since the length of the PLW field in the FH preamble is 12 bits. | Make an exception in the table for the FH interoperability mode. |  |
| 10 | 18.4.6.7 | TG | E | N | In the 4th paragraph, the sentence “To place the encoder in a known state at the end of a packet, six deterministic bits are input immediately following the last data bit input to the convolutional encoder” is incorrect. All lengths must be multiples of 8 bits. | Change references from 6 bits to 8 bits. I list this as an editorial change because during my conversation with the authors of the PBCC proposal, they indicated that the value was supposed to be 8 bits. |  |
| 11 | 18.4.6.8 | TG | e | N | In the first paragraph, there is a reference to table 9. That is not the correct table. | The reference should be to Table 11. |  |
| 12 | 18.4.6.8.1 | TG | e | N | The table reference is incorrect. | Table 11 specifies the operating channels for specified geographical areas. |  |
| 13 | 18.2.2 | TG | t | n | Because the low rates are FH, the stations need the hop sequence and dwell synchronization information available in the FH parameter set element as well as the DS channel information in the DS parameter set element. This does not conflict with the frame formats as specified in clause 7. | When operating in the FH Preamble mode, the Beacon and Probe Response frames must include both an FH Parameter Set element and a DS Parameter Set element. |  |
| 1 | 18.2.2 | Dk | e | N | Last sentence of clause states “…may not use the FH PLCP.” | Should state “…shall not use the FH PLCP.” |  |
| 2 | 18.2.3.6 | Dk | E | N | The definition of CRC16 is not sufficient. | Use the definition in clause 14.3.2.2.3. |  |
| 3 | 18.2.3.15.1 | Dk | E | N | Table 4 does not adequately spell out the remaining patterns that are reserved. | Spell out separately the patterns that are reserved: 1010, 1011, 1100,1101,1110, 1111 |  |
| 4 | 18.4.8.4 | Dk | E | N | The statement is not clear: “The CCA shall be TRUE if there is no energy detect or carrier sense.” | Either delete sentence or correct to say “The CCA indication shall be CLEAR…” |  |
| 5 | 18.4.8.4 | Dk | E | N | The statement is inconsistent with the 802.11 standard: “This implies that the CCA signal is available as an exposed test point.” | Delete sentence. |  |
| 1 | 18.2.3.2 | to | T | Y | Current SFD seems not to be interoperable. New scheme should be included. |  |  |
| 1 | 18.2.3.8 to 18.2.3.11 | JC | T | Y | The specified short preamble is not rationalized with the “optional” FEC modes defined by Alantro; only a single short-preamble mode should be defined, and it should support all modes. | Rationalize short-preamble mode with both Harris and Alantro modes; ensure that optional mode (Alantro) is really an option by making sure that the short preamble supports both. |  |
| 2 | 18.4.8.3 | JC | T | Y | The channelization described requires 30-MHz separation of carrier frequencies. Since the US allocation supports 3 frequency channels only if there is 25-MHz of carrier offset, it is critical that the ACR be specified for 25-MHz separation as well as 30-MHz. | Three channels is (was) a key issue for the standard; since US band only supports 3 channels at 25-MHz spacing, the standard should specify the ACR at this spacing. |  |
| 3 | 18.2.3.15 18.4.6.8 | JC | T | Y | The FH option contained in the draft violates the PAR restriction to a single PHY. Anyone can build a dual-mode transceiver if desired, but specifying how to do this violates our PAR. | Remove FH material from HR DSSS PHY standard. |  |
| 1 | 18.2.3.2 | to | T |  | Current SFD seems not to be interoperable. New scheme should be included. |  |  |
|  | 18.2.2 | lw | T | Y | The channel is 22 MHz wide, multiple FH BSS may be within one HS DS channel. How do we choose which FH BSS channel to transmit the header on? the HS DS transmit/interfere with multiple FH BSS. | I do not know how to resolve this, it should be discussed in the group. |  |
|  | 18.2.2 | lw | T | Y | 8uS between 1Mbit/s FH header and short. | 16 to 20uS is practical. |  |
|  | 18.4.6 | lw | T | N | A transmit to receive turn around time of 10 ms is excessive and maybe a typing error. | 10uS |  |
| 1 | 18.2.1 | sr | T | Y | The combination of an optional short preamble and, especially an optional FH interoperable preamble and header leads to multiple PHY implementations. This is not keeping with the task group’s goal of implementing one high rate PHY. | Eliminate backword compatiblilty to low rate FH systems. Clearly define one prefered implementation. Outline clear situations when the designer would want to implement the options. |  |