## Slide 1
Extension of Bluetooth and 802.11 Direct Sequence Interference Model
Jim Zyren
Harris Semiconductor
jzyren@harris.com

## Slide 2
Summary
Earlier paper presented analysis of influence of BT on co-located 802.11 DS STA
  “Impact of Bluetooth on 802.11 Direct Sequence”
    Doc.: P802.11-98/319
Most of original model is retained
  Modifications to model are proposed for:
    Change probability of co-channel interference
    Use of short preamble and header
    Modified BT interference profile
    Use of longer IFS on dropped packet
  Results using modified assumptions are presented

## Slide 3
BT / DS Topology
802.11 Station
Bluetooth
Nodes
ALL packets from
station immune to
Bluetooth collisions
ALL packets from
AP subject to
Bluetooth collisions
802.11
Access Point

## Slide 4
Original Model
Any collision in time and frequency between BT and DS results in dropped packet
  determine # BT dwell periods (n) a DS packet overlaps
  estimate probability any given BT hop falls in band (Pjam)
  Account for BT piconet utilization factor (UF)
  Probability of collision (Pcoll):
    Pcoll = (Pjam)n * UF
  Add in appropriate network overhead to determine Degradation Factor and Throughput
These features of Original Model are retained for this analysis

## Slide 5
Proposed Modifications

## Slide 6
Co-channel Interference
- Original model assumed probability that BT hop falls in DS passband
(Pco) is 1/3. This corresponds to 26 MHz DS bandwidth
- Measured data for CCK CW jammer suppression suggests assuming
DS BW = 20 MHz is more accurate (Pco = 1/4)

## Slide 7
Co-channel Interference
CW Jammer suppression due to combined effects of IF
Filter and sin (x) / x post-correlation jammer PSD
fc
post-correlation bandwidth
fc - 11 MHz

## Slide 8
Packet Headers
Preamble (144 bits)
Header (48 bits)
192 msec = 144 bits @ 1 Mbps + 48 bits @ 1Mbps
Original Model assumed long preamble & header
Preamble (72 bits)
Header
(48 bits)
96 msec
(72 bits @ 1 Mbps + 48 bits @ 2 Mbps)
Modified Model assumes short preamble & header

## Slide 9
BT Interference Profile
Original Model Assumed BT Tx Burst = BT Dwell Period
Example: DS packet is 2000 msec long
#dwell periods = 2000 / 625 = 3.2 dwells
Prob of overlapping 4 dwells = 20%
Prob of overlapping 5 dwells = 80%
Avg BT overlap = 4.8 dwells

## Slide 10
BT Interference Profile
Modified Model: BT Tx Burst = 366 msec of 625 msec dwell
Example: DS packet is 2000 msec long
#dwell periods = 2000 / 625 = 3.2 dwells
Prob of overlapping 3 dwells = 21%
Prob of overlapping 4 dwells = 79%
Avg BT overlap = 3.8 dwells

## Slide 11
Interframe Spacing
Original Model:
IFS on dropped packet = ACKTimeout + DIFS + 7 slot times
Modified Assumption:
IFS on dropped packet = ACKTimeout + DIFS + 15 slot times
DS PHY MIB specifies default value of CWmin = 31 slot times

## Slide 12
Results w / Modified Assumptions
Degradation Factor v. Fragment Size @ 5.5 Mbps

## Slide 13
Results w / Modified Assumptions
Throughput (Mbps) v. Fragment Size @ 5.5 Mbps

## Slide 14
Results w / Modified Assumptions
Degradation Factor v. Fragment Size @ 11 Mbps

## Slide 15
Results w / Modified Assumptions
Throughput (Mbps) v. Fragment Size @ 11 Mbps

## Slide 16
Predominantly Upstream Traffic
Upstream Traffic (STA to AP) is affected much less because
BT Interference is Localized, and Downstream ACK’s are
very short packets

## Slide 17
Conclusions
DS network thruput w/BT interference is better than initially predicted
Shorter packets at 5.5 and 11 Mbps enable DS to avoid most BT interference
BT interference effects are localized
Fragment size of 750 bytes works well for 5.5 and 11 Mbps
High power BT devices present a completely different problem
  BT piconet will be distributed over greater area
  higher power increases “bubble of interference”, but
  distributed topology mitigates “near/far” problem for DS-STA
DS/BT interference is still an issue
  effect on BT is TBD
  coexistance/interoperability is a desirable goal