## Slide 1: BRAN#11 PHY Decisions & Issues to Resolved with 802.11
Jamshid Khun-Jush
Ericsson Eurolab - Nürnberg
Co-ordinator of HIPERLAN-2 Standard Area &
Chair of Physical Layer Technical Specification Group

## Slide 2: Outline
Decisions on Baseband Parameters
Decisions on Carrier Spacing
Notes: Page <number>
        <footer>
<header>
<date/time>
1

## Slide 3: Decisions on baseband Parameters-1
FFT size:
  64 points
The number of used sub-carriers:
  48
The guard interval:
  800 ns
Sub-carrier modulation:
  BPSK, QPSK, 16QAM, possibly 8PSK and optionally 64 QAM
Demodulation in sub-carriers:
  Coherent

## Slide 4: Decisions on baseband Parameters-2
FEC:
  A mandatory convolutional mother code with constraint length 7 and rate ½
  Required code rates ½, ¾ obtained by puncturing
  Code rate 2/3 will possibly be needed.
  Code rates 1/3 or ¼ might be needed to provide more protection for short control PDUs.
  The code rates shall be selected in such a way that each PDU should be mapped into an integer multiple of OFDM symbols current assumption on data PDU size: 54 bytes.
  Optional coding schemes might be added to the specification later (not in the first stage).

## Slide 5: Decisions on baseband Parameters-3
Interleaving:
  Not decide yet, if the interleaving is to be done OFDM symbol wise or PDU wise.
  More investigation are needed. To be discussed and maybe decided at the interim meeting of the PHY TS Rapporteur Group on December 11.
Oscillator accuracy:
  +/- 20 ppm
Spectral shaping:
  Same approach as IEEE 802.11
    No time windowing specification
    constellation accuracy test specifications in combination with spectral mask

## Slide 6: Decisions on baseband Parameters-4
Training sequence:
  Three different preambles needed, due to the centralised DLC protocol applied to HIPERLAN/2
    One for the beginning of MAC frame could have the same structure as the first part of the training sequence proposed for IEEE 802.11
      AGC symbol(s), the symbols for coarse frequency and timing estimation and the long symbol for fine frequency offset and channel estimation.
      no need for the training part SIGNAL, because the signalling of PHY mode will be performed in other part of the protocol.
    One for each downlink burst and one for each uplink burst could have the same structure as the long symbol T1 in IEEE 802.11 proposal.
    Not clear:
      symbols for coarse frequency offset estimation and timing are needed for downlink and uplink bursts
      AGC symbol(s) in uplink bursts needed if power control is used in uplink.

## Slide 7: Decisions on baseband Parameters-5
Phase tracking:
  A phase tracking scheme is needed due to coherent demodulation.
  No need for pilot symbols to perform phase tracking
    Assessment based on initial results of some members of the PHY TS Rapporteur Group
  But more results needed to make a final decision (to be discussed at the PHY TS interim meeting in December)
    a pilot symbol aided scheme versus a decision directed one

## Slide 8: Decisions on Carrier Spacing-1
150 MHz bandwidth currently available in Europe for HIPERLAN
  in the range 5.15 – 5.3 GHz
  less than –33 dBm/100kHz emitted spurious power outside this band is allowed below
    Assuming a transmit power of 200 mW, a 35 dB attenuation necessary at both edges of the HIPERLAN frequency band.
    Simulation results show that the spacing of the outmost channels from the band’s edges have to be in the order of 22 MHz.
    nonlinear model for a class AB power amplifier with an out put backoff of 5.5 dB.

## Slide 9: Decisions on Carrier Spacing-2
  the number of radio channels achieved by an 18 MHz channel spacing is equal to that achieved by a channel spacing of 20 MHz.
    six radio channels could be obtained in current HIPERLAN band
    distance of the outmost channel from each band edge is 25 MHz
    relaxed requirements on the PA backoff.
    with HIPERLAN/2 PA models, the outmost channels in UNII band need even more distance from the band edges if practical PA backoff values used.
    with 20 MHz channel spacing, 8 radio channels for the 200 MHz band starting at 5.15 GHz (lower and middle U-NII bands) achievable.
    in addition enough spacing for the outmost channels from the band edges available

## Slide 10: Decisions on Carrier Spacing-3
No decision on the sampling rate which determines the bit rate supported in a radio channel.
Two different alternatives
  a rate of 20 Msamples/s
    results in a reduced adjacent channel interference (ACI)
    might be translated in an increased overall system capacity.
  a higher sampling rate (e.g. 22 Msamples/s)
    increased instantaneous bit rate in one radio channel
    but also increased ACI that might be translated in degradation of the overall system throughput
    some mixed frequency products making the RF implementation more complex
Decide on all issues in the PHY interim meeting in December 11