## Slide 1
Harris/Lucent TGb Compromise CCK (11Mbps) Proposal Selection Criterion
Submission to IEEE P802.11 Wireless LANs
Mark Webster and Carl Andren Harris Semiconductor
Jan Boer and Richard van Nee Lucent Technologies

## Slide 2
The Evolution of the Waveform
1. The Walsh functions used independently on both I and Q channels are subject to cross rail interference.
2. By combining the I and Q channel symbols into one complex complementary code symbol, the cross rail interference is mitigated. This new symbol type carries 6 bits and can be QPSK modulated to carry 2 more bits giving 8 bits per symbol as before.

## Slide 3
11 Bit Barker Word
22 MHz
11 MBps
CCK
5.5 MBps
CCK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS BPSK
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit used to
BPSK code word
11 chips
1 MSps
2 bits used to
QPSK code word
8 chips
1.375 MSps
2 bits encoded to
4 complex code
words; 2-QPSK
8 chips
1.375 MSps
I, Q
I, Q
I, Q
Modulation Technique and Data rates
I, Q
6 bits encoded to
64 complex code
words; 2-QPSK
Code set
Notes: The Harris/Lucent suggested high rate modulation is a form of M-ary Orthogonal keying to be known as Complementary Code Keying (CCK). We propose that two Quadrature forms of this modulation be used to provide multiple rates for stressed links.

## Slide 4
Pick One of
64 Complex
Codes
MUX
1:8
6
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Scrambler
1
1
CCK Modulator Technique for 11 MBps
Code Set is defined by formula:
Notes: This slide shows how to form our suggested modulation type. M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal (or nearly orthogonal) vectors by the data word. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality. By extending the Walsh set to complex symbols, a more robust code set can be generated.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 5
Pick One of
4 Complex
Codes *
MUX
1:8
2
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 4 bits/symbol * 1.375 MSps = 5.5 MBps
Scrambler
1
1
CCK Modulator Technique for 5.5 MBps
*= Code Set:
747B
47B7
8B7B
B8B7
see next slide
Notes: To reduce the bit rate and get more performance fro stressed links, the M-ary index can be reduced by picking the best 4 out of the 64 code set. this reduces the number of bits per symbol to 4 and halves the bit rate while increasing the CCK performance.

## Slide 6
The modulator will use I and Q channels to modulate the QPSK and it takes two bits to specify a complex symbol bit, so the hex definition can be:
11h = +1
01h = j
00h = -1
10h = -j
Then the (4) 5.5 Mbit/s base codewords are:
747Bh =
8B7Bh =
B8B7h =
47B7h =
These are QPSK modulated as a symbol to encode two more bits
Codeword Definitions
Codeword 1
:
Codeword 2
:
Codeword 3
:
Codeword 4
:
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 7
Hardware Impact of CCK vs QMBOK
The correlators we used to decode QMBOK were two banks of 8 chip serial correlators which required 128 adds per code symbol.
The 64-ary correlator with the Fast Walsh transform requires 64+32+16 complex adds.

## Slide 8
RF/IF Complexity relative to current low rate PHY
Basically uses same RF and IF as existing 802.11 DS PHY.
RAKE/ Equalized version replaces the IF limiter with AGC and has more A/D converter bits.
A combined DS/FH mode uses non optimal wideband IF filters with some loss of performance in a crowded environment.
Notes: The use of the same RF bandwidth makes the design of the radio more or less the same as the existing low rate PHY. The main change is that to get more delay spread capability, the receiver may be enhanced by channel matched filtering (RAKE) and equalization and that generally is best performed in a linear receiver. That requires an AGC type of receiver rather than a limiting receiver and more bits of ADC conversion.

## Slide 9
Receiver Implementation
0o/90o
M
U
X
M
U
X
RxQ
RxI
VCO &
Synthesizer
Synthesizer
2.4GHz
VCO
RF- IF
IF - BB
I ADC
Q ADC
De-
Spread
De-
Modulate
Spread
Modulate/
Encode
Control
Test I/O
Tx/Rcv
Data I/O
CCA
Media Access
Controller
Baseband
Processor
MAC
RF AGC
Diversity
Tx Detect
IF AGC

## Slide 10
Baseband Processing Complexity relative to current low rate PHYs
Addition of high rate with limited receiver increases the DS only baseband processor complexity from 28K gates to 40 K gates.
Addition of 6 finger RAKE (Channel Matched Filter) to increase delay spread from 40 to 90 ns takes an additional 30 K gates.
The addition of high rate to FH has not been fully worked out yet.
Notes: The complexity of the existing design when stripped to the minimum to support the standard was found to be 23 K gates more or less. To add the high rate capability without the equalizer took 12 K more gates. The equalizer is projected to take an additional 40 K gates. Since many of these will be run at high rates, the power consumption must be carefully managed by selectively turning off sections not needed for the moment.

## Slide 11
BARKER
CORRELATOR
MAGNITUDE
ADC
SUB RATE
SAMPLE
ADC
Iin
Qin
CCA
PSK DEMOD
AVERAGE
PHASE
ERROR
LEAD/LAG
FILTER
ABS
DIF DECODE
COMPLEX
MULTIPLY
SIN/COS
ROM
SYMBOL
DECISION
DECISION
DIRECTED
PHASE DET
DATA
DESCRAM-
BLER
8
INTEGRATE
& DUMP
32 PHASES
PHASE
DET
SYMBOL
TIMING
SQ1
SQ2
DATA
AGC
AGC
CCA
PISO
CCK
CORRELATOR
BANKS
SHADED BLOCK ARE THE ADDITIONS TO DS FOR FH AND HIGH RATES
SUM
ED
NCO
FH DEMOD
CMF
BARKER
CORRELATOR
DEMODULATOR BLOCK DIAGRAM
Notes: The added capability blends well with the existing circuitry.

## Slide 12
+
x0
x1
x2
-x3
f2
f2
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
x4
x5
-x6
x7
f2
f2
+
+
+
+
+
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
f1
(BFWB)
f2 = 1, j, -1, -j
f1 = 1, j, -1, -j
1
j
-1
-j
The input samples are first
multiplied by the f2 vector
and after the butterfly, by the
f1 vector for each of 4 blocks
BASIC FAST WALSH BLOCK

## Slide 13
BFWB
BFWB
BFWB
BFWB
64-ARY
BIGGEST
PICKER
f2 = 1
f2 = J
f2 = -1
f2 = -J
Data out
Samples in
8 CHIP COMPLEMENTARY CODE DECODER

## Slide 14
Antenna Diversity and performance impact
Antenna diversity can improve the performance of the link less costly than an equalizer but not as much.
The performance impact has shown an improvement of a factor of 8 in PER in field testing.
The negative impact is to require additional time in the preamble on the order of 16 us (already covered by the 802.11 preamble).
Notes: The improvements of antenna diversity depend on the ability of the selected decision metric to discriminate the good antenna. The improvement comes cheap, but is is not as much of an improvement as an equalizer can provide.

## Slide 15
PER Vs. Noise

## Slide 16
PER Vs. Multipath Only (No Noise).

## Slide 17
PER vs. Multipath Only (No Noise).

## Slide 18
PER vs. Multipath Only (No Noise).

## Slide 19
PER Vs. Multipath Only (No Noise).

## Slide 20
PER Vs. Thermal Noise with Multipath at 10% PER. Eb/No at 20% PER for 64 and 1000 byte packets.
20%
Notes: The performance in both multipath and thermal noise shows that the system is capable of good performance.

## Slide 21
Required Carrier Frequency Accuracy
The new high rate PHY requires the same carrier frequency accuracy as the existing low rate PHY.
The DSSS limitation is that the maximum carrier frequency offset should be less than 1/8 th of the symbol rate of the preamble.
Notes: The requirements are the same as the existing standard.

## Slide 22
Required Data Clock Frequency Accuracy
The new high rate PHY requires the same clock frequency accuracy as the existing low rate PHY.
We recommend that the data clock be tied to the carrier frequency reference, so that optimizations can be achieved in the symbol tracking circuits.

## Slide 23
Preamble Length
Our basic approach is to include the standard DS or FH 802.11 preamble and header.
This length includes ample time to do diversity and equalization.
For the cases where interoperability is not an issue, a short, high rate header can be used.
Antenna diversity, WEP initialization and equalizer training require a somewhat longer short preamble than the shortest possible.
Notes: The long, interoperable preamble and header allows ample time to do AGC, diversity selection WEP engine initialization, and equalizer training along with the normal modem acquisition processing. In the event a shorter preamble and header is desired for maximizing throughput, it must take into account those extra times.

## Slide 24
Interoperability / Coexistence, short PPDU frame format
shortPLCP Preamble
MPDU
@ shortSIGNAL rate
70 bits @ 1Mbit/s
shortSYNC
shortSFD
16 bits
shortSIGNAL
4 bits
16 bits
shortLENGTH
shortCRC
54 bits
PPDU
shortPLCP Header
35 bits @ 5.5Mbit/s
16 bits
ShortSYNC: 54 scrambled all zero’s used for receiver synchronization:
e.g 30 microsec for CCA @ 20 microsec slottime with or without antenna diversity
shortSFD: bit reverse of original SFD

## Slide 25
Slot Times
We propose no change in the DS PHY slot time of 20 ms or FH slot time of 50 ms.

## Slide 26
CCA mechanism and Co-Channel signal detection time
We measure the correlated signal energy in the preamble over 5 ms dwells beginning when the receiver is enabled and compare that to a threshold.
The detection time is less than the slot time by enough to include diversity.
FH detection is done on clock energy in similar dwells.

## Slide 27
RX/TX turn around time and SIFS
The transmitter has a 1.3 ms processing delay from bits in to bits out the antenna.
The receiver has 3.3 ms processing delay from bits in the antenna to bits out.
The RX/TX turn around time is less than 2ms exclusive of the above delays.
We propose the existing DS 10 ms SIFS.

## Slide 28
Channelization Scheme
We propose the existing DS channelization scheme.
Three non overlapping channels in the band
A choice of 5 MHz channel centers with 11 channels in the ISM band for the US and 13 in Europe.
One channel for JAPAN.

## Slide 29
Adjacent Channel Interference Rejection
6 dB more filter skirt rejection and/or sidelobe attenuation is needed to achieve the same ACI rejection as the existing low rate PHY to account for the difference in SNR required in the spread bandwidth.

## Slide 30
Cell planning and ACI
3 frequency channels where same frequency of different cells share.
ACI must be such that a 3 channel solution is possible.
  interferred devices will fall back in rate
  system throughput more essential than the ACI figure

## Slide 31
Adjacent channel interference
ACI @ 25 MHz separation: 30 - 35dB
  makes a 3 frequency channel topology possible at certain distance mix
  3 X throughput
x
x
x
3m
3m
3m
60m
Notes: In figure x’s are 3 antennas (access points) at three different frequencies. One AP is disturbed by another over 3 meter,but can still receive a station over 60 meters.
dB separation is dependent on filtering (saw filter and transmit spectrum shape) The effect of lower ACI figures will change the distance mix.

## Slide 32
Co-channel interference
CCI is expected to be in the same range as the original Harris proposal.
Improvement because of better codes.
Initial simulations show 5-6 dB CCI.

## Slide 33
PER VS SNR for CCI
PER
SNR

## Slide 34
Interference immunity
Immunity to CW jamming is expected to be in the same range as original Harris proposal.
Improvement because of better codes.
Initial simulation show ~5.5 dB S/J

## Slide 35
PER VS SNR for CWI
PER
SNR
Notes: Figure 1 shows packet error ratio versus signal-to-interference ratio for continuous wave interference in the system at 11 Mbps. The packet error ratio was simulated over 5000 64-byte packets with randomly chosen interference frequencies. A channel matched filter with 6 taps was used. The tap values were obtained by averaging the correlation outputs of 10 training symbols, which are length 11 Barker codes. The 10% point is reached for a signal-to-interference ratio of 6 dB.

## Slide 36
Phase Noise Sensitivity
There is no particular phase noise sensitivity with the proposed waveform. It performs as well in phase noise as any QPSK scheme.
The measured phase noise of our receiver’s LO which performs well is 2 degrees RMS.

## Slide 37
RF PA Backoff
The CCK waveform needs about 4 dB of PA backoff to insure low regrowth of spectral sidebands.
This is the same as the DS BPSK preamble requires.
Substantially better than BCPM.

## Slide 38
DC power consumption
The current, non equalized HFA 3860 QMBOK chip draws 30 mA at 3 VDC with 0.6 micron technology. This represents about 12% of the radio receiver DC power.
We do not expect the current consumption of the simplest CCK receiver to differ from this.
With 0.35 micron technology, the most complex approach will be about the same.

## Slide 39
Patent Submissions
The Harris position is that we will only patent techniques having to do with our chip implementation. (See Harris’ patent submission)
Lucent has not done any patent search and is not aware of any relevant patents.
Anything likely to be embodied in the standard will be free of license from Harris.
The CCK waveform is public domain.

## Slide 40
Interoperability / Co-existence strategy with current low rate PHYs
Interoperable via use of existing low rate preamble and header, either DS or FH.
  In the case of the FH PHY, the low rate preamble and header must be followed by a short high rate header to re-establish antenna diversity and to train the equalizer.
Will defer or cause deferral via 802.11 mechanisms currently in place.
Notes: While we originally only suggested a DS low rate interoperability, Symbol has suggested low rate FH techniques.

## Slide 41
Is the proposal Interoperable at the data and antenna levels?
Yes!

## Slide 42
Performance penalty due to Interoperability / Coexistence.
The DS overhead is 192 ms Vs about 75 ms without interoperability
The FH overhead is 128 + 10 + 75 ms or about the same
This amounts to ~20 % on 1K byte packet
The short preamble and header will be about 75 ms or about 10% overhead on a 1000 byte packet.

## Slide 43
Additional simulation data

## Slide 44
11 MBps RAKE only Multipath only

## Slide 45
11 MBps RAKE, ISI Multipath only

## Slide 46
11MBps RAKE & ISI DFE (Noise and Multipath)

## Slide 47
11 MBps RAKE, ISI, ICI Multipath only

## Slide 48
11 MBps RAKE only (Noise and Multipath)

## Slide 49
11 MBps RAKE, ISI, ICI (Noise and Multipath)

## Slide 50
5.5 MBps Noise only

## Slide 51
5.5 MBps RAKE, (Multipath only)

## Slide 52
5.5 MBps RAKE only (Multipath only)

## Slide 53
5.5 MBps RAKE, ISI (Multipath only)

## Slide 54
5.5 MBps RAKE only (Noise and Multipath)

## Slide 55
5.5 MBps RAKE, ISI (Noise and Multipath)

## Slide 56
5.5 MBps RAKE, ISI (Noise and Multipath)
20%
Notes: The performance in both multipath and thermal noise shows that the system is capable of good performance.