## Slide 1
Harris/Lucent TGb Compromise CCK (11Mbps) Proposal
Submission to IEEE P802.11 Wireless LANs
Mark Webster and Carl Andren Harris Semiconductor
Jan Boer and Richard van Nee Lucent Technologies

## Slide 2
KEY FEATURES
11 and 5.5 Mbps data rates
Outstanding high-multipath performance
Outstanding low-SNR performance
Seamless interoperability with existing DS and FH
Clean, extensible receiver architectures enabled
Maintains QPSK chips at 11 MHz chip rate
Maintains 3 frequency channels
FCC and MKK regulations satisfied

## Slide 3
HARRIS
LUCENT
HARRIS
Codeword change only
Modified QMBOK
LUCENT
Codeword change
Do not position modulate
merge
MERGER EASE
HARRIS/
LUCENT

## Slide 4
COMPROMISE ADVANTAGES RELATIVE TO LUCENT’S MAY PROPOSAL
4 dB less PA Backoff.
RAKE receiver foundation maintained.
RAKE married to HARRIS’s Equalizer simplifies design over BCPM TSE/MS.
11 Mbps 1K byte packet performance.
  May: 130 nsec
  July: 226 nsec at lower complexity

## Slide 5
MAY
JULY
MULTIPATH ROBUSTNESS
RMS delay spread
Bigger is better
64 byte packet
NOISE ROBUSTNESS
Eb/No dB
Smaller is better
With Equalizer
1K byte packet
5.5 Mbps: 226 nsec 450 nsec
11 Mbps: 186 nsec 330 nsec
5.5 Mbps: 25.2 dB 17.7 dB
11 Mbps: 24.7 dB 17.7 dB
200%
Better
7-8 dB
Better
ARCHITECTURE
Design ease
Gate count
Power draw
1, 2 Mbps:
RAKE
FF/FB
Equal
5.5, 11 Mbps:
RAKE and
Equalizer
Integrated
MAY
JULY
MAY
JULY
Cleaner
Design
Chip
Equalizer
RAKE +
ISI Eq.
COMPROMISE ADVANTAGES RELATIVE TO HARRIS’S MAY PROPOSAL

## Slide 6
COMPROMISE OR NEW PROPOSAL?
CLEARLY A COMPROMISE BECAUSE
BPSK or QPSK chips are used (Harris)
1-and-2 MBps DSSS-like signal (Lucent & Harris)
  Phase-modulated codewords
11 Mcps rate maintained (Harris & Lucent)
  Spectrum (bandwidth) unchanged
Next Generation-QMBOK (Harris) codeword called CCK used
Seamless interoperability maintained with DS and FH
Merged architecture: RAKE (Lucent) with Equalizer (Harris)

## Slide 7
PERFORMANCE: WAVEFORM Versus RECEIVER
TRANSMIT
SIGNAL
DESIGN
RECEIVER
DESIGN
Distance properties
Wide choice range
Does it fully exploit Tx signal features?
PERFORMANCE ENABLERS

## Slide 8
SIGNAL DESIGN
MBOK
CoverCode
03 h
CCK
4-ARY
TESTPOINT
5.5 MBPS
8 CHIP CODEWORDS
50
225
320
DELAY
SPREAD
nsec
SIMULATION ASSUMPTIONS
6 Finger RAKE RCVR
8 Samples/chip CIR Decimated To 1
MBOK
CoverCode
12 h

## Slide 9
CODEWORD STUDY
Jointly performed comprehensive codeword study
Examined 8, 11 and 16 chip codes
Examined WALSH and cover codes
Examined real-chip (MBOK) versus complex-chip (CCK) codes
Computed matched-filter-bound to examine fundamental distance properties in multipath
Jointly-examined against receiver architectures
CCK gave best overall performance and architecture

## Slide 10
I/Q MULTIPATH CORRUPTION
HARRIS’S Quadrature-MBOK
LUCENT’S Quadrature-BCPM
CORRUPTED BY MULTIPATH PHASE ROTATIONS
I-Channel Codeword
Q-Channel Codeword
Quadrature Signalling
SUM
SOLUTION:
Serially-Encode QPSK chips

## Slide 11
CODE DIMENSIONALITY
8 BPSK CHIPS: 2^8 = 256 Codewords
8 QPSK CHIPS: 4^8 = 65536 Codewords

## Slide 12
c
e
e
e
e
e
e
e
e
j
j
j
j
j
j
j
j
=
-
-
+
+
+
+
+
+
+
+
+
+
+
+
{
,
,
,
,
,
,
,
}
(
)
(
)
(
)
(
)
(
)
(
)
(
)
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
j
1
2
3
4
1
3
4
1
2
4
1
4
1
2
3
1
3
1
2
1
COMPLEMENTARY CODES
8 Chip/4 Phase
Directly encodes complex (QPSK) chips
f1 quadriphase rotates whole codeword
64 codewords before quadriphase
256 codewords after quadriphase (8 bits)
2 bit sign, 6 bits codeword select
Fast-Walsh-transform like decoder
f: 0, p/2, p, 3p/2

## Slide 13
NAME CHANGE UNAVOIDABLE
QMBOK: Quadrature M-ary Bi-Orthogonal Keying
QMBOK does not make sense for new modulation
Not quadrature, not orthogonal (only nearly orthogonal), not bi-orthogonal
Still 8 chip
CCK -- Complementary Code Keying

## Slide 14
DIFFERENTIAL-PHASE MODULATE CODEWORDS
Codeword
Select Bits
Differential-
Phase Bits
CODEWORD
TABLE
Codeword
rotate
Codeword
PHASE
MAP
Quadri-phase
Previous-phase
Like 1 and 2 Mbps
Noncoherent Rcvr Enabled

## Slide 15
RAKE DESIGN RULES
RULE
VIOLATION
PENALTY
Symbol Duration
Must Be
Much Greater Than
Multipath Spread
HIGH-RATE
INDOOR WLAN
Autocorrelation
Must Be Impulsive
And Cross
Correlation
Zero
200 nsec gives
0.25 - 0.5 Symbol
Overlap
8-16 chips is
too small to be
effective
RAKE ISI
Breakdown
Freq. Selective
RAKE ICI
Breakdown

## Slide 16
RECOMMENDED RAKE RCVR EXTENSIONS
RAKE rcvr alone works great for 1 and 2 Mbps
At high data rates, multipath impairments limit the performance of a RAKE
HARRIS/LUCENT recommend extensions which enable high-performance at 11 Mbps

## Slide 17
INDOOR MULTIPATH EXAMPLE
0
0.2
0.4
0.6
0.8
1
1.2
1.4
0
0.1
0.2
0.3
0.4
0.5
CIR Magnitude
time*symbolRate
IMPULSE RESPONSE PROFILE
SYMBOL
DURATION
100 nsec
RMS Delay
Spread

## Slide 18
INDOOR MULTIPATH EXAMPLE
SYMBOL
DURATION
300 nsec
RMS Delay
Spread
0
1
2
3
4
5
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
CIR Magnitude
time*symbolRate
IMPULSE RESPONSE PROFILE
ENVIRONMENT:
COMMERCIAL/
FACTORY

## Slide 19
MULTIPATH: ISI LOSS
InterSymbol Interference (ISI)
Symbols Smeared Together
Previous Symbol: Post-Cursor ISI
Preceding Symbol: Pre-Cursor ISI
Primary RAKE Failure Mechanism for 802.11
Previous
Symbol
Current
Symbol
Following
Symbol
CHANNEL
IMPULSE
RESPONSE
Post-Cursor
Tail
Pre-Cursor
Ramp
slide into rcvr

## Slide 20
MULTIPATH: ICI LOSS
InterChip (sub-symbol) Interference (ICI)
Chips Smeared Together
Previous Chip: Post-Cursor ICI
Preceding Chip: Pre-Cusor ICI
Codeword Orthogonality Lost
Codeword Equal-Energy Lost
Secondary RAKE Failure Mechanism for 802.11
Symbol’s Chips Smeared

## Slide 21
ISI/ICI MITIGATION IN PRE-JULY PROPOSALS
LUCENT
HARRIS
ALANTRO
MICRILOR
Codeword Design
TSE/MS MLSE
Codeword Design
CHIP DFE
MLSE/DFE
Rate 1/2 CODE
MLSE/DFE
Codeword Design
HARRIS/LUCENT
Codeword Design
RAKE with ISI/ICI Equalizer
JULY’S
PROPOSAL

## Slide 22
CANONICAL ARCHITECTURES
CHIP
EQ.
RAKE
RCVR
RAKE
With
ISI EQ.
RAKE
With
ISI/ICI EQ.
low
high
MULTI-
PATH
ROBUST
low
high
NOISE
ROBUST
1 2 3 4

## Slide 23
CHIP EQUALIZER
QPSK
CHIP
DECISION
+
-
Past-ISI
Cancel
WEIGHT PAST
DECISIONS
WITH CIR
FF
TAPS
FAST WALSH
TRANSFORM
Decision
Rcvd
Signal
2 FF Taps (multiplies) and 10 FB Taps (adds)
Sliding DFE algorithm minimizes FF Taps
Lowest-complexity architecture
226 nsec multipath-spread testpoint at 11 Mbps
20.5 dB SNR testpoint at 11 Mbps (64 byte)

## Slide 24
RAKE RECEIVER
6 tap Channel Matched Filter
Second-lowest-complexity architecture
90 nsec multipath spread testpoint at 11 Mbps
15.5 dB SNR testpoint at 11 Mbps (64 byte)
MATCHED
FILTER
FIR
CODEWORD
CORRELATION
DETECTOR
Received
Signal
COMPLEX
SIGN
DETECT
Sign-Mapped
Info Bits
Codeword-Mapped
Info Bits

## Slide 25
RAKE WITH ISI EQUAL.
6 tap Channel Matched Filter
Third-lowest-complexity architecture
144 nsec multipath spread testpoint at 11 Mbps
15 dB SNR testpoint at 11 Mbps (64 byte)
MATCHED
FILTER
FIR
CODEWORD
CORRELATION/
SIGN
DETECTOR
Received
Signal
+
-
Past-ISI
Cancel
WEIGHT PAST
DECISIONS
WITH CIR
Symbol Decision
Rake Receiver

## Slide 26
RAKE WITH ISI/ICI EQUAL.
6 tap Channel Matched Filter
Highest-complexity architecture
333 nsec multipath spread testpoint at 11 Mbps
15.5 dB SNR testpoint at 11 Mbps (64 byte)
MATCHED
FILTER
FIR
CODEWORD
CORRELATOR
WITH EMBEDDED
ICI EQUALIZER
SELECT
LARGEST
Decision
RAKE RECEIVER
WEIGHT PAST
DECISIONS
WITH CIR
+
-
Past-ISI
Cancel
Received
Signal

## Slide 27
RAKE WITH ISI/ICI EQUAL. CORRELATOR DETAIL
z-1
z-1
z-1
h1
h2
h3
Codeword # 3
Chips
Correlator for
Codeword # 3
Detection
Statistic for
Codeword # 3
Received
Signal
-
+
+
SIMILAR STRUCTURE FOR
ALL OTHER CODEWORDS
MAKE HARD-DECISION
FOR CODEWORD WITH
BEST STATISTIC

## Slide 28
PER FOR MULTIPATH AND NOISE