## Slide 1
Rate Information and the 802.11 MAC
802.11 MAC is designed to operate with exact rate information
Rate information is used in several areas
  Supported Rates element
    Beacons
    Probe Request/Response
    Association/Reassociation
  RXVECTOR, TXVECTOR
    Duration calculation

## Slide 2
Rate Information and the 802.11 MAC
Supported Rates element is used for
  Announcing rates in a BSS (Beacon TX, Probe Response)
  Selecting a BSS (Scanning, Joining)
  Informing AP if Station capabilities (Association, Reassociation)
This information does not need to be exact
  All stations must have the same understanding of a value in the element
  The value in the element can be considered a label for a rate

## Slide 3
Rate Information and the 802.11 MAC
RXVECTOR contains the rate at which a frame is received
TXVECTOR contains rate at which a frame is to be transmitted
  This rate information is used to calculate the duration field in the MAC header
  Must be accurate to make this calculation accurately

## Slide 4
Effect of Inexact Rate Information
Inexact rate information in the calculation of duration
  wastes valuable (usable) bandwidth when the representation of the rate is less than the actual rate
    NAV does not expire until well after frame exchange completes
  causes otherwise avoidable collisions when the representation of the rate is greater than the actual rate
    NAV expires before frame exchange completes

## Slide 5
Effect of Inexact Rate Information
Amount of wasted bandwidth or time vulnerable to collisions is proportional to the percentage error in the representation of the actual rate
Large frames cause greatest waste
Large frames are most vulnerable to collision