## Slide 1
A Review of the Alantro 11Mbps Proposal
Chris Heegard
July 7, 1998
Slide 1
Heegard

## Slide 2
The Alantro Proposal
QPSK @ 11Msps
Basic Rate: 11Mbps (R = 1/2), 64 state BCC
  Coding Gain of ~ 7dB
Variable rate via puncturing (500kbps possible)
Excellent Multipath performance with reasonable complexity
July 7, 1998
Slide 2
Heegard

## Slide 3
How did Alantro get here?
Objective: create a standard that will realistically meet the goal of robust, cost effective, transmission in excess of 10Mbps
Studied existing proposals (summer ‘97)
Decided Harris was best starting point
  MBOK “code” weak
    Small coding gain
    Problems with joint M.P./Decoding
Studied BCC
  Larger gain
  Reasonable Complexity
  Good match to joint M.P./decoding
July 7, 1998
Slide 3
Heegard

## Slide 4
Trellises: A unifying concept for digital transmission
Multipath: h(z)=1+az-1
-0.5
0
0.5
1
1.5
-0.5
0
0.5
1
1.5
1+a
1-a
-1+a
-1-a
+
X
a
July 7, 1998
Slide 4
Heegard

## Slide 5
BCC Trellis
G = [1+D+D2, 1+D2]
The regular trellis structure is consistent with the multipath trellis
Scrambling helps with multipath robustness
0
1
2
3
4
5
6
0
0.5
1
1.5
2
2.5
3
+
+
Periodic
Scramble,
QPSK Mod
+
July 7, 1998
Slide 5
Heegard

## Slide 6
Trellis of a Block Code
(n=8, k=4, d=4) F2
The irregular trellis structure makes it difficult to jointly demodulate/decode
0
1
2
3
4
5
6
7
8
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
8
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
8
0
1
2
3
4
5
6
7
July 7, 1998
Slide 6
Heegard

## Slide 7
CCK code (n=8, k=4) Z4 [(n=16, k=8) F2]
G = [1 1 1 1 1 1 1 1] a = [0 0 0 2 0 0 2 0] [1 0 1 0 1 0 1 0] [1 1 0 0 1 1 0 0] [1 1 1 1 0 0 0 0]
c = mG+a (over Z4)
  A linear code (mG) with scrambling (a)
d = 4
Number of Nearest Neighbors = 24
July 7, 1998
Slide 7
Heegard

## Slide 8
Code Performance
Free Distance (AWGN tolerance)
  Coding Gain
  BER vs Eb/No
Complexity
  Additions/bit
  Comparisons/bit
Multipath Robustness
  Joint Demodulation/Decoding
  BER vs Eb/No with Delay Spread
July 7, 1998
Slide 8
Heegard

## Slide 9
Examples
(n=2, k=1, v=2) [4 state BCC]
  d = 5 (3.97 dB), adds = 12, cmps = 4
(n=8, k=4) E.H.C. - F2 [MBOK]
  d = 4 (3.01 dB), adds = 14, cmps = 3.75
(n=8, k=4) Z4 [CCK]
  [(n=16, k=8) F2]
  d = 4 (3.01 dB), adds = 32, cmps = 8
(n=2, k=1, v=6) [64 state BCC]
  d = 10 (6.99 dB), adds = 132, cmps = 64
July 7, 1998
Slide 9
Heegard

## Slide 10
Block versus Convolutional Coding
BCC’s are a well established technique that dominates successful standards
  v.34, v.90, HDTV, DirectTV, CDMA cell phones, 802.14, HDSL-2, …
  Block codes???
BCC’s have a consistent trellis structure that compliments the trellis of the multipath
July 7, 1998
Slide 10
Heegard

## Slide 11
802.11 Code selection
Consider which coding options will provide for the best trade-off between AWGN performance, complexity and multipath robustness
Comparison of coding techniques should be made on a quantitative technical basis
Programmable code??? (v.34, HDSL-2,…)
July 7, 1998
Slide 11
Heegard