## Slide 1
The Short Preamble for 802.11 2.4 GHz WLANs
Carl Andren Harris Semiconductor
Notes: A new modulation scheme has been adopted by the IEEE 802.11 standards committee to implement Wireless Local Area Networks (WLANs) that will provide 1 to 11 MBps rates in the 2.4 GHz ISM band. This scheme will provide interoperability with the 802.11 DS equipment operating at 1 and 2 MBps and also offer rates of 5.5 and 11 MBps for those users that need more speed. This paper discusses the new modulation scheme and the considerations that led to the adoption of this technique for the standard.

## Slide 2
Summary
A long preamble will allow both interoperability and co-existence with low rate LANs
A short preamble will allow better throughput when the LAN does not need to contend with low rate PHYs.
The preamble length has been designed to allow for AGC settling, antenna diversity selection, and equalizer training
Notes: Harris has built chips on the MBOK waveform and extensively tested them in the lab and field. Several commercial applications have been tested and are ready to be fielded. Based on this performance and the simulations that show the CCK waveform to be superior, we are embarking on the development of chips to embrace the CCK waveform as well. We are also working on the design of the fully equalized version for introduction early to mid next year.
We thank Lucent Technologies for the extensive help in the definition and simulation of the CCK waveform and their help in getting it adopted in the IEEE 802.11 high speed 2.4 GHz PHY standards group. We look forewords to rapid development of the standard so that the market can enjoy Ethernet line speeds in the indoor wireless LAN arena.

## Slide 3
shortPLCP Preamble
MPDU
72 bits @ 1 Mbit/s
shortSYNC
shortSFD
16 bits
SIGNAL
8 bits
8 bits
16 bits
LENGTH
CRC
56 bits
SERVICE
PPDU
PLCP Header
48 bits @ 5.5 Mbit/s
16 bits
variable @ 5.5 or 11 Mbit/s
SCRAMBLED
ZEROS
BACKWARDS
SFD
DBPSK BARKER
5.5 Mbps CCK
PACKET WITH SHORT PREAMBLE
80.7 us

## Slide 4
The Alantro Proposal
Alantro proposes to modulate the header portion of the short preamble with 2 MBps instead of 5.5 MBps CCK.
  This makes the Es/N0 more of a match to PBCC coding, helping their option
  What this does is extend the length of the overhead by 16 us to 96 us, hurting throughput.
  It does allow the equalizer training more time
Harris/Lucent feels this is unnecessary for our approach

## Slide 5
Throughput with short preambles

## Slide 6
Throughput hit
The curves show a small hit in throughput for the 96 us preamble with ACKs.
When RTS and CTS are added, there is an additional hit making the total 64us.

## Slide 7
No
Hit
Ant A
No
Hit
Ant B
Hit
Ant A
Hit
Ant B
Hit
Ant A
AGC
Ant B
AGC
Ant A
CIR & Freq
Estimate
Ant B
CIR & Freq
Estimate
Ant A
SFD
Switch Ant.
&
SFD Search
MPDU
TAIL
0 5 10 15 20 25 30 35 40 45 50 55 60
CCA
SLOT k
CCA
SLOT k+1
AGC LOCK
ON ANT B
AGC LOCK
ON ANT A
SYNC
mSEC:
56 mSec
ANTENNA
SELECT
ANTENNA DIVERSITY: SIGNAL PRESENT AT BOTH ANTENNAS
SHORT PREAMBLE TIME LINE
SWITCH DUE
TO TRANSPORT
LAG
CCA
SLOT k+2

## Slide 8
Timeline Considerations
As you can see from the slide, the time line is tight, so a shorter sync field is not acceptable
Antenna selection must occur enough before the SFD comes along to allow descrambler seeding
Not all of the SFD has be used if the SNR is high enough
AGC settling takes 10 us and the AGC is locked down during the packet to keep it from thwarting the equalizer

## Slide 9
No
Hit
Ant A
No
Hit
Ant B
Hit
Ant A
No
Hit
Ant B
Hit
Ant A
AGC
Ant A
CIR & Freq
Estimate
Ant A
SFD
SFD Search
MPDU
TAIL
0 5 10 15 20 25 30 35 40 45 50 55 60
AGC LOCK
ON ANT A
SYNC
mSEC:
56 mSec
ANTENNA DIVERSITY: SIGNAL FADED ON ANTENNA B
SHORT PREAMBLE TIME LINE
No
Hit
Ant B
SWITCH DUE
TO TRANSPORT
LAG
CCA
SLOT k
CCA
SLOT k+1
CCA
SLOT k+2

## Slide 10
Frame Duration Comparison

## Slide 11
Simple Throughput Comparison

## Slide 13
RTS CTS Effect on Throughput
802.11 has the advantage of utilizing the RTS/CTS mechanism to reduce collisions due to hidden nodes (virtual carrier sense)
The extra transaction on each packet reduces the overall throughput
Adding 16 us more to each preamble costs 4 times that much for the whole transaction

## Slide 15
Comparison with Loading
Simulates the effect of back-off’s on the throughput with short and long preamble
Effect of preamble length is less pronounced with increasing load

## Slide 17
CCA mechanism and Co-Channel signal detection time
Measure the correlated signal energy in the preamble over 5 us dwells beginning when the receiver is enabled and compare that to a threshold
The detection time is less than the slot time by enough to include diversity
FH detection is done on clock energy in similar dwells.

## Slide 18
Interoperability
The CCK receiver can recognize both long and short preambles. If the CCK receiver detects a short preamble it trains on the short. If the receiver detects the long preamble it trains on the long preamble. This allows the receiver to better process the channel impulse response.
Scenario: CCK starts with a short preamble. Legacy DSSS modems defer on that preamble. It is normally received by the CCK modems that have the option to receive a short preamble. The CCK modem can receive both CCK (short and long) and legacy DSSS transmissions. If reception is poor (or there is, for whatever reason, a coexistence problem with IEEE modems), the transmitter falls back to 5.5 Mbit/s or to the long preamble. The long preamble is also recognized by the legacy DSSS only modems, making use of the IEEE imbedded multi-rate capability.
Result: CCK modems send, if circumstances allow, the short preamble, making full use of the higher throughput capabilities. They are at all times interoperable with legacy DSSS modems, recognizing the long preamble, receiving (and sending) at the low rates. If there are coexistence problems the CCK modems falls back to the long preamble.

## Slide 19
Coexistence
Low rate and high rate PHYs will coexist within the same network.
Short preambles will be used only within networks of exclusively high rate capable PHYs
Short and long preambles may be intermingled on the same network as long as all PHYs are high rate capable and the MAC software is configured to allow mingling.
All (rate) PHYs will perform CCA on either long or short preambles
Performing CCA in the middle of a packet on CCK is problematic.
Notes: By designing in the long preambles with the high rate hardware, we have tacitly assumed that they will coexist with the low rate stations on the same network. Dynamic switching of rates is expected. Even if all stations are high rate capable, some may require low rates in order to maintain connection.
A network can be set up to maximize throughput at the expense of reliability by using only short preambles. This does not allow downshifting to 1 and 2 MBps. If downshifting was needed, the short preamble would not be useable to convey this information if the SNR could only support 1 MBps.
For example, the beacon transmissions may be performed with long preambles in order to make sure that all PHYs can get the message. The high rate stations can sense that the short or long preamble is incoming by the state of the unmodulated sync section and process it accordingly. This allows it to do a better job in setting up an equalizer on the long preamble. This allows all PHYs to use all four rates for maximum reliability.
Leakage from nearby low rate networks may occur. A low rate station receiving the short preamble will not see the SFD and will probably not even be tracking when it occurs. It will miss the SFD but will none the less perform CCA on the preamble since it exists for more than 20 us. Once the body of the packet is started, it will not see it unless it is processing ED. Thus, low rate PHYs using CS only for CCA may interfere with high rate PHYs. High rate PHYs will be able to sense the length field of the low rate transmissions and defer.

## Slide 20
Coexistence Philosophy
Coexistence means that short preamble CCK defers for legacy DSSS (and long CCK) and vice versa.
legacy DSSS Receiver
  detects short preamble (carrier or energy); CCA reports channel busy;
  waits for Start frame delimiter but will not find it.
  It is not prescribed in the standard what action the receiver has to take, there are several possibilities:
  once the CCK signal starts after the preamble, the receiver will lose code lock and cause CCA to go to the channel IDLE state. The receiver returns to the RX idle state and starts looking for a carrier, which it does not see (because of CCK). This might result in a collision or the receiver being out of slot sync.
  The receiver times out on the SFD. This also leads to out of sync and possible collision
  CCA reports channel busy until the ED drop of the CCK signal. In this case the DSSS receiver stays in slot sync.
  It is clear that the third implementation (ED) is the best guaranty for coexistence.

## Slide 21
Coexistence Philosophy
CCK receiver
  configured to process a short preamble, the receiver will also detect the long preamble and process the legacy DSSS frame. The CCK receiver can see the legacy transmitter CS in the middle of a message and defer if necessary.
  On the CCK portion of the packet, the CCK receiver also loses the CS if it is based on Barker correlation and will not behave properly in a network. Therefore, it too could perform better if it had an improved CCA measure like an ED that works or a time out feature.