## Slide 1
Clock Coupling in the HR Standard
By Jan Boer
Lucent Technologies
and
Mark Webster
Harris Semiconductor

## Slide 2
The Problem
Harris Semiconductor and Lucent Technologies independently analyzed timing recovery requirements and algorithms
Conclusion:
  if the LO oscillator and the sampling clock at transmit are not coupled the receiver will suffer severe performance degradation compared to a situation where the clocks are coupled

## Slide 3
Timing recovery #1
Analyze zero crossings at the incomming CCK signal.
  Zero crossings very noisy, especially in a real environment
  Timing tracking becomes unreliable at about 50 ns delayspread
relatively simple circuit, low performance

## Slide 4
Timing recovery #2
Early late detection after Channel Matched Filter..
  CMF has to run at twice the chiprate, extra circuitry to calculate the interchip values
  Signal after CMF/ Walshcorrelation still very noisy; effect of channel estimation on performance
  Timing tracking reliable up to 200-250 ns delayspread.

## Slide 5
Timing recovery with coupled clocks
Estimation of phase error (easy on QPSK/CCK)
Timing tracking can be easily calculated from the phase error and clock can be adjusted.
Simple circuitry; no performance limitations because of the sample timing

## Slide 6
Proposal
Normally (just because of the bill of materials) clocks are coupled. In some applications the clocks have to be uncoupled.
Notify the receiver through the service field that the clocks are coupled, such that receiver can make use of this for optimal performance.