## Slide 1
IEEE 802.11 Wireless Access Method and Physical Specification
Title: FH Interoperability Option of HR/DSSS PHY
Date: January 12, 1999
Author: Dean Kawaguchi
Symbol Technologies, Inc.
2145 Hamilton Ave
San Jose, CA. 95125
Telephone: (408)369-2629
FAX: (408)369-2737
email: deank@psd.symbol.com

## Slide 2
Summary of FH Interoperability Method
We propose an FH PHY backward interoperability mode as an option for the Harris HS proposal
  This proposal does not modify the basic modulation format, but it assumes the addition of the HS preamble; wraps around the Harris proposal
  Two fundamental changes required for FH interoperability are 1) hopping of the wideband DS signal synchronized to the FH hop sequences 2) using the FH preamble in front of the HS preamble and data

## Slide 3
Backward Interoperability to FH
There is a significant volume of 802.11 interoperable FH radios being sold today by a number of manufacturers
  HR/DS/FH will enable FH users to migrate to HR/DSSS
    Users can maintain investments in low cost FH appliances while also adding rate scaling capability using HR/DSSS
  Option brings together the previously distinct FH and DS camps
    Any station which can support the HR/DS/FH will also be required to support the basic HR/DSSS, HR/DSSS/short, and by inference legacy DSSS and FHSS
    Home centered initiatives coming out with new FH solutions
  HomeRF is based on the 802.11 FH; considering using whatever mechanisms we develop here to provide higher data rates
Coexistence to basic HR/DSSS and DSSS can be improved by additional CCA requirements on HR/DS/FH units
  Use wideband energy detect with timeout or
  Use full bandwidth correlation detection

## Slide 4
Robustness in Interference Limited Environments
Symbol’s experiences in the 900 MHz band since 1990 have shown
  Fixed frequency systems will fail in the presence of fixed freq interference
  Changing channels is slow and often does not work
  Our proprietary 900 MHz DS system has evolved into a hopping DS system to provide reliable connection in the presence of interference
  The 2.4 GHz band may eventually be worse than the 900 MHz band since it is the only unlicensed band available worldwide
  Also, non-802.11 systems in this band are already and will continue to be a significant portion of the usage of this band
Hopping of the wideband HS signal will provide protection against a variety of fixed frequency and hopping interference
  As a last line of defense, backing down to 1/2 Mbps FH with 79 1 MHz channels will provide the best chance of operating through interference.

## Slide 5
Limitations
There were some limitations that were pointed out in my original presentation in March 98
  Most efficient use of the band would be achieved by frequency planning in a cellular arrangement such as used by DS
    However, that requires exclusive use of the band which cannot be guaranteed in the unlicensed ISM band
    It trades off the efficiency of the cell planning approach for the reliability of frequency hopping and the flexibility of scaling down to a 1 MHz narrow FH signal
    Backward interoperability with the DS PHY necessitates turning off the hopping feature since hopping is not part of existing DS PHY
    In addition, we recognize that the FH/DS cross CCA issues must be resolved because this option uses both modes
  I made specific recommendations in the letter ballot 16 comments to add the cross mode CCA requirements to resolve this issue

## Slide 6
Goal: Work Toward Consensus
Dateline: March 1998…
  FH and DS interoperability was part of the comparison criteria
  Symbol and Harris presented proposal for FH interoperability option
  Lucent and Micrilor unilaterally accepted same method for in their proposal to provide FH interoperability
Dateline: Today (January 1999)
  The FH interoperability mechanisms have been refined and clarified over the past year but remain essentially the same
  We have 77% approval of the draft and rising
  6 out of 9 NO-FH votes are from Lucent saying that there are some problems with it so throw it out
Goals: Build on our hard earned progress rather than destroying it
  There are limitations to what this mode can do as we pointed out from the beginning, but it fills a need that goes unanswered without this option