## Slide 1: Wireless Personal Area Network Study Group
Tutorial
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 2: Agenda
Vision Statements
WPAN Study Group Objective
Methodology of Study
  Solicited and Reviewed Study Group Member Protocol Proposals & Applications, via Calls
  Reviewed IEEE 802.11 Standard
  Reviewed HomeRF Specification
  Reviewed Bluetooth Specification
Summary
WPAN Background

## Slide 3: IEEE 802 Wireless Vision Statement
802.11 Base Standard
  2.4GHz Frequency Hopping Spread Spectrum (1Mbit/s)
  2.4GHZ Direct Sequence Spread Spectrum (2Mbit/s)
  Infrared (1Mbit/s)
802.11a 5GHz Extension (>20Mbit/s)
802.11b 2.4GHz Extension (>8Mbit/s)
Broadband Wireless LANs (LMDS) - ECSG
Wireless Personal Area Networks - WGSG
Bluetooth?
HomeRF?
“IEEE 802 is the focal point for Wireless LAN standards.” Jim Carlo
Source: Jim Carlo, 802 Chair [JC-802-Consortium.PDF] can be downloaded from the following URL: ftp://ftp.flexipc.com/wearablesgroup/802/

## Slide 4: WPAN Vision Statement
Continuum of needs for wireless products
No one product which can fill all needs
Family of complementary devices
RFID
WPAN
WLANs
Low performance,
low cost
High performance,
higher cost
Source: doc.: IEEE 802.11-98/97 (Pat Kinney, Intermec)

## Slide 5: WPAN Study Group Objective
Review WPAN/WLAN Requirements
Determine Need for Standard
If warranted draft a PAR for submittal
Seek appropriate Sponsorship within 802
The IEEE 802 Local and Metropolitan Area Network Standards Committee
has the basic charter to create, maintain, and encourage the use of
IEEE/ANSI and equivalent IEC/ISO JTC 1 standards primarily within
layers 1 and 2 of the OSI (Open System Interconnection) Reference Model.

## Slide 6: WPAN PAR: Purpose
To provide a supplemental standard for low complexity, low power consumption wireless connectivity to support interoperability among devices within or entering the POS. This includes devices (see below) that are carried, worn, or located near the body. The proposed project will address Quality of Service to support a variety of traffic classes.
Examples of devices, which can be networked, include Computers,
Personal Digital Assistants (PDAs)/Handheld Personal Computers (HPCs),
printers, microphones, speakers, headsets, bar code readers, sensors,
displays, pagers, and cellular & Personal Communications Service (PCS) phones.

## Slide 7: WPAN PAR: Scope
To define derivative versions of the 802.11 PHY and MAC specifications for wireless connectivity with fixed, portable and moving devices within or entering a Personal Operating Space (POS). A goal of the WPAN Group will be to achieve a level of interoperability (see -99/5) sufficient to transfer data between a WPAN device and an 802.11 device.
A Personal Operating Space (POS) is the space about a person that typically extends up
to 10 meters in all directions and envelops the person whether stationary or in motion.

## Slide 8: WPAN PAR: Scope (Continued)
The 802.11 PHY and MAC have been reviewed to determine their suitability to meet the Functional Requirements of the WPAN Applications as specified in IEEE documents -98/295-298 and -98/352. Detailed suggestions on proposed changes to the IEEE 802.11 MAC & PHY Standard have been reported in documents -98/322r2, 323, 324.

## Slide 9: WPAN Original Functional Requirements published 1/98
January 22, 1998
Power Management: Low current consumption
Range: 0-10 meters
Speed: 19.2 - 100Kbps (actual)
Small Size e.g., ~.5 cubic inches no antenna
Low Cost: i.e., relative to target device
Should allow overlap of multiple networks in the same area
Networking support for a minimum of sixteen devices
March 4, 1998
May 20, 1998
1997
Source: doc.: IEEE 802.11-98/58 (Bob Heile, GTE)

## Slide 10: Current WPAN Guidelines- “A” List
WPANs will seek worldwide spectrum allocations for unlicensed bands e.g., 2.4GHz
Low Cost: i.e., relative to target device
Small Size e.g., ~.5 cubic inches( excludes antenna & battery)
Power Management: Very Low current consumption (Average 20mW @ 10/90 or less)
Data
Should allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Should allow coexistence of multiple Wireless Systems i.e. P802.11 in the same area
WPAN Network Access Control
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 11: Current WPAN Guidelines- “B” List
Delivered Data Throughput at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
All devices within a WPAN must be able to communicate with each other
Networking support for a minimum of 16 devices
Voice
Range: 0-10 meters
Attach: within one (1) second, once within range
Bridge or Gateway connectivity to other data networks
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 12: Current WPAN Guidelines- “C” List
No single element of failure
Video
Roaming: hand-off to another PAN
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 13: Additional Guidelines
WPAN Density: 1 WPAN in 2 square meters, average density at acceptable [TBD] performance levels
Power Consumption: Each WPAN Device will consume <20 mW long term average [TBD] given a 10% TxRx load in the WPAN
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 14: WPAN Application Feature List
Consensus
Strong
Weak
Priority
High
Low
low cost
low power
small size
packet data < 1 Mbps
range < 10m
active devices < 10
manual auth/auto attach
coexistence with 802.11
packet + isochronous
encryption
mobility < 10 mph
gateway
native IP
inter-pan connectivity
topology
active devices 10 - 128
coexisting PANs 4-30
Source: doc.: IEEE 802.11-98/353 (Bruce Kraemer, Harris)

## Slide 15: We focused only on the Lower Layers
Medium Access Control Sub Layer
Physical Layer
Physical
Data Link
Network
Transport
Session
Presentation
Application
ISO/OSI Reference Model
Area
of
Focus
}

## Slide 16: We reviewed the IEEE 802.11 Standard for a WPAN fit
WPAN
2.4 GHz radio
Freq. Hopping
Spread Spectrum
2.4 GHz radio
Direct Sequence
Spread Spectrum
Infra-Red
1 Mbit/s
2 Mbit/s
2 Mbit/s
1 Mbit/s
1 Mbit/s
2 Mbit/s
Legend: italic (and red) = optional
Higher data rate extension in 2.4 GHz
802.11b
Higher data rate extension in 5 GHz
802.11a
11 & 5.5 Mbit/s
6-12-18...54 Mbit/s
MAC
Lower data rate extension in 2.4 GHz
802.11x
<1Mbit/s
MAC Lite

## Slide 17: WPAN Interoperability Classes
Class 4 - Full Compliance to the 802.11 MAC & PHY PICS
Class 3 - Partial Interoperability: there is a way on the medium to exchange data without an intermediate device
  Class 3a Transmit and Receive
  Class 3b Receive Only
  Class 3c Detect Energy
Class 2 - Bridge-like (1 MAC/2 PHYs)
Class 1 - Gateway-like (> 1 MAC)
Class 0 - Non Interoperable

## Slide 18: Medium Interoperability Continuum
Background White noise
Full compliance
Destructive Interference
Significant Degradation
coexistence
Acceptable to 802.11 ?
WPAN proposal ?
interference
interoperable
communication
Spectrum
sharing
etiquette
Data transfer capability
Class 4
Class 3a
Class 3b
Class 3c
WPAN GOAL

## Slide 19: WPAN Liaison & Submissions
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
3. November 13, 1998 or sooner
IEEE 802.11
1997
Bluetooth
5/20/98
GTE
5/22/98
Intermec
5/22/98
M/A-COM
5/22/98
1. May 22, 1998 or sooner
HomeRF
3/4/98
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
4. January 15, 1999 or sooner
Kodak
IEEE 802.11
HomeRF Lite
Bluetooth
GTE
Intermec
Motorola
2. July 10, 1998 or sooner
M/A-COM
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
5. March 8, 1999 or sooner
Kodak
Wireless Personal Area Networking
Call For Proposals
Liaison
Convergence Achieved
Convergence Happening
Possible Convergence

## Slide 20: Company Participation as of March 1999
Bluetooth
~504 Bluetooth Adopters,
SIG Members
~50 Attendees
~82 HomeRF Adopters,
Participants/Core Members

## Slide 21: WPAN Timeline vis a vis a Specification(s) or a Standard
1998
1999
J
J
A
S
O
N
D
J
F
M
A
M
J
J
A
S
O
N
M
D
11/00
Bluetooth
v1.0
HRF-Lite
v1.0
SWAP-CA
v1.0 Provisional
3/12/98
WPAN SG
Formed
2/4/99
2nd PAR to ExCom
& WG LB17
6/4/98
1st PAR to
ExCom
CFP
CFA

## Slide 22: Standards should be written between the two elephants
Activity
Research
Investment
Standards
Time
Source: “Apocalypse of the two Elephants”, David Clark, MIT
Today
Today
Today

## Slide 23: Archive, Mailing List, URLs
WPAN Archives
  ftp://ftp.flexipc.com/wearablesgroup/Index.htm
  ftp://ftp.flexipc.com/wearablesgroup/
WPAN Mailing List
  stds-802-wpan@majordomo.ieee.org
IEEE 802.11
  http://grouper.ieee.org/groups/802/11/
Bluetooth Special Interest Group
  http://www.bluetooth.com/
Home RF Working Group
  http://www.homerf.org/
To add your name to IEEE mailing list please send an e-mail
to Ian Gifford giffordi@amp.com

## Slide 24: WPAN
Background

## Slide 25: WPAN Background - PR
During the March 1998 802 LMSC Plenary, a Study Group was formed to investigate the MAC & PHY Layers for Wireless Personal Area Networks (WPANs). This study will examine the requirements for WPAN for PCs, HPCs, peripherals, and consumer electronic devices to communicate and interoperate with one another in the home, office, etc. The WPAN Study Group has defined a WPAN with 0 to 10 metre range, data rates of less than 1 Mbit/s, low power consumption, small size less than 0.5 cubic inches and low cost relative to target device. One of the first applications anticipated is for wireless communications for Wearable computing devices.

## Slide 26: WPAN Background - Meetings
June, 1997. Cleveland, OH, Request to PASC
July 16, 1997. Nashua, NH IEEE PASC Plenary Meeting
December 2, 1997. Cleveland, OH Ad Hoc Wearables Committee Meeting
January 14-15, 1998. Memphis, TN, Ad Hoc Wearables Committee Meeting
January 19-23, 1998 Lynnwood, WA IEEE 802.11 Interim Meeting
March 9-13, 1998 Irvine, CA IEEE 802 Plenary Meeting (SG formed)
April 8-9, 1998 Cambridge, MA IEEE 802.11 WPAN SG Meeting
May 4-8, 1998 Utrecht, NL IEEE 802.11 Interim Meeting
May 19-21, 1998 Irving, TX IEEE 802.11 WPAN SG Meeting
July 6-10, 1998 LaJolla, CA 802 Plenary Meeting
September 14-18,1998 Westford, MA 802.11 Interim Meeting
October 26, 1998 Atlanta, GA Ad Hoc WPAN SG Meeting
November 9-13, 1998 Albuquerque, NM 802 Plenary Meeting
January 11-15, 1999 Orlando, FL 802.11 Interim Meeting
March 8-12, 1999 Austin, TX 802 Plenary Meeting

## Slide 27: WPAN Background - Liaisons
Our Sponsor submitted an IEEE Liaison Letter to the following Groups:
ATM Forum Wireless ATM (WATM) Working Group
Bluetooth Special Interest Group
ETSI Broadband Radio Access Networks (BRAN) Project
Infrared Data Association (IrDA)
Internet Engineering Task Force (IETF), MobileIP
Home Radio Frequency Working Group (HRFWG)
Wireless LAN Alliance (WLANA)

## Slide 28: We reviewed the HomeRF Specification, via Liaison & Public info
HomeRF Working Group Formed March 4, 1998
  Liaison #1 May 5, 1998 -98/217
  Liaison #2 July 7, 1998 -98/251r1
  Liaison #3 September 15, 1998 -98/299
  Liaison #4 November 26, 1998 -98/360
  Liaison #5 January 12, 1999 -99/004r1 (Minutes only)
  Liaison #6 March 9, 1999 -99/054 Tutorial

## Slide 29: We reviewed the Bluetooth Specification, via Liaison & Public info
Bluetooth Special Interest Group Formed May 20, 1998
  Liaison #1 July 7, 1998 -98/253
  Liaison #2 September 15, 1998 -98/300
  Liaison #3 October 26, 1998 -98/350 (Minutes only)
  Liaison #4 December 14, 1998 J. Carlo 802 Overview to Bluetooth SIG
  Liaison #5 March 9, 1999 -99/053 Tutorial

## Slide 30: We reviewed the Liaison Usage Models for applicability
Bluetooth
Three-In-One Phone
Interactive Conference
Briefcase Trick
Forbidden Message
Automatic Synchronizer
Instant Postcard
Portable PC Speaker Phone
Cordless Desktop
Videos
Ultimate Headset
Internet Bridge
HomeRF
Set up a wireless home network to share voice and data between PC's, peripherals, PC-enhanced cordless phones, and new devices such as portable, remote display pads
Access the Internet from anywhere in and around the home from portable display devices
Share an ISP connection between PC's and other new devices
Share files/modems/printers in multi-PC homes
Intelligently forward incoming telephone calls to multiple cordless handsets, FAX machines and voice mailboxes
Review incoming voice, FAX and e-mail messages from a small PC-enhanced cordless telephone handset
Activate other home electronic systems by simply speaking a command into a PC-enhanced cordless handset
Multi-player games and/or toys based on PC or Internet resources

## Slide 31: WPAN Application Summary
Submitter
Attributes
Source: doc.: IEEE 802.11-98/353 (Bruce Kraemer, Harris)

## Slide 32: WPAN Background - Companies
3Com
Aironet
Amerisys
AMD
AMP
ARIB
Boeing
Bosch
BreezeCOM
Broadband Access Systems, Inc.
Butterfly Communications, Inc.
Carnegie Mellon
Clarion
Commcepts
Compaq/DEC
Conexant
FedEx
GTE/BBN
Harris
H-P
Informed Technology, Inc.
Intermec/Norand
Kodak
Kyocera
Lace
Lucent
McDonnel Douglas
Micrilor
MIT Media Lab
Motorola
Netwave
PED Inc.
Philips
Raytheon
Sanders
Sprint PCS
Symbol
Texas Instruments
Unisys
ViA
Walt Disney
Xetron
etc.