## Slide 1
A comment on line spectra at pilot sub-carriers
Masahiro Morikura and Masato Mizoguchi
NTT

## Slide 3
Extract

## Slide 4
This cause line spectra at the pilot sub-carriers.
Constant phase pilot signal in current Draft
Pilot signal allocation and signal power spectrum

## Slide 5
Power spectrum of modulated signal with constant phase pilot tone
Resolution band width 40 kHz
Power spectrum of modulated signal
The constant phase pilot tones generate line spectra at the pilot sub-carriers.

## Slide 6
Scrambled pilot signal
To avoid generating line spectra, the pilot signal is desired to be modulated by scrambled pattern.
This causes no performance degradation in demodulation.
Extra hardware is negligible (simple random pattern generator)
The pattern generation method in tk’s comment is a good solution.
Pilot signal modulated by scrambled pattern