## Slide 1: HIPERLAN-2 PHY Status
Jamshid Khun-Jush
Ericsson Eurolab - Nürnberg
Coordinator of HIPERLAN-2 Standard Area &
Chair of Physical Layer Technical Specification Group

## Slide 2: Outline
Preamble issue
Other decisions
Notes: Page <number>
        <footer>
<header>
<date/time>
1

## Slide 3: Preamble - I
A simplified HIPERLAN-2 MAC-Frame structure

## Slide 4: Preamble - II
Three different preambles for HIPERLAN-2 due to the centralised DLC protocol applied to HIPERLAN-2
    One for the beginning of MAC-Frame (for BCCH)
      short symbols for AGC setting, (coarse) frequency acquisition as well as timing acquisition and long symbols for channel estimation (and fine frequency acquisition).
      Currently no need for the IEEE PLCP Header, because the signalling of LENGTH, PHY mode and SERVICE are performed in the other part of protocol (in FCCH)
    One for each downlink burst and one for each uplink burst including long symbols C64 (T1/T2 in IEEE 802.11a). Not agreed yet:
      symbols for coarse frequency and timing acquisition for downlink bursts needed? (most likely NOT)
      symbols for coarse frequency and timing acquisition and/or AGC symbol(s) in uplink bursts.

## Slide 5: Preamble - III
HIPERLAN-2 preamble structure for BroadCast Channel (BCCH)
Currently two proposals exists
The issue will be resolved in BRAN#13 meeting on April 13-16, in Stockholm

## Slide 6: BCCH Preamble
A preamble introduced at the IEEE/BRAN joint meeting in Orlando by Ericsson/Nokia
AGC settling, frequency offset estimation, and time synchronization
AGC and coarse time synchronization
A16
A32
A16
A32
B32
B32
B32
B32
Channel estimation
C32
C64
C64
A preamble proposed by SONY based on 1/4 symbols for A part

## Slide 7: SONY proposal - I
6 repetitive symbols of length 16
Last pattern is phase-shifted by 180° (sign-bit flipped)
Advantages (SONY claims!!)
  Auto-correlation receiver implementation:
    Higher synchronization accuracy
    Maintains excellent False Alarm/Detection Failure rates
  Cross-correlation receiver implementation:
    Clear identification of last repetition (CC-peak phase shift) for length 16 cross correlation
    Clear CC peak in case of length 32 cross-correlation
  High commonality to IEEE802.11 preamble
Notes: To improve the preamble detection probability and time acquisition accuracy we propose to use the structure of the A-field as depicted in this slide.
The length of the A-field is not changed by the alternative structure (still 96 samples in total).
The A-field consists of 6 repetitive short OFDM symbols.
The complex samples of the last short symbol are phase-shifted by 180°.
Several advantages are achieved with this structure:
The granularity of the short symbols is higher, which leads to a larger AC window.
A shorter AC delay allows the detection of larger frequency offsets.
For CC the structure allows correlation over 16- or 32 samples
The proposal is almost identical to current IEEE proposal which is advantageous for harmonisation.
Overall this provides more flexibility and better performance

## Slide 8: SONY proposal - II
New sequence proposal for A16, sub-carrier mapping, generation same as in IEEE (see [BRAN12.5, HL12.5SON2.a])
  Minimize Peak-to-Average-Power-Ratio and dynamic range to improve AGC lock-in speed and reduce nonlinear distortion
    IEEE: PAPR=3dB, Dynamic Range=30.8dB
    A16 proposal: PAPR=2.2dB, Dynamic Range=7.0dB
Contact: Ralf Boehnke (boehnke@sony.de)
Notes: To show the improved acquisition reliability we want to consider the synchronisation using auto-correlation (AC).
The received signal is delayed by the correlation delay Dac.
The conjugate complex samples of the delayed version are multiplied with the received samples. The products are feed into the moving average of window size Wac and are then post-processed for a threshold detection and/or maximum search to find the correct timing.
The complex correlation result at the peak position can be used to estimate the frequency offset.
The maximum detectable frequency offset is different for both structures, the current WA has a detection range of 208kHz, the new proposal can detect up to 635kHz.
Considering frequency allocation of H/2 systems (e.g. 5.15G-5.35G) max. frequency offset is 214kHz (5.35G)
Current A-field structure can not be used for Frequency offset detection and coarse frequency synchronisation.
The new proposal achieves reliable FO detection.

## Slide 9: Other Decisions
C64 symbol
    The content of T1/T2 symbol in 802.11a is used.
Data interleaving
    The same block size and permutation rule as 802.11a
PHY data scrambling
    A MAC-frame synchronous scrambler with the generator polynomial used in 802.11a. Only 16 initial states are needed which are defined by the first four bits of BCCH.
Convolutional code and puncturing patterns
    A rate-1/2 “mother code” with generator polynomials g0=133 and g1=171 in octal representation as used in 802.11a
    for code rate 3/4 the same pattern as 802.11a (2/3 is currently not used in HIPERLAN-2)